## Slide 1: Rapid Product Development Meeting 6
Richard W. Roberts
UCSD Extension

## Slide 2: Agenda
Failure Mode and Effects Analysis
Computer Tools

## Slide 3: Tonight’s Humor

## Slide 4: Failure Mode and Effects Analysis
A tool by any other name
  Failure Tree (similar)
  Potential Failure Mode and Effects Analysis
  FMEA

## Slide 5: Failure Mode and Effects Analysis
An FMEA is a systematic method of identifying and preventing product and process problems before they occur.

## Slide 6: FMEA
History
  Started in aerospace to identify safety problems-mid 1960’s
  Become one of the basics for safety improvement programs especially in the chemical process industry
  Goal to prevent safety accidents and incidents from occurring
  Automotive industry adapted as a quality improvement tool

## Slide 7: FMEA
Why
  Used in both design and manufacturing process to reduce cost by identifying potential product failures early in the development process
  results in a more robust process that reduces the need for after the fact corrective action

## Slide 8: FMEA
FMEA is typically implemented as part of a comprehensive quality program in order to derive maximum benefits from the process.
Integral in Malcolm Baldrige, ISO9000 and the automotive QS-9000 programs

## Slide 9: FMEA
Results
  effective use has had a positive impact on many organizations bottom line.
  Reduces product defects
  Helps mistake-proof processes
  improves customer satisfaction

## Slide 10: FMEA
Types of FMEA’s
  Product (Design)
    detect flaws in design that will result in customer dissatisfaction
    can be conducted in all phases of design process, concept, prototype, and final, or as a last resort on existing products
  Process
    people, materials, equipment, methods, and environment

## Slide 11: FMEA
Overview of the FMEA Process
  Team Based
  Objective is to look at all of the ways that a process or product can fail.
  List Features
  List Potential Failure Modes

## Slide 12: FMEA
Overview of the FMEA Process
  Evaluate the risk of failure
    Severity - The consequence of failure
    Occurrence - The probability of failure
    Detection - The probability of the failure being detected before the effect is realized
  Assess a Risk Priority Number
  Rank the needs for corrective action

## Slide 13: FMEA
FMEA team
  Multidisciplinary
  Small
  members both familiar and unfamiliar with process/product
  Leader
  Process Expert (good and bad)
  Training
  Team Boundaries
  Scope - Objective

## Slide 14: FMEA
FMEA team
  Multidisciplinary
  Small
  members both familiar and unfamiliar with process/product
  Leader
  Process Expert (good and bad)
  Training
  Team Boundaries
  Scope - Objective

## Slide 15: FMEA Process
The FMEA Process
  The Start up Worksheet offers a good place to make sure members are aware of the FMEA process parameters and team boundaries.

## Slide 16: FMEA Process

## Slide 17: FMEA Process
The FMEA Process
  1 - Review the product/process
  2 - Brainstorm potential failure modes
  3 - list potential effects of failures
  4 - assign a severity rating to each
  5 - assign an occurrence rating to each

## Slide 18: FMEA Process
The FMEA Process
  6 - assign a detection rating to each
  7 - calculate the risk priority number
  8 - Prioritize the failure modes for action
  9 - Take action to eliminate or reduce high risk failure modes
  10 - recalculate the resulting RPN

## Slide 19: FMEA Process
The FMEA Worksheet
  Use a standardized worksheet to document the FMEA process.
  This document can help guide the team through the process and provide a lasting indication of the result of the FMEA process.

## Slide 20: FMEA Process Worksheet

## Slide 21: FMEA Process
Step 1 - Review the Process / Product
  Ensure that all team members are aware of the product.
    Use Blueprints, models, flowcharts as appropriate to familiarize the team.
    If nothing available, create one.

## Slide 22: FMEA Toaster Matrix

## Slide 23: FMEA Process
Step 2 - Brainstorm Potential Failure Modes
  Potential failures that effect manufacturing or product quality
  Organize or group your ideas as it makes sense (by type, area, user..)
  Some modes can be combined as they may be results of another or related.

## Slide 24: FMEA Process Worksheet
Toaster
RPD - 6
Rick Roberts
Later
Class 6
#1

## Slide 25: FMEA Process
Step 3 - List Potential Effect of Each Failure Mode
  may be several effects
  be very thorough
  If the fail occurs, what will be the consequences

## Slide 26: FMEA Process
Step 4 - Assign Severity Ratings

## Slide 27: FMEA Process
Step 5 - Assign Occurrence Ratings

## Slide 28: FMEA Process
Step 6 - Assign Detection Ratings

## Slide 29: FMEA Process
Step 7 Calculate the Risk Priority Number for Each Failure Mode
  Risk Priority Number = Severity X Occurrence X Detection

## Slide 30: FMEA Process
Step 8 Prioritize the Failure Modes for Action
  A Pareto Diagram is useful
  Decide which items need to be worked on.
  Set a RPN cut-off point to help pick the first level of items to work on.

## Slide 31: FMEA Process
Step 9 - Take action to eliminate or reduce unacceptable risk
  Ideally, eliminate it completely
  Work on reducing the level of all three scales.
  Increasing Delectability may improve the risk level, but generally does not improve the quality.

## Slide 32: FMEA Process
Step 9 - How can you reduce
  Severity?
  Occurrence?
  Detection?

## Slide 33: FMEA Process
Step 10 - Calculate the resulting RPN from the planned actions. After completing the actions reevaluate the product to ensure the process worked.

## Slide 34: Computer Tools
The tools available for the computer make the process of Rapid Product Development easier to achieve.
This is due mainly to the speed at which things can now be accomplished.

## Slide 35: Computer Tools
PC Based Design Packages bring mainstream design capabilities to the small and large business environment
CAD, CAE, Simulation, etc. are all tools which are now available for every engineer.

## Slide 36: Computer Tools
PC Based Based Business applications make analysis and presentations easier, quicker and more informative.
The use of spreadsheet software is unlimited in its application.

## Slide 37: Homework
Start working on team projects.

## Slide 38: Next Week
Meeting 7
  Design of Experiments
  DFX
  Costing Models