## Slide 1: Rapid Product Development Meeting 7
Richard W. Roberts
UCSD Extension

## Slide 2: Agenda
Meeting 7
  Design of Experiments
  DFX
  Costing Models
  Time for working on Project

## Slide 3: Humor

## Slide 4: Humor 2

## Slide 5: Design of Experiments
The experiment we are concerned with is the process. A properly designed process can reduce variability, improve yields, reduce development time and reduce cost.
The technique called Design of Experiments can be used to quickly test multiple parameters and focus on the most important.

## Slide 6: Design of Experiments

## Slide 7: Design of Experiments
Process is created by:
  Inputs
  Controllable Variables
  Uncontrollable Variables
  Outputs

## Slide 8: Design of Experiments
Example - Soldering
  Inputs
    PCB’s & Components
  Output
    Soldered PCB (with components attached
  Controllable Variables
    solder temperature, solder flux type, solder depth, and conveyor speed

## Slide 9: Design of Experiments
Example - Soldering - cont’d
  Uncontrollable variables
    thickness of board, layout of board, operable skill, and type of components used.
An experimental design can be used to determine the process settings and make the process insensitive to the uncontrollable variables

## Slide 10: Design of Experiments
A designed experiment is a test, or a series of tests, in which purposeful changes are made to the inputs of a process or system so that one may observe and identify the reasons for changes in the outputs.

## Slide 11: Design of Experiments
Designed Experiments Categories
  comparative and evaluative
  screening
  optimization
  regression

## Slide 12: Design of Experiments
Objectives of a planned experiment
  determining which variables are most influential on output
  determine variable settings to:
    outputs are almost always near the desired value
    variability is minimal or small
    effects from uncontrollable variables are minimized

## Slide 13: Design of Experiments
Facts about designed experiments
  Not all experiments are equally good
  Well designed experiments enhance quality and ultimately save money
  A well planned experiments results in more information about more factors in fewer runs than either unplanned or one factor at a time experiments
  To know about a process one must actively interfere with it.
  The cost of experimentation increases the more “developed” the process is.

## Slide 14: Design of Experiments
What is an undesigned experiment?
  An experiment where all factors are tested in all environments
  the number of experiments grows exponentially with the number of factors.
DOE is a method of making the number of these experiments manageable.

## Slide 15: Design of Experiments
Guidelines
  Generate a clear statement of the problem and well defined objectives
  Select the appropriate response variables
  Choose the factors and their levels
  Choose the appropriate experimental design, sample size, order of runs and blocking. Determine the desired degree of precision.
  Perform the experiment - KISS
  Analyze the data and graph
  Draw conclusions and make recommendations

## Slide 16: Design of Experiments
Why is DOE so important to us?
  It allows a reduction in the total number of test required to be run to derive a statistically significant result.
  Typical testing (or factorial testing) for a 2 factor, 2 level test would require at least 4 (22) tests. Three factors 2 levels would require 8 (23). Four factors 2 levels would require 16 (24)
  Known as 2k factorial analysis.

## Slide 17: Design of Experiments

## Slide 18: Design of Experiments
Why is DOE so important to us? - cont’d
  Using what is called a 2k Fractional Factorial Analysis, the number of tests required can be significantly reduced.
  This method introduces a problem called confounding. That is that one is unable to differentiate between either a main effect and it’s interaction or an interaction and other interactions.
  Typically used when these problems are understand from previous knowledge or from a screening test.

## Slide 19: Design of Experiments

## Slide 20: Design of Experiments
There are four examples of Design of Experiments work in Chapter 11 of the book. Read the chapter and review the examples.
The use of statistics is very important in the analysis of the result and determining which factors are the most important.

## Slide 21: Design for X
Design for X is a general topic concerning taking several X’s into consideration in the design.
These X’s can be
  Manufacturibility
  Predictability
  Maintainability
  reliability
  Serviceability
  the “ibilities”

## Slide 22: Design for X
The concept being that all important factors concerning a design be considered.
“The best design is the simplest one that works”
        Albert Einstein
It started as Design for Manufacturability and has evolved and is evolving to include all other aspects of the lifecycle.

## Slide 23: Design for X

## Slide 24: Design for X
The Economic Importance of Manufacturing
  World Wealth comes from three sources
    What is removed from the ground
    What is grown from the ground
    What is manufactured
So, ensuring that a design is economical to make is important!

## Slide 25: Design for X
The attributes of a good design:
  Performance
  Features
  Reliability
  Conformance
  Durability
  Serviceability
  Aesthetics
  Perceived Quality

## Slide 26: Design for X
To those desirable attributes we would now add:
  Manufacturibility
  Safety
  Environmental Friendliness
  User Friendliness
  Short Time to Market
  Upgradability

## Slide 27: Design for X
Historically, Designers have concentrated on the first list with little or no consideration of the second list.
  Concentrated on:
    function
    features
    appearance
  Neglected the downstream considerations

## Slide 28: Design for X
Using a Taguchi approach the following attributes become important:
  Minimum manufacturing costs
  Minimum quality costs
  Minimum operating costs
  Minimum costs from safety defects
  Long Life, (minimum depreciaton)
  Minimum environmental cost

## Slide 29: Design for X
Combining all of the lists produces a list of factors to be optimized for the ideal product
  Function and Performance
  Safety
  Long-term quality
  Manufacturibility
  Environmental friendliness
  Serviceability
  User friendliness
  Appearance
  Features
  Short time to market

## Slide 30: Design for X
DFX
  design for all desirable characteristics
  design for excellence
Only the very beginning of the concept of DFX
  However - DFX is only another piece in the Rapid Product Design process.

## Slide 31: Design for X
Reference Books
  Design for Excellence
    James G. Bralla
    ISBN 0-07-007138-1
  Chapter 10 in Integrated Product and Process Design and Development (textbook)
    Edward B. Magrab
    ISBN 0-8493-8483-4

## Slide 32: Product Cost Analysis
Why is product cost important?
  Great Decision maker
What makes up the product cost?
Types of Costs
Types of Costing Models
The Cost of Time

## Slide 33: Product Cost Analysis
Why is product cost important?
  Building a product that costs too much is not profitable.
  Building a cheap product that doesn’t meet the customer’s needs is not profitable.
  Profit is the goal of a manufacturing company.
  Cost is most often the basis of corporate decisions

## Slide 34: Product Cost Analysis
What are the factors that determine cost?
  Cp = Np(M + L + R) + T0 + S + D
    Cp - Products total cost
    Np - lifetime product volume
    M - material cost per unit
    L - Direct Labor per unit
    R - Production Resource per unit
    T0 - tooling and capitalization costs
    S - System Costs
    D - Development Costs

## Slide 35: Product Cost Analysis

## Slide 36: Product Cost Analysis
Types of Cost
  Product Costs
    Material, direct labor, resources, etc.
  Overhead/System Costs
    Activity bases accounting
    indirect labor
    management
  Development Costs

## Slide 37: Product Cost Analysis
Cost Models
  Return Map
  Design to Cost
  Spreadsheet Models

## Slide 38: Product Cost Analysis

## Slide 39: Product Cost Analysis

## Slide 40: Product Cost Analysis

## Slide 41: Product Cost Analysis

## Slide 42: Product Cost Analysis

## Slide 43: Product Cost Analysis

## Slide 44: Product Cost Analysis
Spreadsheet Models allow what-ifs and can help derive tradeoff rules:

## Slide 45: Product Cost Analysis
Cost of Time
  using a spreadsheet model a tangible cost of time in developed
  Why do you think time to market is so important?

## Slide 46: Meeting 8
  Integration of the design process
  Database Sharing
  Team Project Time

## Slide 47: Exercises / Homework
Read Chapters 3, 10, 11
Work on Team Projects