## Slide 1: Guaranteed ATM: Design, Verification, and Performance Optimization
Highest Honors Thesis
Purvesh B. Thakker
July 23rd, 1998

## Slide 2: Introduction
ATM networking technology
Bridges LAN/WAN
Delivers many types of data
Synergistic opportunities
No delivery guarantee

## Slide 3: Presentation Overview
Project Goals
Design
Verification
Optimization
Performance Benchmarks
Summary and Future Research

## Slide 4: Project Goals
Guaranteed Delivery
Maximized Performance
Future Integration with SCALE

## Slide 5: The Outside World
Application
Guaranteed ATM
Network Adapter
Computer A
Computer B
Application
Guaranteed ATM
Network Adapter
ATM switch
Fore API
Fore API

## Slide 6: Design
Flow control
  Stop-and-wait
  Windowed
Error control
  Checksum
  Negative Acknowledgements
  Forward Error Correction

## Slide 7: Automatic Repeat Request (ARQ)
Combined implementation of error and flow control
Four ingredients
  Positive Acknowledgement
  Retransmission after Timeout
  Error Detection
  Negative Acknowledgement and Retransmission
Go-back-N ARQ versus Selective Reject ARQ

## Slide 8: Go-back-N ARQ
0
1
2
3
4
5
2
3
4
5
7
6
0
3
4
5
ACK0
ACK1
NACK2
ACK2
ACK3
ACK4
Station A
Station B
Time
(Frames)
Error
Discard
Discard
Discard
2
1

## Slide 9: Implementation
Fore API / network
Message out
Message out
Acks
(In),
nacks
(In)
Acks
(out),
nacks
(out)
Resends
Resends
Frames,
acks,
nacks
Copy In
Empty Output
Buffer
Send Frame
Timeout
Thread
Receive Frame
Fill Input
Buffer Thread
Copy Out
Application
Timeout
Thread
Application
Input buffer
Output buffer
Copy In
Empty Output
Buffer
Send Frame
Receive Frame
Fill Input
Buffer Thread
Copy Out
Input buffer
Output buffer
Send Stream
Receive Stream
Receive Stream
Message in
Message in
Send Stream
Acks
(out),
nacks
(out)
Acks
(In),
nacks
(In)

## Slide 10: Structure of Buffers
Output buffer
  Shaded areas indicated partially filled frames
  Unacknowledged data between begin and cur markers
  Unsent data between cur and end markers
Input Buffer
  No Frame structure needed
  Data received but not retrieved by application between begin and end markers
Window
Buffer
Out_buffer_begin
Out_buffer_cur
Out_buffer_end
Window
Buffer
In_buffer_begin
In_buffer_end
Frame

## Slide 11: Verification
Test Applications
  Half-Duplex Framework
  Full-Duplex Framework
Extreme Condition Tests
  Network Errors
  Application Anomalies

## Slide 12: Optimization
Buffer Copy
Checksum
Acknowledgement
Header
Window
200-Mhz UltraSPARC workstation
256 MB of memory
ForeRunner SBA-200 ATM adapter.
ForeRunner ASX-200BX ATM switch
155 Mb/s, full-duplex
155 Mb/s, full-duplex
200-Mhz UltraSPARC workstation
256 MB of memory
ForeRunner SBA-200 ATM adapter.

## Slide 13: Buffer copy optimization
Buffer copies originally took 500 s each allowing performance of 15 Mb/s
Highly optimized memory-to-memory copy written in assembly code
Data 64-byte aligned and in multiples of 64-bytes
Throughput shot up to 75 Mb/s

## Slide 14: Checksum Optimization
Checksums do not have to be sum of bytes of data
Data added up in eight byte chunks
Top half and bottom half added to give four byte checksum
Performance increased to 100 Mb/s

## Slide 15: Acknowledgement Optimization
Piggyback acks
Ack force mechanism
  Timer
  Yield technique
  Ack counter
Half -duplex throughput increased to 119 Mb/s

## Slide 16: Header Optimization
Header originally sent separately from payload. Small messages take longer so bandwidth wasted
Combined header requires leaving space in output buffer at beginning of each frame
Almost doubled throughput for 64-byte messages

## Slide 17: Window Optimization
Window of size eight requires over 72-kB buffers
Experimentally determine minimum window size that provides maximum throughput

## Slide 18: Performance Benchmarks
Half-duplex throughput
Full-duplex throughput
Latency
Latency Breakdowns

## Slide 19: Half-duplex Throughput
Extra overhead processing for small messages
Syracuse University: Fore API max throughput of 121.8 Mb/s
Guaranteed ATM shows max throughput of 119.0 Mb/s
TCP performance superior
Cornell’s Active Messages originally achieved similar results, then modified Fore API to achieve dramatic improvements

## Slide 20: Full-duplex Throughput
Not quite double half- duplex throughput
Max throughput of 216 Mb/s

## Slide 21: One-way Latency
Larger messages take longer to transmit
Minimum latency of .89 ms
Cornell’s Active Messages
  Originally achieved similar results using Fore API
  Showed that Fore API yields one-way latency of .85ms without guaranteed delivery
  Eventually modified Fore API to work well with small messages
  With modifications achieved latencies of 71s without guaranteed delivery, and 157 s with TCP guaranteed delivery

## Slide 22: Latency Breakdown, 8-kB
Measurements made using gethrtime
Fore API / network take 74% of Latency
University of Illinois at Urbana-Champaign indicates that network should take 30% of latency
Synchronization loss between 12% and 18%
Maximum throughput still possible because of buffering

## Slide 23: Latency Breakdown, 64-B
Fore API / network still take 73% of Latency
University of Illinois at Urbana-Champaign indicates that network should 30% for small sized messages also
Synchronization loss of 12% to 14%
Latency times scale down from 8-kB message. Overhead does not yet dominate latency

## Slide 24: Future Integration with SCALE
Imposed few demands on project
  Guaranteed ATM channel should be non-blocking
  All data passed should be 64-byte aligned and multiples of 64-bytes
Guaranteed ATM designed to be used with any application

## Slide 25: Summary
Design uses go-Back-N ARQ window-based error and flow control
Verification through torture tests
  Half-duplex framework and Full-duplex framework
  Simulation of network errors and application anomalies
Optimization
  64-byte buffer copy and checksum optimizations
  Acknowledgement, Header, and Window optimizations

## Slide 26: Future Research
Tighten integration with layers of code above and below
  Fore API provides excessive features such as quality of service and multicasting
  Fore API does not take advantage of 64-byte alignment
  Better coordination between two buffers at Guaranteed ATM and Fore API levels
Reduce synchronization loss
Tighten Integration with higher layers of SCALE