## Slide 1: Cisco Call Manager Architecture
References:
Cisco IP Telephony, Cisco Press, ISBN 1-58705-050-1
Cisco CallManager Fundamentals: A Cisco AVVID Solution, Cisco Press, ISBN 1-58705-008-0

## Slide 2: Topics
Abbreviations
Architecture Layer Overview
Link Layer
Device Layer
Media Control Layer
Call Control Layer

## Slide 3: Abbreviations
Abbreviations and their meaning are listed at URL
  http://www.cisco.com/univercd/cc/td/doc/product/voice/evbugl4.htm

## Slide 4: Architecture Layer Overview
Feature
Call Control
Aggregator
Device
Media Control
Link
Supplementary
Service API
Call Control
Signal
Call Control
Signal
TCP Library
Au Signal

## Slide 5: Cisco CallManager Architecture
Feature layer – handles all features that IP phones enable other than normal call operations
Call Control layer – handles communications with
  Feature layer using SSAPI
  Media layer using Au signals
  Aggregator layer using Cc signals
Media Control layer – provides media-related support for call connectivity between devices
Aggregator layer - uses Device layer to determine device registration
Device layer – controls the devices that are registered with CCM
Link layer – provides connectivity between devices

## Slide 6: Link Layer
TCP sockets are used to communicate across the network
  Transmission Control Protocol
  User Datagram Protocol
TCP libraries are used to implement the communication process

## Slide 7: Device Layer
Controls all devices that register with CCM
Provides 3 protocols for device support
  MGCP – used for gateways
  SCCP – used for phones
  H.323
Device layer entities
  H.323 – provides capability for connecting H.323 devices to CCM
    Device initialization
    Device registration
    Device deletion
    Other call-relate processing

## Slide 8: Device Layer (continued)
Device layer entities (continued)
  Station interface – processes all call signaling between CCM and phones
    Device registration
    Device deletion
    Other call-related processing
  PRI – ISDN primary rate interface (23B+D)
    Processes all call signaling between CCM and PRI gateway
    Communication to control, maintain and clear calls through the PSTN
  MGCP – Media Gateway Control Protocol
    Processes all call signaling between CCM and MGCP gateway
      Gateway registration
      Gateway deletion
      Other external call-related processing

## Slide 9: Device Layer Details
Feature
Call Control
Aggregator
Entities – Skinny, PRI, MGCP
Media Control
Link
Supplementary
Service API
Call Control
Signal
Call Control
Signal
TCP Library
Au Signal
Device Layer controls all devices
that register with CCM

## Slide 10: Call Manager Device Classes
Terminals
  Phones (clients)
  Applications (servers)
Gateways
  Voice only
  Voice/router

## Slide 11: Terminal Devices
Single output stream
Multiple input
streams
Voice
Single I/O
stream
IP
Multiple output
streams
Multiple input
streams
IP
Phone
Application

## Slide 12: Gateway Devices
Multiple output
streams
Multiple input
streams
IP
Multiple output
streams
Multiple input
streams
IP
Multiple I/O
streams
Multiple I/O
streams
Single I/O
stream
WAN
Voice
Voice
Voice-only
Voice/Router

## Slide 13: H.323 Implementation in CCM
Implementation of fully compliant H.323 terminal requires extensive computing power and memory
H.323 proxy can be implemented in a high performance server and can communicate with a “Skinny” client
Skinny client uses SCCP
  TCP/IP to communicate with CCM
  RTP/UDP/IP to communicate with another Skinny client or a H.323 terminal
  Establish, control and clear audio calls

## Slide 14: H.323 Implementation
IP Network
SCCP
Signaling
H.225, H.245
Signaling
Skinny
Client
H.323
Device
CCM
RTP audio stream

## Slide 15: Station Interface
Responsible for
  Device registration
  Device deletion
  Other call processing
Communicates with
  IP Phones using SCCP
  Call Control Layer
    Uses Aggregator layer to manage audio calls
      Establish
      Control
      Clear

## Slide 16: PRI Interface
PRI is ISDN PRI
  23B + D
    64 Kbps channels
    1544 Kbps total bandwidth (T1)
  Uses Q.931 on D channel for signaling
    Comparable to TCP in Internet protocol stack
    Doesn’t provide flow control or retransmission
      Assumes underlying layer is reliable
    Manages connection setup and tear-down

## Slide 17: MGCP
Supported in Device layer
Used to control VoIP gateways
Processes all call signaling between CCM and gateway
Responsible for
  Gateway registration
  Gateway deletion
  External call processing
    Communicates with telephony gateways
    Communicates with Call Control layer through Aggregation layer
      Establish, control and clear audio calls

## Slide 18: Media Control Layer
Responsible for connecting IP media to clients
IP media transported over RTP
Control of RTP source and receiver addresses is done by
  MGCP/SCCP – client server
  SIP/H.323 – peer/peer
Functions provided
  Simple connections – HDX and FDX connections
    Uses different codecs depending on situation
  MDCX functions – hold, transfer
  Multiple connections
    Uni-directional – unicast, multicast (used for music and paging)
    Bi-directional – Ad Hoc conferencing, Meet-Me conferencing

## Slide 19: Call Control Layer
Major functions
  Call Control – one instance of Cc/CCM
    Responsible to initialization and tear-down
  Call Control Child Process – one instance per-call basis
    Many processes may exist depending on call activity
    Life span = life of a call
  Digit Analysis – handles network addressing
    Uses tables to understand national dialing plans
      Tags used to understand digit strings
      Wildcards used to understand range of numbers