## Slide 1
High-Speed LANs

## Slide 2
LAN Backbone Local Networks
Used instead of single-LAN strategy
Better reliability
Higher capacity
Lower overall cost

## Slide 3
Applications Drive New Technology Usage
Token
Ring
Ethernet
Frame Relay
ATM
LAN
Campus
MAN
WAN
Private Line T1/T3
1000
100
10
FDDI
Bandwidth (Mbps)
1

## Slide 4
Application Demands
Shared LANs
ATM
Network Delay-Tolerant Application
Network Delay-Sensitive Application
Network Delay-Intolerant Application
Switched LANs
Traditional computing
Facsimile
E-mail
Compound document transfer
Videoconferencing
  Local
  Campus
  Wide area
Document imaging
Real-time multimedia playback off network Training videos Audio/video from laser discs, etc.

## Slide 5
Network Applications
Bandwidth
Time
Alphanumeric
Terminal/Host
Graphical
Client/Server
Multimedia
Client/Client
Notes: Network bandwidth requirements continue to increase because users continually demand that the network “go faster”. This demand is driven by several factors. Processor speeds continue to grow rapidly. Intel processor speeds have increased over 1000 fold from the 80286 to the Pentium. The information that is being processed is derived from local storage or obtained from across the network.
The first network applications involved alphanumeric interfaces which transfered 2000 characters between terminals and the host. Next came graphical interfaces involving approximately 400,000 pixels per screen between the server and the client. Today these applications are widely used and require additional bandwidth. The future indicates that first video and then multimedia applications will become common place. These applications require screen refreshment approximately 20 times per second. This requirement identifies the need for additional bandwidth. In addition to the increased bandwidth requirements more and more users are requiring network access.

## Slide 6
Network Applications
Referring Physicians, Clinics and HMOs
Medical Records
Image Storage
Specialists
Hospitals
Physician’s Workstation
Systems Services
Applications
Network Services
Transport
Computed Tomography
Gamma
Camera
Magnetic
Resonance
Imaging Devices
Telemedicine

## Slide 7
Network Applications
Videoconferencing
Re-engineering Program
• Core competencies
• Horizontal teams
• Time to market
Re-engineering Program
• Core competencies
• Horizontal teams
• Time to market
Re-engineering Program
• Core competencies
• Horizontal teams
• Time to market
Chicago
Los Angeles
Washington

## Slide 8
User Population
Increasing Bandwidth Usage in LAN’sToday
Bandwidth Per User
Terminal
10 Users per LAN
100 Kbps
1 Mbps
10 Mbps
100 Mbps
100 Users per LAN
ATM
FDDI Fast Ethernet
Dedicated
LAN
Notes: The cost of networking technology is continually being reduced which permits more bandwidth to be available for each user. Consequently, the number of users increases and the peak of the curve shifts toward the right side of the graph.
Over time the peak of the curve shifts toward dedicated LANs which will provide 10 to 16 Mbps of bandwidth per user. A peak point of 10 - 16 Mbps is important because it requires no change in the end point hardware or software or in the network wiring. In addition, technicians are already trained and experienced in supporting Ethernet and Token Ring environments.
As the costs of LAN switches decline they will be used to provide a dedicated LAN port per user. The use of dedicated LAN ports will supplant shared LAN hubs.
As the peak of the curve shifts to the right it is important to note that users will continue to connect to LANs at all bandwidths.

## Slide 9
Fast Ethernet
Integrates with existing systems
Media types
  100BaseTX: UTP5
  100BaseFX: Fiber optics
Uses star topology
  Broadcast mode
    Multi-port hub
  Full-duplex mode
    Switching hub must be used

## Slide 10
Switched Fast Ethernet
Switch
Unshielded twisted pair
Fiber optic cable
Full duplex messaging
100 Mbps link speed
Distributed folded bus topology
Dedicated bandwidth environment
Notes: CSMA/CD media access protocol
10/100 Mbps twisted pair or fiber media
1518 byte maximum link level frame
Full duplex message traffic is possible if the link from the switch to the user is point-to-point

## Slide 11
Value of Fast Ethernet
Same format, MAC as 10Mbps Ethernet
Mature technology = low prices
Can be mixed to provide more aggregate bandwidth but no change on the desktop
Can go up to 200Mbps to servers, graphics workstations, etc.

## Slide 12
Gigabit Ethernet
Standard in development
  IEEE 802.3z (Draft 3 is latest)
Designed for upgrade
  CSMA/CD media access
  Ethernet frame format
Uses optical fiber cable
  1000BaseSX (MMF - 500 m)
  1000BaseLX (SMF - 3 Km)
Provides backbone connectivity

## Slide 13
Fiber Distributed Data Interface
Multimode/single mode optical fiber
Half duplex messaging
100 Mbps link speed
Dual counter rotating rings
Single/dual station attachment
Shared bandwidth environment
Notes: Dual counter rotating rings with dual attached stations allows for loopback if a node fails
Maximum frame size is 4500 bytes
Token passing media access protocol
Deterministic performance

## Slide 14
When to Consider Switching
Traffic is no longer mostly local
  80/20 rule does not apply
When routing table updates consume large amounts of bandwidth
To avoid LAN bottlenecks
To provide constant bandwidth to a large number of users
To increase throughput and availability

## Slide 15
When to Consider Switching
Use of client/server technology
Use of dynamic workgroups
Increased user bandwidth requirements
Individual port management required
Need port, protocol, addressing flexibility
Preserve installed technology investment

## Slide 16
Virtual LANs
Switching arrangements that group users into virtual communities
Create logical networks independent of physical location
Permits moves, adds and changes without
  Reassigning IP addresses
  Changing physical wiring structures

## Slide 17
Virtual LANs
Three implementation methods
  ATM LAN Emulation
  IEEE 802.10
  Proprietary
    Cisco Tag Switching

## Slide 18
ATM LANs
Support multiple classes of service
Support isochronous traffic
Link LAN to WAN without technology change
Scale to higher speeds
Permit desired level of performance to be assigned as needed
Performs like a multi-protocol switch

## Slide 19
ATM Forum LAN Emulation
A MAC (Media Access Control) layer specification, known as LANE 1.0, that allows the ATM fabric to emulate a logical Ethernet or Token Ring segment.
Definitions:
  LAN Emulation User Network Interface - Referred to as “LANE 1.0”. It defines the interface between a legacy LAN attached device and the ATM network.
  LAN Emulation Services - They serve the following functions: initialization , address registration / resolution, and data forwarding. They consist of the LECS, LES, and BUS.

## Slide 20
ATM Forum LAN Emulation
Definitions (continued):
  LAN Emulation Configuration Server (LECS) - Maintains the configuration information for each emulated LAN.
  LAN Emulation Server (LES) - Performs the MAC-to-ATM address resolution functions in an emulated LAN.
  Broadcast Unknown Server (BUS) - Performs the multicast server function and broadcasts packets to multiple LECs.
  LAN Emulation Client (LEC) - Multiple LECs connect to the LANE services. Client functionalities are typically implemented on adapters, routers, and ATM-to-LAN edge devices.

## Slide 21
LAN Emulation
AAL 5 segments data frames into cells
ATM LAN Edge Device implements Proxy LANE Client and MAC Layer LANE
Proxy client forwards unregistered MAC addresses
Legacy LAN Host requires no changes
LANE emulates a bridged LAN segment

## Slide 22
LAN Emulation Network
UNI 3.0/3.1 Signaling
IISP routing
Static ATM addressing
LANE provides LAN connectivity
Switch
IISP
LANE Clients
UNI
Switch
Switch
Switch
Bridge
Bridge
IISP
Bridge
TR Network
Ethernet Network
Ethernet Network
LANE Servers
(LES, BUS)
LANE Clients
(Edge Devices)
Notes: SONET - Layer 1
LANE - Layer 2
* UNI 3.0/3.1 signaling
* IISP (Interim Interswitch Signaling Protocol) uses static table for routing

## Slide 23
RFC 1483
Defines multi-protocol encapsulation for network traffic over ATM AAL 5
  Routed Encapsulation
    Non-VC Multiplexing - protocol families share a VC
    LLC/SNAP Header identifies protocol type
    Used in RFC 1577
  Bridged Encapsulation
    Non-VC Multiplexing used for “Bridging over ATM”
      Used by pre-LANE products
    VC-Multiplexing - Protocol families on separate VCs
      Used by LANE products

## Slide 24
RFC 1577
Classical IP and ARP over ATM
  Defines the ATM address resolution protocol
  Maps IP addresses to ATM addresses within a logical IP subnet.
  A group of IP Hosts on the same subnet are connected to a single ATM Network called a logical IP subnet
  ATM Address Resolution Server
  No Broadcasts
  No Routing