## Slide 1
WAN Multiservice Backbone Solutions
Cisco Systems
Networkers ‘98
Denver, CO

## Slide 2
WAN Networking Environment
Branch Offices
Regional Offices
Headquarters
Home Offices
Telecommuters
Backbone
Access
Other
Multiple Networking Environments where All Users Require Ubiquitous Access to Corporate Applications

## Slide 3
WAN Networking Challenges
Multiple Traffic Types
Increasing Traffic Volumes
Telecom Budget
Increased Scope of WAN
Telecom
Manager

## Slide 4
Wide Area Network Requirements
Multiservice Consolidation
Bandwidth Efficiency
Performance and QoS Guarantees
Carrier-Class Reliability
Ease of Operation and Management
Minimize Bandwidth Costs
Maximize Efficiency
Maximize Performance
Maximize Availability
Minimize Management and Maintenance

## Slide 5
Wide Area Network Costs
Capital costs (hardware): non-recurring
  Written off over three to five years
Bandwidth rental costs: recurring
  One to five year contracts
  Penalties for cancellation
  Highest month recurring expense
Source: Data Communications
Transmission Costs 87.8%
Hardware Costs 8.0%
Software Costs 2.7%
Maintenance 1.5%

## Slide 6
WAN Service Requirements
LAN interconnectivity
  Router and workgroup switches
Voice toll bypass
  PBX tie trunking and voice switching
Videoconferencing
  Room-to-room, desktop
Legacy data
  SNA, X.25, async data
TDM migration
  Transport option for aging TDM systems
Multiservice Networking
PBX
Videoconferencing
Legacy Data
WAN Router
Workgroup Switch
ISDN
FR/LL
VPN/LL
FR/LL
ATM/LL
Notes: 4
Within an enterprise backbone location, there are several applications that require connectivity to other locations. These include:
- LAN interconnectivity using routers and campus switches
- corporate voice interconnectivity for PBX tie trunking
- videoconferencing - either desktop or room-to-room
- legacy data connectivity for SNA, X.25, Async applications
In most current networks, these applications use a separate network infrastructure - either via public services (like VPNs for voice and data) or using private lines. Although some customers have consolidated these applications over a single infrastructure, in most cases they are using a circuit switched infrastructure - using time division multiplexed technology. This infrastructure consolidates the interfaces but still using separate bandwidth in the network.

## Slide 7
Multiservice Integration
Leased Line
or
Public
Network
PBX
Videoconferencing
Legacy Data
WAN Router
Workgroup Switch
Notes: 6
The Cisco IGX addresses all of the current enterprise WAN requirements.
It is high performance (1.2Gbps), multiservice, carrier class wide area switch that is used in both enterprise and service provider networks worldwide.
The IGX is the choice of customers who want to implement a reliable, bandwidth efficient wide area backbone that can provide the necessary Quality of Service mechanism needed when consolidating multiple applications.

## Slide 8
WAN Trunking Requirements
Flexible trunking
  Sub-rate leased lines (64kbps to T1/E1)
  n x T1/E1 leased lines
  T3/E3 leased lines
  OC-3/STM-1 leased lines
  Carrier services
Bandwidth efficiency
OC-3
STM-1
T3/E3
n x T1/E1
Public
Network

## Slide 9
Typical Wide Area Costs
Capital costs (hardware): non-recurring
  Written off over three to five years
Bandwidth rental costs: recurring
  One to five year contracts
  Penalties for cancellation
Design costs
  A quick-and-dirty WAN design can waste millions in recurring bandwidth cost

## Slide 10
Design Process
Understand network environment—tariffs, traffic
Understand network requirements—strategy, growth
Understand effect of the requirements
Create data to represent network environment
Design the proposed network
Interpret results
Abstract
Practical

## Slide 11
Why a Design Process?
Spare bandwidth = growth potential
Unused bandwidth = wasted money
New unused bandwidth too early = wasted money
Trunk Bandwidth
Kbps
Primary
Resilience
Growth
time
Today
Failure
Additional BW
> Provisioning Time

## Slide 12
Beancounter’s View
The accountant sees bandwidth as a recurring cost
Any cost not covered by revenue is loss
Unnecessary distance/hops = loss
For each day new capacity is early—loss rises
kbps
Trunk Total
Utilization
New Trunks
Profit
Loss

## Slide 13
Designing the WAN Backbone— An Iterative Process
Identify all network design requirements
Identify all network locations
Identify all applications
Collect historical network traffic data and determine transaction profiles, rates as well as application topology
Identify all traffic growth
Analyze data and design the multiservice network
Determine equipment configuration
Optimize design to ensure design criteria are met or exceeded
Finalize equipment configuration

## Slide 14
Network Design Assumptions
Service levels
  Network performance
    CLR, CDV, and CTD for ATM
    Grade of service for voice
  Acceptable response times for transaction-oriented applications
  Minimum bandwidth requirement
  Availability requirement
Application types and profiles
  Individual user transaction (bytes in/bytes out)
  Peak transaction rate (transaction/hour or min or sec)

## Slide 15
Network Applications
Data
  All real-time transaction-oriented data applications (IP, SNA, X.25)
  All non-real time data applications (e-mail, ftp)
  Legacy async/sync data
Voice
  PBX interconnectivity—toll bypass
  Private Line Auto Ringdown (PLAR)
  Hoot ’n’ Holler
Video
  Room-to-room videoconferencing
  Desktop video

## Slide 16
Collect Historical Traffic Data
Collect available usage data for all applications (for as long a duration possible to capture seasonalities)
Identify source and destination of traffic
Data
  Router: traffic reports, accounting data, server usage data
  Other: mainframe reports
Voice
  PBX call detailed records
Video
  MCU usage reports

## Slide 17
Data Network Analysis
Analyze available data traffic reports
Use seasonal information to determine average and most busy days
Determine amount of traffic in these days, estimate the busy and average hour traffic
  x% of daily traffic occurs in busy hour
  y% of daily traffic occurs in average hour
  Confirm assumptions:
    Total daily traffic/number of business hours in the day
    Identify busy hour

## Slide 18
Data Applications - Network Traffic
Minimum Throughput Requirements in Kbps During Busy Hour
To
From

## Slide 19
Voice Network Analysis
Analyze voice call detailed records
Use seasonal information to determine average and most busy days
Number of calls and average duration
Determine amount of traffic in these days, estimate the busy and average hour traffic
  x% of daily traffic occurs in busy hour
  y% of daily traffic occurs in average hour
  Confirm assumptions:
    Total daily traffic/number of business hours in the day
    Identify busy hour

## Slide 20
Voice Applications - Network Traffic
Average Number of Calls Between Locations During Busy Hour
To
From

## Slide 21
Video Network Analysis
Analyze MCU usage stats
Use seasonal information to determine average and most busy days
Number of conferences and average duration
Identify busy hours
start here

## Slide 22
Video Network Analysis
Average Number of Calls Between Locations During Busy Hour
To
From

## Slide 23
Sample Daily Traffic Pattern
kbps
Time of Day
Data
Voice
Video

## Slide 24
Identify Traffic Growth
Growth of existing applications
  More users
    Mergers
    Acquisitions
  New sites
  % growth over one, two, and three years
New applications
  Business and productivity applications

## Slide 25
Overall WAN Network Analysis All Applications
Current Traffic With Some Growth Projections (X% in the Next Y Years)
To
From

## Slide 26
Designing the Optimal Backbone Topology
Attempt to select the best network
Exercise 1
Notes: Cannot link the nodes because we do not know the traffic volume at each site

## Slide 27
Exercise 2
Designing the Optimal Backbone Topology
Circle size represents traffic volume to node
Attempt to design best network
Notes: Cannot link nodes because we do not have a traffic matrix

## Slide 28
What Is Needed to Design the Optimal Backbone Topology?
Considerations when determining the optimal topology:
  Traffic flows between locations for transaction-oriented and non-transaction-oriented traffic
  Availability requirements—network resiliency
  Congestion conditions
  Cost of bandwidth between locations

## Slide 29
Designing the Optimal Backbone Topology
Attempt to design best network adding only T1
A B C D E
A 0 3 3 7 0
B 0 0 2 0 0
C 1 0 0 0 1
D 0 2 0 0 2
E 1 0 6 0 0
Traffic Volume in 64k
A
B
C
D
E
Exercise 3
Notes: Cannot link nodes because we do not know the tariffs
We need to know the tariffs in order to determine which trunks to select

## Slide 30
Designing the Optimal Backbone Topology
Design best network using available tariff and traffic matrix
A B C D E
A 0 3 3 7 0
B 0 0 2 0 0
C 1 0 0 0 1
D 0 2 0 0 2
E 1 0 6 0 0
Traffic Volume in 64k
Tariff = $15000 link setup (FT1, T1, nXT1)
$5/mile
5 miles
A
B
C
D
E
Exercise 4
Notes: In order to design a network we need to have:
nodal site definitions
capacity requirements from node to node matrix
tariff information
strategy for growth

## Slide 31
Solution
What if the link between A and B fails?
Site B is isolated and loses communication with the rest of the network
A
B
C
D
E
A
B
C
D
E
x

## Slide 32
Better Solution
Each site has an alternate path
A
B
C
D
E

## Slide 33
Re-Routing Capacity
If link between A and B fails, is there sufficient capacity to re-route all connections?
A
B
C
D
E
A B C D E
A 0 3 3 7 0
B 0 0 2 0 0
C 1 0 0 0 1
D 0 2 0 0 2
E 1 0 6 0 0
Traffic Volume in 64k
T1
T1
T1
T1
T1

## Slide 34
PBX
Videoconferencing
Legacy Data
WAN Router
Workgroup Switch
Multiservice Integration
Leased Line
or
Public
ATM
Network
ATM
Notes: 6
The Cisco IGX addresses all of the current enterprise WAN requirements.
It is high performance (1.2Gbps), multiservice, carrier class wide area switch that is used in both enterprise and service provider networks worldwide.
The IGX is the choice of customers who want to implement a reliable, bandwidth efficient wide area backbone that can provide the necessary Quality of Service mechanism needed when consolidating multiple applications.

## Slide 35
ATM Services
High-performance, high-density standards-based ATM services (Multiple T1, T3 or OC-3 ports)
High sustained backplane throughput
VPC or VCC connections (CBR, VBR, UBR, ABR Class of Service)
Standards-based ABR support
  EFCI marking
  Explicit Rate (ER)
  Virtual Source/Virtual Destination VS/VD
Standards-based dual leaky bucket policing
Per virtual circuit buffering (large number of cells buffers)
Dynamic buffer management and scaling
OC-3
OC-3
T3
n x T1
OC-3
ATM UNI
T1, T3
ATM UNI
Foreign
ATM
Network

## Slide 36
Frame Relay Services
High-performance, high-density standards-based Frame Relay services (Multiple T1, V.35 or HSSI ports)
Standards-based UNI/NNI interfaces
PVC connections with QoS capabilities
ITU standards-based congestion avoidance support (ABR)
Standards-based Congestion Notification (FECN/BECN)
Standards-based Frame Relay to ATM network and service interworking
Standards-based dual leaky bucket policing
Per virtual circuit buffering (large number of frame buffers)
Dynamic buffer management and scaling
V.35/T1/HSSI
FR UNI
T1
FR UNI/NNI
T3
n x T1
OC-3
OC-3
Foreign
ATM
Network
Foreign
FR
Network

## Slide 37
T3
n x T1
OC-3
OC-3
Voice Services
High-performance, high-density voice services (Multiple T1 ports)
Cell switching ensures low delay and low variability in delay
Standards-based compression (ADPCM, LD-CELP, and CS-ACELP) and silence suppression
On-board echo cancellation
Fax/modem detection—automatically disables compression and echo cancellation; fax relay
CAS and CCS support—transport and signaling
T1
T1
PBX
PBX
Foreign
ATM
Network
Notes: By providing the adaptation layer on a per connection basis, the IGX is able to examine the traffic to determine if it is meaningful information or silence. Voice Activity Detection determines if a person is speaking, and if so, generates cells. When someone is silent or the phone is on-hook, that bandwidth is made available to other connections. During a conversation, a person speaks less than 40% of the time. The rest of the time, that bandwidth can be saved. When the phone is on-hook, 100% of the bandwidth can be saved.
This bandwidth savings means that more connections can be carried on fewer trunks, thus saving money. It also frees bandwidth for reroutes, and so that frame relay/frame forwarding connections can burst in order to improve the performance of those applications.
TDMs, or TDMs that encapsulate an entire trunk into ATM, must use valuable bandwidth to carry this silence across the network.
Voice Activity Detection can be enabled on a per-channel basis.
Voice Activity Compression is in addition to the normal digital voice compression techniques that the IGX can do.

## Slide 38
Voice Switching
High-performance, highly scalable distributed voice switching capability
Q.SIG, DPNSS, Q.931A, CAS, 4ESS supported
DSS1 Interworking with Q.SIG and DPNSS
Interoperability testing conducted with Nortel, Lucent, Siemens, OKI, Fujitsu, Alcatel, Ericsson, Phillips, NEC PBXs
T1
T1
PBX
PBX
T1
Voice
Switching
Voice Switching Saves Equipment (PBX and Switch) Costs and Enhances Bandwidth Efficiency
PBX
Notes: By providing the adaptation layer on a per connection basis, the IGX is able to examine the traffic to determine if it is meaningful information or silence. Voice Activity Detection determines if a person is speaking, and if so, generates cells. When someone is silent or the phone is on-hook, that bandwidth is made available to other connections. During a conversation, a person speaks less than 40% of the time. The rest of the time, that bandwidth can be saved. When the phone is on-hook, 100% of the bandwidth can be saved.
This bandwidth savings means that more connections can be carried on fewer trunks, thus saving money. It also frees bandwidth for reroutes, and so that frame relay/frame forwarding connections can burst in order to improve the performance of those applications.
TDMs, or TDMs that encapsulate an entire trunk into ATM, must use valuable bandwidth to carry this silence across the network.
Voice Activity Detection can be enabled on a per-channel basis.
Voice Activity Compression is in addition to the normal digital voice compression techniques that the IGX can do.

## Slide 39
T3
n x T1
OC-3
OC-3
Foreign
ATM
Network
Circuit Data Services
High-density circuit data services for transparent data connectivity
  T1 with sub-rate (fractional DS0) or super-rate (n x 56/64 Kbps)
  Multiple V.35 or RS-449 ports (for data rates > 20 Kbps)
  Multiple RS-232 ports (for data rates < 20 Kbps)
Cell switching ensures low delay and low variability in delay
Repetitive pattern suppression and on-demand connections enable cost savings through better use of bandwidth
Sync/Async
Device
Sync/Async
Device
T1
T1
Notes: By providing the adaptation layer on a per connection basis, the IGX is able to examine the traffic to determine if it is meaningful information or silence. Voice Activity Detection determines if a person is speaking, and if so, generates cells. When someone is silent or the phone is on-hook, that bandwidth is made available to other connections. During a conversation, a person speaks less than 40% of the time. The rest of the time, that bandwidth can be saved. When the phone is on-hook, 100% of the bandwidth can be saved.
This bandwidth savings means that more connections can be carried on fewer trunks, thus saving money. It also frees bandwidth for reroutes, and so that frame relay/frame forwarding connections can burst in order to improve the performance of those applications.
TDMs, or TDMs that encapsulate an entire trunk into ATM, must use valuable bandwidth to carry this silence across the network.
Voice Activity Detection can be enabled on a per-channel basis.
Voice Activity Compression is in addition to the normal digital voice compression techniques that the IGX can do.

## Slide 40
WAN Trunking Requirements
Flexible trunking
  Sub-rate leased lines (64kbps to T1)
  n x T1 leased lines
  T3 leased lines
  OC-3 leased lines
  Public/private ATM services
Bandwidth efficiency
OC-3
OC-3
T3
n x T1
Public ATM
Network

## Slide 41
Intelligent Quality of Service Management

## Slide 42
Connection Routing Management
WAN switches implement distributed intelligence mechanisms
Easy connection routing and fast re-routing
The network is the database!

## Slide 43
Class of Service Management Per VC Queuing
Accommodates large bursts of incoming frames
Provides user and traffic “firewalling”
Enables network to provide performance guarantees for different types of traffic
Allows the network to buffer incoming data during times of congestion
Customer
Access
Equipment

## Slide 44
Class of Service Management Per VC Rate Scheduling
Intelligent admission policy into the network
Optimal architectural framework for implementation of advanced traffic management feedback
Admission rate adjusted down if congestion indication is received
Admission rate adjusted up if no congestion indication
Per VC Rate Scheduler
Per VC Queue
Network Feedback
User Data
User Connection

## Slide 45
Class of Service Management Multiple Class of Service Queues
Ingress
Per-VC
Queues
Network
Queues
Egress
Egress
Queues
VC x
VC y
VC z
Port A.1
Trunk N
Port B.1
Node A
Node B
Notes: Per VC buffers and queuing are an essential ingredient in delivering a guaranteed level of performance to all users.
Per VC queues allows firewalling each connection. It’s almost like having your own lane on the highway. Traffic in other lanes cannot really affect your lane.
Why is this important? To be able to deliver performance guarantees to users based on the subscribed rate.
So consider a network where you have both SNA traffic and TCP/IP traffic operating on separate PVCs on the same Frame Relay port. Per VC queuing and buffering can allow the SNA traffic to be serviced with a higher priority level than the TCP/IP traffic.
Most competitors use FIFO queues at the egress ports instead, where increased usage of one “port” can totally block another port.

## Slide 46
Optimized Bandwidth Management
Voice compression
  32 kbps, 24 kbps, 16 kbps ADPCM, 16 kbps LD CELP, 8kbps CS ACELP
  D-Channel Compression
Silence suppression
  No cells generated for silence
Fax Relay
  Using 9.6kbps of bandwidth for Group 3 Fax
Speech
Speech
Silence
PBX
PBX
Minimizing Network Bandwidth for Voice

## Slide 47
Optimized Bandwidth Management
Repetitive pattern suppression
  No cells generated for repetitive patterns
  Example: SDLC/HDLC Information frames have multiple flags {7E(H)} between each frame. Why send those flags on the trunks?
Data
Data
Flags
Legacy Data Device
Legacy Data Device
Compressing Repetitive Patterns for Legacy Data

## Slide 48
Network Applications
Home Office
  Voice—analog (one or two ports)
  Data—LAN and serial
Branch Office
Voice—analog (up to 10 ports), some up to one T1/E1
Data—LAN and serial ports
Video—videoconferencing
Backbone
Voice—digital (multiple T1/E1 interfaces)
Data—higher speed LAN and serial ports
Video

## Slide 49
Access Networking Requirements
Enterprise Wide Area Backbone
Dedicated Line
Access
Voice
Video
LAN
Ser. Data
QoS Guarantees
Survivability
Scalability
Efficiency
Cost
Interfaces
Trunking
Intelligence
Voice
Video
LAN
Ser. Data
Branch/Regional Office
Collector Network
Connectivity
Quality of Service
Management
Frame Relay
or ATM
Notes: The branch office has some specific requirements:
1) Due to the generally large number of branches compared to the number of central or regional sites the solution has to be cost effective
2) While providing a cost effective solution the vendor has to make sure that a wide variety of interfaces is available to serve all the applications
3) The trunking option are also very important, because the line costs easily exceed the actual equipment cost. Trunking has to be flexible (ISDN, leased line, Frame Relay, ATM) to choose the most effective trunking for each branch without degrading the service level
4) To save on WAN bandwidth the access device has to have a certain intelligence to generate minimum traffic flows over the wide area and has to make most efficient use of the available bandwidth
In the backbone spanning central and regional sites features like reliability (redundancy), scalability (port density) and bandwidth efficiency are the major differentiator between vendors.
To offer a complete solution for the individual application the seamless interworking between the branch and the backbone becomes key. Connectivity, Quality of Service (QoS) and Management make the difference between isolated solutions and true End-to-End solutions.

## Slide 50
T3
n x T1
Increasing demand to extend the multiservice backbone to branch offices or to customer premises
A consistent set of services (data, voice, video) has to be available everywhere in the network
Access-Backbone Interworking
T1
Public
ATM/FR
Network
64kbps to T1
Public
FR/ATM
PBX

## Slide 51
Extending the Backbone…
Depending on the specific customer environment, multiple solutions exist
Connectivity to the access layer can be provided via Leased Lines, ATM, or Frame Relay running at speeds from 64kbps to 155 Mbps
Data applications can be based on LANs, Frame Relay, ATM or legacy protocols
Voice can be VoFR, VToA, or VoIP
Video can be a synchronous bitstream, Frame-, ATM-, or IP-based
Notes: The different applications which need to be supported all the way to the branch office also result in different requirements for the branch office networking equipment.
Data applications may be based on LANs (Ethernet or Token Ring), Frame Relay ATM or legacy protocols. Depending on the type of application different type of services characteristics are required:
- specific physical interfaces
- specific protocols (layer 3 routing, layer 2 switching)
- delay requirements
Voice applications can also be served using different technologies:
- Voice over Frame Relay (VoFR)
- Voice Transport over ATM (VToA)
- Voice over IP (VoIP)
Video can also come in many flavors and the equipment has to provide the flexibility to support all of them.
Last but not least the size of the branch office, i.e. the data and voice volume present has to be considered in during the selection of the networking equipment.
CISCO’s branch office solutions offer most available technologies to support any application and scale to any branch office size.