## Slide 1: Signaling System 7
Chapter 4

## Slide 2: SS7 Architecture
Used to switch information messages
  Set up calls
  Manage calls
  Release calls
  Maintain the signaling network

## Slide 3: SS7 Architecture
Common channel signaling network
  Separated from the voice plane
  3 signaling elements
    Service Switch Point (SSP) – end office or tandem switch that connect voice circuits and provide call management
    Signal Transfer Point (STP) – routes all signaling messages in network
    Service Control Point (SCP) – provides database access for additional routing information used in call management

## Slide 4: SS7 Architecture
Signaling Modes
  Associated signaling – signaling and voice paths are directly connected between the signaling endpoints
  Nonassociated signaling – signaling and voice paths are logically separated
    Signaling messages may pass through multiple end points to reach destination while voice path may be direct
    Most common implementation used

## Slide 5: SS7 Protocol Stack
L 7
L 6
L 4
L 5
L 3
L 1
OSI
L 2
TCAP
SCCP
MTP L3
MTP L2
MTP L1
ISUP
TUP
Signaling Point Functions
L 4
L 3
L 1
SS 7
L 2

## Slide 6: MTP L1 – Physical Layer
North American standard is T1 (DS1)
  Total payload is 1536 Kbps
  T1 link framing is 8 kbps
  Each DS1 is 193 bits
    Frame rate is 8K frames/sec
  24 Full duplex channels (DS0)
    Each DS0 has 64 Kbps bandwidth

## Slide 7: MTP L2 – Data Link Layer
Provides reliable point to point links between network endpoints
  Error detection and correction
    Use CRC-16 for detection
    Use frame retransmission for correction
  Frame (packet) sequencing
    Used to manage frame acknowledgment
    Used to manage frame retransmission

## Slide 8: MTP L2 – Data Link Layer
Frame types
  Fill-In Signal Unit (FISU)
    Provides link error detection
  Link Status Signal Unit (LSSU)
    Provides link status on link between 2 directly connected nodes
  Message Signal Unit (MSU)
    Provides structure to carry SS7 information messages

## Slide 9: FISU Format
Flag
FCS
BSN
FSN
LI
BIB
FIB
Direction of frame transmission
Flag – Start of frame indicator 8 bits pattern 01111110
BSN – Backward Sequence Number used in frame acknowledgment
FSN – Forward Sequence Number used to identify transmitted frame
BIB – Backward Indicator Bit used in frame retransmission
FIB – Forward Indicator Bit used in frame retransmission
LI – Length Indicator identifies type of signaling unit 6 bit field 2 bits unused
LI = 0 indicates FISU LI = 1,2 indicates LSSU
LI = 3,…,63 indicates MSU
FCS – Frame Check Sequence uses CRC-16 to calculate value used to verify link integrity
usually a 16 bit field

## Slide 10: LSSU Format
Flag
FCS
BSN
FSN
LI
BIB
FIB
Direction of frame transmission
Flag – Start of frame indicator 8 bits pattern 01111110
BSN – Backward Sequence Number used in frame acknowledgment
FSN – Forward Sequence Number used to identify transmitted frame
BIB – Backward Indicator Bit used in frame retransmission
FIB – Forward Indicator Bit used in frame retransmission
LI – Length Indicator identifies type of signaling unit 6 bit field 2 bits unused
LI = 0 indicates FISU LI = 1,2 indicates LSSU
LI = 3,…,63 indicates MSU
SF – Status Field 8 bits in North America but only 3 are used to report link status
FCS – Frame Check Sequence uses CRC-16 to calculate value used to verify link integrity
usually a 16 bit field
SF

## Slide 11: MSU Format
Flag
FCS
BSN
FSN
LI
BIB
FIB
Direction of frame transmission
Flag – Start of frame indicator 8 bits pattern 01111110
BSN – Backward Sequence Number used in frame acknowledgment
FSN – Forward Sequence Number used to identify transmitted frame
BIB – Backward Indicator Bit used in frame retransmission
FIB – Forward Indicator Bit used in frame retransmission
LI – Length Indicator identifies type of signaling unit 6 bit field 2 bits unused
LI = 0 indicates FISU LI = 1,2 indicates LSSU
LI = 3,…,63 indicates MSU
SIO – Service Information used to indicate the protocol type and SS7 version
SIF – Service Indicator Field contains routing label & upper layer control information
FCS – Frame Check Sequence uses CRC-16 to calculate value used to verify link integrity
usually a 16 bit field
SIO
SIF

## Slide 12: SCCP – Signaling Connection Control Part
SCCP provides network services on top of MTP3
  Combination known as Network Service Part (NSP)
  SCCP has interfaces to TCAP and ISUP
SCCP Services
  Connection-Oriented Services – not used
  Connectionless Services and Messages
    Provides transport layer for TCAP connectionless services

## Slide 13: SCCP – Signaling Connection Control Part
SCCP Services (Continued)
  SCCP Management Functions
    Maintain transfer of SCCP messages during failure conditions
      Provide alerts to TCAP and ISUP
      Maintains interfaces to MTP and SCCP connectionless control
    Divided into 3 groups
      Signaling Point Status – relies on TMP services
        MTP pause, resume and status information
      Subsystem Status – each subsystem provides information directly to SCCP management process
      Traffic Management – reroutes messages between duplicate subsystems to ensure that service is maintained when a failure occurs

## Slide 14: ISUP – ISDN User Part
ISUP connects, manages and disconnects all voice and data calls to PSTN
  Supports ISDN, analog, and ISDN-to-analog users
  Widely implemented in North America
  Widely adopted internationally but with national variations
  Provides increased capabilities over TUP

## Slide 15: ISUP – ISDN User Part
ISUP Services
  Basic service – setup, management and teardown of voice and data calls in PSTN
  Supplementary services – used to support voice and data calls (not needed for setup)
    Caller ID
    Call forwarding
    Last number redial

## Slide 16: ISUP – ISDN User Part
End-to-End Signaling
  Procedures to establish, maintain and release connections
  Uses messages to indicate capabilities
    Initial Address Message (IAM)
    Address Complete Message (ACM)
    Answer Message (ANM)
    Call Progress (CPG)
  Two methods for passing end-to-end signaling
    Pass-along method – information passes through a series of switches to reach terminating end office
    SCCP method – uses SCCP to route signaling information through the network. Signaling path can change for a particular circuit

## Slide 17: ISUP – ISDN User Part
Call Setup
Off hook
Dial tone
Send address
IAM
Local Office
Remote Office
Intermediate
ACM
IAM
Provide ringback
tone
ACM
Ring remote
Off hook
ANM
Create voice path
Create voice path
ANM
Enable connection

## Slide 18: ISUP – ISDN User Part
Call Teardown
Hang up
indication
Local Office
Remote Office
Intermediate
SUS
SUS
On hook
RLC
RLC
On hook
REL
REL