## Slide 1
Introduction to WAN Switching
Cisco Systems
Networkers ‘ 98
Denver, CO
June 1998
Notes: 1
3
3

## Slide 2
Agenda
Wide Area Network Environment
Wide Area Network Requirements
WAN Switching Technologies
Cisco WAN Solution
Case Study
Notes: The agenda is as follows:
First we will briefly review the requirements for the enterprise WAN and see which Cisco products address these needs
We will then cover an update of the IGX product - where it has been, where it is today
Last, but not least, I will provide you an overview of the current roadmap for this specific product.
This presentation does not cover roadmaps of any other Cisco products.

## Slide 3
WAN Networking Environment
Branch Offices
Regional Offices
Headquarters
Home Offices
Telecommuters
Backbone
Access
Other
Multiple Networking Environments where All Users Require Ubiquitous Access to Corporate Applications

## Slide 4
WAN Networking Challenges
Multiple Traffic Types
Increasing Traffic Volumes
Telecom Budget
Increased Scope of WAN
Telecom
Manager

## Slide 5
Multiple Traffic Types
IP
IPX
AppleTalk
X.25
SNA
Voice
Video
Wide Area Network
Leased Lines, Satellite, Microwave Circuit Switched, IP, Frame Relay, ATM
Wide Area Network

## Slide 6
Source: Gartner Group, 1997
Traffic Explosion
More than 300% Growth in WAN Traffic by 2002!
1997
2002
Voice
Video Teleconference
Office Applications
Client to Server
Server to Server
Internet/Intranet
Notes: Welcome to the Enterprise WAN segment of the Integrated Service show. Over the next hour we will cover the latest Cisco solutions for integrating voice into a data network. Specifically we will cover Voice over ATM, Voice over Frame Relay, and Voice over IP. You should be working with your customers today in engineering their integrated voice and data networks. The customer benefits are clear - greatly reduced networking costs by consolidating access lines and parallel networks into one seamless network infrastructure from the branch office site through the wide area network. In addition, customers will benefit from improved quality of service, and simplified network management.
To start, lets take a look at what is driving WAN traffic today. Gartner group predicts more than 300% growth in WAN traffic by the year 2002. This traffic will be a mix of voice, client-server, and video services such as distance learning applications.

## Slide 7
Telecom Budgets
Although Traffic Volumes Are Increasing, Telecom Budgets Are Not— in Fact in Some Cases Decreasing
Old
Telecom
Budget
New
Telecom
Budget

## Slide 8
Wide Area Network Requirements
Multiservice Consolidation
Bandwidth Efficiency
Performance and QoS Guarantees
Carrier-Class Reliability
Ease of Operation and Management
Minimize Bandwidth Costs
Maximize Efficiency
Maximize Performance
Maximize Availability
Minimize Management and Maintenance

## Slide 9
Wide Area Network Costs
Capital costs (hardware): non-recurring
  Written off over three to five years
Bandwidth rental costs: recurring
  One to five year contracts
  Penalties for cancellation
  Highest month recurring expense
Transmission Costs 87.8%
Hardware Costs 8.0%
Software Costs 2.7%
Maintenance 1.5%
Source: Data Communications
Transmission Costs 87.8%
Hardware Costs 8.0%
Software Costs 2.7%
Maintenance 1.5%

## Slide 10
WAN Service Requirements
LAN interconnectivity
  Router and workgroup switches
Voice toll bypass
  PBX tie trunking and voice switching
Videoconferencing
  Room-to-room, desktop
Legacy data
  SNA, X.25, async data
TDM migration
  Transport option for aging TDM systems
Multiservice Networking
PBX
Videoconferencing
Legacy Data
WAN Router
Workgroup Switch
ISDN
FR/LL
VPN/LL
FR/LL
ATM/LL
Notes: 4
Within an enterprise backbone location, there are several applications that require connectivity to other locations. These include:
- LAN interconnectivity using routers and campus switches
- corporate voice interconnectivity for PBX tie trunking
- videoconferencing - either desktop or room-to-room
- legacy data connectivity for SNA, X.25, Async applications
In most current networks, these applications use a separate network infrastructure - either via public services (like VPNs for voice and data) or using private lines. Although some customers have consolidated these applications over a single infrastructure, in most cases they are using a circuit switched infrastructure - using time division multiplexed technology. This infrastructure consolidates the interfaces but still using separate bandwidth in the network.

## Slide 11
Wide Area Connectivity Requirements
Flexible trunking
  Sub-rate leased lines (64kbps to T1/E1)
  n x T1/E1 leased lines
  T3/E3 leased lines
  OC-3/STM-1 leased lines
  Public/private ATM services
Bandwidth efficiency
OC-3
STM-1
T3/E3
n x T1/E1
Public
ATM Network

## Slide 12
WAN Switching Technologies
Application
Presentation
Session
Transport
Network
Link
Physical
Link
Physical
Circuit Switching
Frame Switching
Cell Switching
CPE A
CPE B
WAN
Switch A
WAN
Switch B
Circuit Switching Time Division Multiplexing (TDM)
Frame Switching X.25/HDLC, SNA/SDLC
Cell Switching ATM
Frame/Cell
Application
Presentation
Session
Transport
Network
Link
Physical
Link
Physical

## Slide 13
Circuit Switching Overview
Time division multiplex bus
Available bandwidth is statically partitioned amongst the applications
Each application has access to the allocated bandwidth only; no single application can burst up to the entire bandwidth capacity
Example: available bandwidth = 24 DS0s
  Four channels for router data; eight for voice calls; six for video; six channels not allocated
Circuit switching delay: application frame size/ allocated bandwidth
Variability in delay: low
PBX
PBX

## Slide 14
Circuit Switching:Delay &Overhead
Example: Four-node TDM network using 2.048Mbps trunks. Two routers connected to TDM muxes at 256kbps. 4DS0s allocated between muxes for router traffic.
Delay for a 2048byte frame:
  Serialization delay between routers and TDM muxes:
    d1, d5 = (2048*8)bits/256kbps = 64msec
  TDM Switch Delay: ds
  Serialization delay between TDM muxes:
    d2, d3, d4 = (256*8)bits/256kbps = 64msec
  Total Delay:
    d1 + d2 + d3 + d4 + d5 + 4*ds = 5 * 64msec + 4*ds = 320msec + 4*ds
Overhead is insignificant or none
2.048Mbps
256kbps
Ten Voice
Channels
256kbps
Ten Voice
Channels
2.048Mbps
2.048Mbps
ds
d1
d2
ds
d3
ds
d4
ds
d5
PBX
PBX
PBX

## Slide 15
Circuit Switching - Pros & Cons
Predictable Performance
As bandwidth is allocated statically, all applications get consistent performance and predictable delay
Protocol-independent
End devices can be using any protocol over the wide area network
Inefficient Bandwidth Utilization
No dynamic allocation of bandwidth
No bursting capability - one application cannot use bandwidth allocated to the other even if that traffic is not present
Bandwidth Limited
Once all of the available bandwidth is allocated, additional bandwidth must be procured
Pros
Cons

## Slide 16
Frame Switching Overview
Either cells or frames within a switch but frames only at egress
Available bandwidth is dynamically allocated
Each application gets access to all available bandwidth; any application can burst up to the entire bandwidth capacity
Frame switching delay: increases with number of switches in path
Variability in delay: high
PBX
PBX

## Slide 17
Frame Switching: Delay
Example: Four-node Frame Switch network using 2.048Mbps trunks. Two routers connected to frame switches at 256kbps.
Delay for a 2048byte frame:
  Serialization delay between routers and frame switches:
    d1, d5 = (2048*8)bits/256kbps = 64msec
  Frame Switch Delay: ds
  Serialization delay between Frame Switches:
    d2, d3, d4 = (2048*8)bits/2.048Mbps = 8msec
  Total Delay:
    d1 + d2 + d3 + d4 + d5 + 4*ds = 2 * 64msec + + 3 * 8msec + 4*ds = 152msec + 4*ds
  Note: each switch must wait for entire frame before forwarding it to the next switch
2.048Mbps
256kbps
Ten Voice
Channels
256kbps
Ten Voice
Channels
2.048Mbps
2.048Mbps
ds
d1
d2
ds
d3
ds
d4
ds
d5
PBX
PBX

## Slide 18
Traffic Handling in Frame-Switched Network
Router Sends Frame to First Frame Switch
2048 bytes
2.048Mbps
256kbps
Ten Voice
Channels
256kbps
2.048Mbps
2.048Mbps
PBX
PBX
PBX
PBX

## Slide 19
Traffic Handling in Frame-Switched Network
First Frame Switch Waits for the Entire Frame,
Adds Header and Forwards to Next Switch
2048 bytes
2.048Mbps
256kbps
Ten Voice
Channels
256kbps
2.048Mbps
2.048Mbps
PBX
PBX
2048 bytes
2.048Mbps
256kbps
Ten Voice
Channels
256kbps
2.048Mbps
2.048Mbps
PBX
PBX
PBX
PBX
PBX
PBX

## Slide 20
Traffic Handling in Frame-Switched Network
Second Frame Switch Waits for the Entire Frame, and Forwards to Next Switch
2048 bytes
2.048Mbps
256kbps
Ten Voice
Channels
256kbps
2.048Mbps
2.048Mbps
PBX
PBX
2048 bytes
2.048Mbps
256kbps
Ten Voice
Channels
256kbps
2.048Mbps
2.048Mbps
PBX
PBX
PBX
PBX
PBX
PBX

## Slide 21
Traffic Handling in Frame-Switched Network
Next Frame Switch Waits for the Entire Frame, and Forwards to Next Switch
2048 bytes
2.048Mbps
256kbps
Ten Voice
Channels
256kbps
2.048Mbps
2.048Mbps
PBX
PBX
2048 bytes
2.048Mbps
256kbps
Ten Voice
Channels
256kbps
2.048Mbps
2.048Mbps
PBX
PBX
PBX
PBX
PBX
PBX

## Slide 22
Traffic Handling in Frame-Switched Network
Last Frame Switch Waits for the Entire Frame, Adds Header and Forwards to Next Switch
2048 bytes
2.048Mbps
256kbps
Ten Voice
Channels
256kbps
2.048Mbps
2.048Mbps
PBX
PBX
2048 bytes
2.048Mbps
256kbps
Ten Voice
Channels
256kbps
2.048Mbps
2.048Mbps
PBX
PBX
PBX
PBX
PBX
PBX

## Slide 23
Traffic Handling in Frame-Switched Network
Last Frame Switch Receives the Entire Frame and Forwards It to the Router
2048 bytes
2.048Mbps
256kbps
Ten Voice
Channels
256kbps
2.048Mbps
2.048Mbps
PBX
PBX
2048 bytes
2.048Mbps
256kbps
Ten Voice
Channels
256kbps
2.048Mbps
2.048Mbps
PBX
PBX
PBX
PBX
PBX
PBX

## Slide 24
Overhead in Frame Switch Networks
Router sends 2048byte frame to Frame Switch
Frame Switch adds header and sends the frame
Overhead for frame switch varies by vendor
If frame switch does fragmentation, overhead is applied to each frame
  Assume 256byte fragmentation and 20 byte overhead
  2048 bytes = 8 x 256byte frames
  Overhead = 20 x 8 = 160 bytes for 2048 byte frame = 7.8%

## Slide 25
Frame Switching - Pros & Cons
Dynamic allocation of bandwidth
Available bandwidth is allocated dynamically to any application that needs it
An application can use bandwidth allocated to another if that traffic is not present
Pros
Cons
Unable to guarantee performance
Frame Switches typically operate in FIFO (First In-First Out) mode, so one application can impact the performance of others.
High delay and variability in delay
Each switch has to receive an entire frame before forwarding it to the next switch; therefore transit delay increases with number of switches in the path
The FIFO mode of each switch causes a variability at each switch
Typically data only
As a result of high delay and variability in delay, frame switches are more suited for data-only environments that have little or no delay-sensitive applications

## Slide 26
Cell Switching Overview
Cells only within a switch and cells only at the egress of a switch
Available bandwidth is dynamically allocated
Each application gets access to all available bandwidth; any application can burst up to the entire bandwidth capacity
Cell switching delay: low delay
Variability in delay: low
PBX
PBX
PBX
PBX

## Slide 27
Cell Switching: Delay
Example: four-node cell switch network using 2.048Mbps trunks. Two routers connected to frame switches at 256kbps.
Delay for a 2048byte frame:
  Serialization delay between routers and cell switches:
    d1, d5 = (2048*8)bits/256kbps = 64msec
  Frame switch delay: ds
  Serialization delay between cell switches (cell size = 53bytes):
    d2, d3, d4 = (53*8)bits/2.048Mbps = 0.2msec
  Total delay:
    d1 + d2 + d3 + d4 + d5 + 4*ds = 2 * 64msec + + 3 * 0.2msec + 4*ds = 128.6msec + 4*ds
  Note: each switch does not wait for entire frame, it switches each cell as it is received
2.048Mbps
256kbps
Ten Voice
Channels
256kbps
Ten Voice
Channels
2.048Mbps
2.048Mbps
ds
d1
d2
ds
d3
ds
d4
ds
d5
PBX
PBX
PBX
PBX

## Slide 28
Traffic Handling in Cell-Switched Network
Router Sends Frame to First Cell Switch
2.048Mbps
256kbps
Ten Voice
Channels
256kbps
Ten Voice
Channels
2.048Mbps
2.048Mbps
PBX
PBX
2048 bytes
PBX
PBX

## Slide 29
Traffic Handling in Frame-Switched Network
2.048Mbps
256kbps
Ten Voice
Channels
256kbps
Ten Voice
Channels
2.048Mbps
2.048Mbps
PBX
PBX
2.048Mbps
256kbps
Ten Voice
Channels
256kbps
Ten Voice
Channels
2.048Mbps
2.048Mbps
PBX
PBX
2048 bytes
First Cell Switch Starts to Receive the Frame. As It Receives Enough Data to Fill up the Payload
of One Cell, It Adds Header and Forwards to Next
Switch.
PBX
PBX
PBX
PBX

## Slide 30
Traffic Handling in Frame-Switched Network
Second Cell Switch Receives the Cell and Switches it to the Next Switch
2.048Mbps
256kbps
Ten Voice
Channels
256kbps
Ten Voice
Channels
2.048Mbps
2.048Mbps
PBX
PBX
2.048Mbps
256kbps
Ten Voice
Channels
256kbps
Ten Voice
Channels
2.048Mbps
2.048Mbps
PBX
PBX
2048 bytes
PBX
PBX
PBX
PBX

## Slide 31
Traffic Handling in Frame-Switched Network
2.048Mbps
256kbps
Ten Voice
Channels
256kbps
Ten Voice
Channels
2.048Mbps
2.048Mbps
PBX
PBX
2.048Mbps
256kbps
Ten Voice
Channels
256kbps
Ten Voice
Channels
2.048Mbps
2.048Mbps
PBX
PBX
2048 bytes
Next Cell Switch Receives the Cells and Forwards
to Next Switch Till the Last Switch Where All Cells
Are Collected Until the Last Cell Is Received.
PBX
PBX
PBX
PBX

## Slide 32
Traffic Handling in Frame-Switched Network
Last Switch Assembles the Frame and Forwards to the Attached Router
2.048Mbps
256kbps
Ten Voice
Channels
256kbps
Ten Voice
Channels
2.048Mbps
2.048Mbps
PBX
PBX
2.048Mbps
256kbps
Ten Voice
Channels
256kbps
Ten Voice
Channels
2.048Mbps
2.048Mbps
PBX
PBX
2048 bytes
2048 bytes
PBX
PBX
PBX
PBX

## Slide 33
Traffic Handling in Frame-Switched Network
2.048Mbps
256kbps
Ten Voice
Channels
256kbps
Ten Voice
Channels
2.048Mbps
2.048Mbps
PBX
PBX
2.048Mbps
256kbps
Ten Voice
Channels
256kbps
Ten Voice
Channels
2.048Mbps
2.048Mbps
PBX
PBX
2048 bytes
2048 bytes
PBX
PBX
PBX
PBX

## Slide 34
Overhead in Cell-Switch Networks
Router sends 2048 byte frame to cell switch
Cell switch receives enough data to fill up one cell and sends the cell to the destination switch
Overhead for ATM cells is 5 bytes per cell (53 bytes)
Overhead calculation
  48 byte data payload in each cell and 5 byte overhead
  2048 bytes = 43 x 48 byte cells
  Overhead = 5 x 43 = 215 bytes for 2048 byte frame = 10.5%

## Slide 35
Cell Switching - Pros & Cons
Pros
Cons
Dynamic allocation of bandwidth
  Available bandwidth is allocated dynamically to any application that needs it
  One application can use bandwidth allocated to the other if that traffic is not present
Guaranteed performance
  Cell switches with efficient traffic and bandwidth management schemes can ensure that each application receives guaranteed performance
  Low delay and low variability in delay
  Using fixed length cells inside the network ensures that network transit delay is minimized and the variability in delay is also minimized
  Typically multiservice
  As a result of low delay, low variability in delay and the ability to guarantee performance, cell switches can support multiple services concurrently
Overhead
However the bandwidth efficiency and ability to provide low delay and low variability in delay in cell switching easily overcomes the small incremental overhead (refer to example)

## Slide 36
Frame/Cell Switching Overview
Either cells or frames within a switch and both frames and cells at egress of switch
Frame switching is used for data and cells are injected for delay-sensitive traffic
Available bandwidth is dynamically allocated
Each application gets access to all available bandwidth; any application can burst up to the entire bandwidth capacity
Frame/cell switching delay: increases with number of switches in path
Variability in delay: high
PBX
PBX
PBX
PBX

## Slide 37
Frame/Cell Switching - Pros & Cons
Cons
Dynamic allocation of bandwidth
  Available bandwidth is allocated dynamically to any application that needs it
  One application can use bandwidth allocated to the other if that traffic is not present
Multiple traffic types
  Cell injection process is used to ‘insert’ delay sensitive traffic (like voice) during the transfer of a data frame.
Proprietary
There are no standards for Frame/Cell switching.
Unable to guarantee performance
Cell injection causes frames to be partially transmitted and possibly buffered along the path. Frame-based traffic (data) suffers at the expense of cell traffic. Increased volumes of cell traffic can impact quality throughput and performance of frame-based traffic.
Bandwidth inefficiency
Increased cell traffic can cause frame traffic to be discarded in the network, thereby reducing the ‘quality throughput’ or ‘goodput’ of the network
High delay and variability in delay
Frame/cell switches operate as frame switches for data and have similar delay characteristics. Cell injection causes additional delays for frame traffic.
Pros