## Slide 1: Chapter 22
Addressing and Routing Design
Access
Access
Access
Backbone
What’s IP Subnet Masking all about?

## Slide 2: IP Networking
Addressing permits end station communications
Path choice depends upon location
Each location assigned a unique address

## Slide 3: IP Addressing
Network
Host
32 bits
8 Bits
8 Bits
8 Bits
8 Bits
131
108
122
204
.
.
.
Uses: Dotted decimal notation

## Slide 4: IP Address Format
N
H
H
H
Class A:
N
N
H
H
Class B:
N
N
N
H
Class C:
N - Network Number, NIC assigned
H - Host Number, Network administrator assigned

## Slide 5: IP Address Classes
Address
Class
A
B
C
Decimal
Value
1st Byte
1-126
128-191
192-223
High
Order
Bits
0
10
110
Class D: Multicast usage - 224.0.0.0
Class E: Experimental usage - 240.0.0.0

## Slide 6: Addressing Exercise
ADDRESS
CLASS
NETWORK
HOST
10.2.1.1
128.63.2.100
201.222.5.64
192.6.141.2
130.113.64.16
256.241.201.5

## Slide 7: Addressing Exercise
ADDRESS
CLASS
NETWORK
HOST
10.2.1.1
128.63.2.100
201.222.5.64
192.6.141.2
130.113.64.16
256.241.201.5
A
B
C
C
B
Invalid
10.0.0.0
128.63.0.0
201.222.5.0
192.6.141.0
130.113.0.0
2.1.1
2.100
64
2
64.16

## Slide 8: Host Addressing
15.180.30.118
131.108.200.1
131.108.3.10
131.108.12.12
131.108.2.1
15.6.24.2
15.1.1.1
15.250.8.11
Networks are identified by addresses of the form X.X.X.0
Host address of all ones is an IP broadcast
Each interface must have a nonzero host number
Network - 131.108.0.0
Host - 12.12
Network - 15.0.0.0
Host - 180.30.118

## Slide 9: Addressing without Subnets
World sees Network 131.108.0.0 as 1 flat network
No knowledge of internal organization
Inefficient usage of address space
131.108.0.0

## Slide 10: No Subnet Masking
Network Bits Host Bits
131.108.2.160 10000011 01101100 00000010 10100000
255.255.0.0 11111111 11111111 00000000 00000000
10000011 01101100 00000000 00000000
131 108 0 0
Default Case -- No Subnets Used

## Slide 11: Subnet Addressing
131.108.3.150
131.108.2.200
131.108.2.2
131.108.2.160
131.108.2.1
131.108.3.1
131.108.3.5
131.108.3.100
Subnet is an extension of the network number
Subnets divides large network in smaller subnetworks
Routing decisions based on network and subnetwork
Network - 131.108.0.0
Subnet - 131.108.2.0
Host - 160
Network - 131.108.0.0
Subnet - 131.108.3.0
Host - 150

## Slide 12: Addressing with Subnets
World see Network 131.108.0.0 as 3 subnetworks
Provides knowledge of internal organization
More efficient usage of address space
Subnetting causes loss of address space
131.108.1.0
131.108.2.0
131.108.3.0

## Slide 13: Subnet Masking
131
108
0
0
Class B
IP Address
255
255
0
0
Class B
Default Mask
255
255
255
0
Class B with
8-Bit Subnet
Mask
Use host bits starting with high
order bit position

## Slide 14: Subnet Masking
Network administrator decides size of subnet
Subnet masks identify which host bits are used to specify the subnetwork
Subnet mask bit layout
  Binary 1 identifies network bit
  Binary 1 identifies subnet bit
  Binary 0 identifies host bit

## Slide 15: Subnet Masking
Network Bits Host Bits
131.108.2.160 10000011 01101100 00000010 10100000
255.255.255.0 11111111 11111111 11111111 00000000
10000011 01101100 00000010 00000000
131 108 2 0
Subnet Used to Extend Network Number
Reduces Range of Available Host Numbers

## Slide 16: Subnetting Exercise
ADDRESS
CLASS
SUBNET MASK
SUBNET
BITS
131.108.2.10
15.6.24.20
168.124.36.12
128.16.32.13
255.255.255.0
255.255.0.0
255.255.255.0
153.50.6.27
201.222.10.60
255.255.255.252
255.255.255.128
255.255.255.248
B
A
B
B
B
C

## Slide 17: Subnetting Exercise
ADDRESS
CLASS
SUBNET MASK
SUBNET
BITS
131.108.2.10
15.6.24.20
168.124.36.12
128.16.32.13
255.255.255.0
255.255.0.0
255.255.255.0
153.50.6.27
201.222.10.60
255.255.255.252
255.255.255.128
255.255.255.248
B
A
B
B
B
C
131.108.2.0
8
15.6.0.0
8
168.124.36.0
8
128.16.32.12
14
153.50.6.0
9
201.222.10.48
5