## Slide 1: ISDN Layers
Physical Layer
Data Link Layer

## Slide 2: Physical Layer
OSI Layer 1 Functions
  Encoding of digital data
  Full duplex transmission
    B Channel
    D Channel
  Multiplexing of channels for basic or primary service
  D Channel contention access
  Terminal identification

## Slide 3: Physical Layer
Methods of Line Coding
  Nonreturn to Zero
    NRZL
    NRZI, Used by IBM
  Multilevel Binary
    Bipolar Alternate Mark Inversion (AMI)
    Pseudoternary
      Binary 0 -- alternating positive/negative
      Binary 1 -- absence of line signal

## Slide 4: Examples of Line Coding
0
1
0
0
1
1
0
NRZ-L
AMI

## Slide 5: Physical Layer
Methods of Line Coding
  Scrambling Techniques
    No dc component
    No long sequences of zero-level line signals
    No reduction in data rate
    Provides error-detection
  Bit Encoding Using Scrambling
    Binary with 8-zeros substitution (B8ZS)
    High density bipolar-3 zeros (HDB3)

## Slide 6: Physical Layer
Basic User-Network Interface
  Line coding
  Physical connector
  Framing and multiplexing
  Contention resolution
  Multidrop connections

## Slide 7: Physical Layer
Line Coding
  S and T reference points
  Full duplex digital data transmission
  4 wire circuit
  Electrical specification
    Pseudoternary coding
    Positive/negative voltage pulses: 750 mV 10%
    Data rate 144 Kbps
    Transmission rate 192 Kbps

## Slide 8: Physical Layer
Basic Access Physical Connector
  Physical connection between TE and NT at S or T reference points
  ISO 8887 specifies 8 pin physical connector
  In US use RJ-45

## Slide 9: Physical Layer
Framing and Multiplexing
  144 Kbps data multiplexed on 192 Kbps transmission
  Repetitive, fixed length frames
    Each frame 48 bits long
    Frame repeats every 250
    Frame uses pseudoternary bit coding
  Bits
    16 bits B1 channel, 16 bits B2 channel
    4 bits D channel
    12 bits frame management

## Slide 10: Physical Layer

## Slide 11: Physical Layer
NT1
LT
TE11
TE12
TE13
TE14
TE15
CONTENTION
NO CONTENTION
FULL DUPLEX
(any way possible)
FULL DUPLEX
(192 Kbps)
2 wire circuit
2 wire techniques:
Time Compression Multiplexing
Echo Cancellation

## Slide 12: Data Link Layer
Given the following data sequence: ...111111111111011111101111110...
Using standard bit stuffing rule: insert 0 after detecting 11111
The transmitted bit pattern: 11111011111011011111010101111101010

## Slide 13: Data Link Layer
What is effect of using NRZL bit encoding?
1 = 0 or -V (low level), 0 = +V (high level)
The transmitted bit string: 11111011111011011111010101111101010
Inserted 0’s

## Slide 14: Data Link Layer
What is effect of using pseudoternary bit encoding?
1 = 0 (no voltage), 0 = alternating +V, -V
The transmitted bit string: 11111011111011011111010101111101010
Inserted 0’s

## Slide 15: Data Link Layer
Bit Synchronous Protocol Legacy
IBM SDLC
ANSI ADCCP
ISO HDLC
ITU-T LAP,
LAPB, LAPD,
LAPF, etc.
Vendor
Adaptations
Standards
Adaptations

## Slide 16: Data Link Layer
Bit synchronous frame format
Bit synchronous frame types
  Information
  Supervisory
  Un-numbered
FLAG
ADDR
CNTR
INFO
FCS
FLAG
FLAG 8 bits
ADDR 8*n bits (n = 1, 6)
CNTR 8*m bits (m =1, 2)
INFO 8*r bits (r = 1, R; R configurable)
FCS 8*x bits (x = 1, 4)
FLAG 8 bits

## Slide 17: Data Link Layer
LAPD frame format
LAPD frame types
  Information: 16 bit control field
  Supervisory: 16 bit control field
  Un-numbered: 8 bit control field
FLAG
ADDR
CNTR
INFO
FCS
FLAG
FLAG 8 bits
ADDR 16 bits
CNTR see below
INFO 8*r bits (r = 1, R; R configurable)
FCS 16 bits
FLAG 8 bits

## Slide 18: Data Link Layer
LAPD address field format
FLAG
ADDR
CNTR
INFO
FCS
FLAG
X
0
1
SAPI
TEI
SAPI Service Access Point Identifier
TEI Terminal End Point Identifier
X Command/Response Bit

## Slide 19: Data Link Layer

## Slide 20: Data Link Layer

## Slide 21: Data Link Layer
Terminal Adaption
  Mapping non-ISDN device into Interface
Functions Provided
  Rate adaption
  Signal conversion
  X.25 conversion
  Physical interface conversion
  Digitization

## Slide 22: Data Link Layer
Bearer Channel Data Link Control
  Uses I.465/V.120
Data Streams Supported
  Asynchronous protocol sensitive
  HDLC synchronous protocol sensitive
  Bit transparent

## Slide 23: Data Link Layer
V.120 Provides
  Operation over circuit mode connections
  Operation over frame mode connections
  Uses demand connection establishment
  Uses semipermanent connection establishment
  Supports access channel types
    Circuit-mode: B, H0, H10, or H11
    Frame-mode: B, H0, H10, H11, or D