## Slide 1: ISDN Basics
Overview and History
Interfaces
Reference Points
Features and Functions

## Slide 2: Overview
Digital Switching
Digital Transmission
Voice Support
  Pulse Code Modulation
  Time Division Multiplexing
IDN is backbone for ISDN

## Slide 3: Overview
Principles of ISDN
  Support voice/nonvoice
  Support standardized facilities
  Support switched/nonswitched
  Reliance on 64 Kbps rates
  Intelligence in network
  Layered architecture
  Variety of configurations

## Slide 4: Overview
Evolution of ISDN
  Based on telephone IDNs
  Long term transition
  Use existing networks
  Interim user-network arrangements
  Connections at non 64Kbps rates

## Slide 5: Connections
IDN

## Slide 6: Overview
Objectives
  Standardization
  Transparency
  Separation of competitive functions
  Leased and switched services
  Cost-related Tariffs
  Smooth migration
  Multiplexed Support

## Slide 7: Overview
Benefits
  Customers
    Cost savings
    Flexibility (Tailored service)
  Network providers
  Manufacturers
  Enhanced service providers
  Intelligent Network

## Slide 8: Overview
Services
  Important Applications
    Facsimile -- graphics, handwritten, printed messages
    Teletex -- prepare, edit, transmit and print messages
    Videotex -- interactive information retrieval service
  Service Catagories
    Voice, Digital data, Text, and Image

## Slide 9: History
Historical Background
  Special Study Group D (1969 - 1976)
    1969 - 1972 Planning for digital systems
    1973 - 1976 Planning for digital system, integrated services
  Study Group XVIII (1977 - 1992)
    1977 - 1980 Overall aspects of ISDN
      G.705 issued 1980
    1981 - 1984 General network aspects of ISDN
      I series first issued 1984

## Slide 10: History
Historical Background
  Study Group XVIII (1977 - 1992)
    1985 - 1988 General question of ISDN
      I series reissued in 1988
    1989 - 1992 General aspects of ISDN
      I series revisions begin in 1992
  1993 Formation of ITU-T
  15 study groups develop recommendations

## Slide 11: History
I-Series Recommendations
  Characterized 3 main areas
    Standardization of services
    Standardization of user-network interfaces
    Standardization of ISDN capabilities

## Slide 12: History
I-Series Recommendations
  I.1XX -- General Concepts
  I.2XX -- Service Capabilites
  I.3XX -- Network Aspects
  I.4XX -- User-Network Interfaces
  I.5XX -- Internetwork Interfaces
  I.6XX -- Maintenance Principles

## Slide 13: Recommendation I.110
Sections
  General
  Service Capabilities
  Overall Network Aspects and Functions
  User-Network Interface
  Internetwork Interfaces
  Maintenance Principles
ISDN
Table of Contents

## Slide 14: Recommendation I.112
Created by SG XVIII
  Provides plain English definition of terms
  Basis for translation into the 3 official languages
ISDN
Dictionary

## Slide 15: Recommendation I.111
SG XI - Switching Systems
SG XV - Transmission Systems
SG III - Tariff Principles
SG II - Telephone Operations
SG VII - Data Networks
SG IV - Maintenance
SG XVIII - “The ISDN Orchestra Conductor”

## Slide 16: ISDN’s Ten Commandments
Provides a wide range of voice and non-voice services
Provides a limited set of interfaces
Provides a limited set of connection types
Supports circuit-switched service
Supports packet-switched service
Supports non-switched service
Compatible with 64 Kbps rate
Offers intelligence to provide service features
Uses layered protocols
Offers flexibility to suit national needs
ISDN
The evolutionary path:
1. Start with IDN
2. Interwork with dedicated networks
3. Incorporate functions of dedicated networks

## Slide 17: Architecture

## Slide 18: Architecture
ISDN Services
  Basic service, 2B + D
    144 Kbps data and control
    192 Kbps transmitted signal
  Primary service, 23B + D
    1536 Kbps data and control
    1544 Kbps transmitted signal

## Slide 19: Interfaces and Functions
Channel Types
  B Channel: 64 Kbps
  D Channel: 16 or 64 Kbps
  H Channel: 384 (H0), 1536 (H11), 1920 (H12) Kbps
Connections over B Channel
  Circuit-switched
  Packet-switched
  Semipermanent

## Slide 20: Interfaces and Functions
Connections over D Channel
  Call establishment
  Packet-switching
  Low speed telemetry ( < 100 bps )
Connections over H Channel
  High bit rate user access
  User defined TDM schemes

## Slide 21: Interfaces and Functions
Basic Access
  2 B Channels, 64 Kbps/channel
  1 D Channel, 16 Kbps
  Total Data Rate: 144 Kbps
  Overhead and Framing: 48 Kbps
  Measurable Link Speed: 192 Kbps
  Available Options: B + D and D

## Slide 22: Interfaces and Functions
Primary Access
  North America, Japan
    23 B Channels, 64 Kbps/channel
    1 D Channel, 64 Kbps
    Total Data Capability: 1536 Kbps
    Overhead and Framing: 8 Kbps
    Measurable Link Speed: 1544 Kbps
    Available Options: 24 B; nB + D, n = 1, 23

## Slide 23: Interfaces and Functions
Primary Access
  Rest of World
    30 B Channels, 64 Kbps/channel
    1 D Channel, 64 Kbps
    Total Data Capacity: 1984 Kbps
    Overhead and Framing: 64 Kbps
    Measurable Link Speed: 2048 Kbps
    Available Options: 31 B; nB + D, n = 1, 30

## Slide 24: Interfaces and Functions
Primary Access
  H Channel Structures
    3 H0 + D; 4 H0; 1 H11 for 1544 Kbps
    5 H0 + D; 1 H12 + D for 2048 Kbps
  H and B Channel Structures
    3 H0 + 5 B + D; 3 H0 + 6 B for 1544 Kbps

## Slide 25: User-Network Interfaces
ISDN Reference Points
U
T
S
NT1
NT2
TE1
3
2
1
U - Defined by ANSI only for US

## Slide 26: User-Network Interfaces
ISDN Reference Points
T
S
R
NT2
TA
TE2
5
4
2
U - Defined by ANSI only for US

## Slide 27: Interfaces and Functions
Reference Points
  U -- Full duplex data signal on subscriber line
    Not defined by ITU-T in I.411, US only
  T -- Minimal ISDN network termination on user premise
    Separates network provider equipment from user equipment

## Slide 28: Interfaces and Functions
Reference Points (Continued)
  S -- Individual ISDN terminals on user premise
    Separates network communication functions from user terminals
  R -- Non-Interface on user premise
    Connects pre-ISDN equipment to ISDN adapter
    Usually V or X series interface

## Slide 29: Interfaces and Functions
Functional Groupings
  NT1 -- Functions belonging to OSI layer 1
    Physical and electrical termination of the ISDN on the user premise
  NT2 -- intelligent device that may include OSI layer 1 - 3.
    Switching and concentrating functions, ie., PBX

## Slide 30: Interfaces and Functions
Functional Groupings (Continued)
  TE1 -- User device with Interface
  TE2 -- User device with non-Interface
    X or V series ITU-T interfaces
  TA -- User device
    Converts non-Interface to Interface

## Slide 31: Interfaces and Functions
Service Support
  Bearer service: access point 1 and/or access point 2
  Teleservice: access point 3 -- ISDN compatible, access point 5 -- non-ISDN compatible
  Other service: access point 4 -- X or V series compatible

## Slide 32: Interfaces and Functions
Modified OSI Architecture
  Control Protocol Block -- Supports ISDN signaling
  User Protocol Block -- Supports transparent transfer user information
  Plane Management Function -- Network management functions
    Controls parameters & operation of remote system
    Collects local configuration & operational information

## Slide 33: Interfaces and Functions
ISDN End-to-End Communication Services
  Circuit-switched calls over B or H Channel
  Semipermanent connections over B or H Channel
  Packet-switched calls over B or H Channels
  Packet-switched calls over D Channel
  Frame relay calls over B or H Channel
  Frame relay calls over D Channel

## Slide 34: Interfaces and Functions
Addressing Requirements
  Easily understood and usable by subscriber
  Compatible with existing & planned switching equipment
  Allow for expansion of subscriber population
  Facilitate interworking with existing public network numbering schemes

## Slide 35: Interfaces and Functions
Addressing Principles
  Enhancement of E.164 -- country code identifies countries in the ISDN numbering plan
  Independent of nature of service
  Independent of performance characteristics
  Sequence of decimal digits
  Sufficient for interworking between ISDNs

## Slide 36: Interfaces and Functions
ISDN Address Structure
  ISDN number -- a number that relates to the ISDN network and ISDN numbering plan. Permits ISDN network to route a call.
  ISDN address -- the ISDN number and any additional manditory or optional addressing information. The additional information is not required to route the call through the ISDN network.

## Slide 37: Interfaces and Functions
ISDN Address Example
    PBX National Number 617-543-7000
    Local telephone extension 678
    Remote caller dials 617-543-7000-678
    ISDN uses first 10 digits, PBX uses 678
    Remote caller dials 617-543-7678 (Direct Dial-In)
    Block 543-7XXX must be assigned to PBX

## Slide 38: Customer Usage
Problem:
An ISDN customer has offices at several locations.
Each location is served by 2 1.544 Mbps digital circuits.
One circuit provides circuit-switched access to ISDN.
The second circuit provides a semi-permanent connection
to another office. The on-premise equipment consists
of a digital PBX and a host computer system with X.25
capability. The user requires:
a. Telephone service
b. Private packet-switched data service
c. Periodic inter-office video conferencing at
1.544 Mbps
How might the user allocate the on site capacity to meet
his requirements?

## Slide 39: Customer Usage
Solution:
Since the video conferencing is periodic, the 1.544 Mbps
line should be available on a reservation basis only.
When not required for video conferencing, the leased line
semi-permanent connection is available to support the
private packet data service. When in use, the leased line
is dedicated to video conferencing and the private packet
data service uses the ISDN line along with any inter-office
telephone service.
Intra-office telephone service is provided by each local
PBX.