## Slide 1
X.25 Interface
Multiple Virtual Circuits
Over Single Physical Circuit

## Slide 2
X.25 and OSI
Application
Presentation
Session
Transport
X.25 PLP
LAPB
EIA-232, V.35
(Network)
(Data Link)
(Physical)

## Slide 3
What X.25 Is Not
A packet network definition
X.25 does not
  Provide end-to-end communications
  Provide for the use of multi-point circuits
  Provide data format compatibility
  Ensure compatability of service subsets

## Slide 4
What X.25 Is
A recommended packet interface for data networks
The interface provides
  3 Level interface definition
    A physical connection interface
    A point-to-point data link procedure
    A multiplexing packet procedure
  A set of enhancing supplementary services

## Slide 5
Packet Switching
S
S
U1
U3
N2
N4
N5
N6
U2
U4
N1
N3
Using virtual circuits
X.25
X.25

## Slide 6
Packet Switching
S
S
U1
U3
N2
N4
N5
N6
U2
U4
N1
N3
Using datagrams
X.25
X.25

## Slide 7
Traffic Characteristics
Bursty
  Transmission duration < 5 seconds
Delay-insensitive
Traffic predominantly in 1 direction
  Low volume to host
  High volume to terminal

## Slide 8
Packet Flow
2
5
1
3
6
4
User A
User B
P1
P2
P3
P4
P1
P4
P3
P1
P4
P3
P1
P2
P3
P4
P2
P2
P3
P3
Message
Message

## Slide 9
Acknowledgment Flow
2
5
1
3
6
4
User A
User B
A1
A2
A3
A4
A1
A2
A3
A4
A4
A1
A1
A4
A3
A3
A2
A2
A3
A3
ACKs
ACKs

## Slide 10
Errors that Affect Traffic Flow
Errored packets
  Transmission errors
Lost packets
Duplicate packets
Sequence errors

## Slide 11
Packet Switching
X.25 Interface
  Physical level
    EIA 232, V.35 -- Leased line service
  Link level
    LAPB -- Bit synchronous transmission
  Packet level
    Permanent virtual circuit
    Switched virtual call
    Multiplexing -- Logical channel
    Flow control, error control

## Slide 12
Data Link Layer
Bit Synchronous Protocol Legacy
IBM SDLC
ANSI ADCCP
ISO HDLC
ITU-T LAP,
LAPB, LAPD,
LAPF, etc.
Vendor
Adaptations
Standards
Adaptations

## Slide 13
Data Link Layer
Bit synchronous frame format
Bit synchronous frame types
  Information
  Supervisory
  Un-numbered
FLAG
ADDR
CNTR
INFO
FCS
FLAG
FLAG 8 bits
ADDR 8*n bits (n = 1, 6)
CNTR 8*m bits (m =1, 2)
INFO 8*r bits (r = 1, R; R configurable)
FCS 8*x bits (x = 1, 4)
FLAG 8 bits

## Slide 14
Data Link Layer
LAPB frame format
LAPB frame types
  Information: Command only
  Supervisory: Command and Response
  Un-numbered: Command or Response
FLAG
ADDR
CNTR
INFO
FCS
FLAG
FLAG 8 bits
ADDR 8 bits
CNTR 8 bits modulo 8; 16 bits modulo 128
INFO 8*r bits (r = 1, R; R configurable)
FCS 16 bits
FLAG 8 bits

## Slide 15
Data Link Layer
LAPB address field format
FLAG
ADDR
CNTR
INFO
FCS
FLAG
X
1
X = 1 DTE Address (Subscriber)
= 0 DCE Address (Network)
0
0
0
0
0
0

## Slide 16
X.25 Packet and Frame Formats

## Slide 17
X.25 PLP Format
Q
D
0
1
LCGN
LCN
Packet Type
LCGN: 0 - 15
LCN: 0 - 255
8
1
1
2
3
N

## Slide 18
Logical Channel Assignment
0
LIC
LTC
LOC
HOC
1
HTC
HIC
Permanent Virtual Circuits
One-way Incoming Virtual Calls
One-way Outgoing Virtual Calls
Two-way Virtual Calls
DCE
Assigned
DTE
Assigned

## Slide 19
Companion ITU-T Standards
X.121 addressing formats
X.96 call progress signals
X.1 user access classes
X.2 user facilities
X.32 dial-up access procedures
X.3 Packet assembly and disassembly
X.28 PAD interface protocol
X.29 PAD messaging protocol

## Slide 20
User Network Interface
l
l
l
l
AT&T
✿
PAD
DCE
PAD
DCE
DCE
X.32, X.25
X.28
X.28
X.25
X.25
X.25

## Slide 21
Optional User Facilities
Closed User Groups
Negotiation
  Window Size
  Packet Size
  Throughput Class
Reverse Charging
RPOA Selection
Fast Select

## Slide 22
“Standard” PAD
PAD - Packet Assembler/Disassembler
  Converts ASCII start/stop character strings to X.25 Data packets
  Permits complete user management of the virtual circuit
  Based on ITU-T Standards X.3, X.28 and X.29

## Slide 23
ITU-T Recommendation X.3
Defines the PAD services
  22 multi-valued parameters which are used to manage the connected start/stop device
  Data input management
  Error management
  Print management
  Connection management

## Slide 24
ITU-T Recommendation X.28
Defines the User to PAD interface
Commands and Responses
  Defined by ASCII character strings
  9 user command signals
    STAT, CLR, PAR?, SET?, PROF, RESET, INT, SET, SELECTION
  12 PAD service signals (responses)
    RESET, CLR, COM, PAD Id, ERROR, XXX, ENGAGED, FREE, PAR, PAD Prompt, Format, Incoming Call

## Slide 25
ITU-T Recommendation X.29
Defines the PAD to PAD message protocol
  8 messages
    SET, READ, SET & READ, ERROR
    PARAMETER INDICATION
    INVITATION to CLEAR
    INDICATION of BREAK
    RESELECTION
  Transported in Qualified X.25 Data Packets

## Slide 26
X.121 Addressing
Prefix
  1 digit optional
Data Network Identification Code
  4 digits uniquely identifies network
National Terminal Number
  1 - 8 digits (routes call to user location)
  0 - 2 digit subaddress (not used for routing)

## Slide 27
Addressing Examples
SprintNet
  No prefix
  DNIC = 3110
  National Terminal Number
    Area Code - 3 digits
    Host Address - 5 digits
    Subaddress - 2 digits, optional
  Example: 31108030004535

## Slide 28
Addressing Examples
Bell South Pulse Link
  Prefix = 1
  DNIC = 3142 (not used intranetwork)
  National Terminal Number
    Area Code - 3 digits
    Exchange - 3 digits
    Host Number - 2 digits
    Subaddress - 2 digits, optional
  Example 18032528105

## Slide 29
Advantages of X.25
Format, code, speed conversions
Secure transmission schemes
Fault tolerant technology
Packetized messages
Leased line and dial access
Network functions transparent to user
Synchronous and asynchronous interfaces
Better circuit utilization
International connectivity

## Slide 30
Disadvantages of X.25
Low access speeds
Variable delay potential
High overhead

## Slide 31
X.75 Internetworking Protocol
DCE
STE
DCE
STE
l
l
l
l
X.75
STE - Signaling Terminal Exchange
- X.121 Address Translation
- Facilities Translation
- Logical Channel Mapping