## Slide 1
Classless and Subnet Address Extensions
(Chapter 10)

## Slide 2: IP Address Review
In original IP addressing scheme, each physical network assigned unique network address
Each host on network has network address as prefix (netid) of host’s individual address
TCP/IP accommodates diverse network sizes by having three classes of primary addresses
Class | Lowest Address | Highest Address
A | 1.0.0.0 | 126.0.0.0
B | 128.1.0.0 | 191.255.0.0
C | 192.0.1.0 | 223.255.255.0

## Slide 3: Minimizing Network Numbers
Running Out of ADdress Space (ROADS) problem
Growth of Internet has led to address space (especially popular class B) being exhausted
Techniques to minimize address use
  Proxy ARP
  Subnet Addressing
  Classless Addressing (Supernetting)

## Slide 4: Proxy ARP
Two physical networks share single IP network address
Proxy ARP router hides host’s hardware address on one network from another network
R
H1
H2
Hidden Network
H3
Main Network
Router running proxy ARP
H4
H5

## Slide 5: Subnetting
Partition local portion of IP address into physical subnet part and host part.
Internet Part | Local Part
Internet Part | Physical Network | Host Identifier
Subnet Prefix

## Slide 6: Subnetting Example
Rest of
the
Internet
R
All traffic
to 128.10.0.0
Network 128.10.1.0
Network 128.10.2.0
128.10.1.2
128.10.2.8
128.10.2.7
128.10.1.1
Hierarchical addressing results in hierarchical routing

## Slide 7: Subnet Masks
Site using subnet addressing chooses 32-bit subnet mask for each network
Contiguous bits in subnet mask are set to
  1 if corresponding bits in IP address represent subnet prefix
  0 if corresponding bits in IP address represent host identifier
Subnet Mask 11111111 11111111 11111111 00000000 255.255.255.0
IP Address 10000010 10100110 01100001 00011001
Binary
Decimal
130.166.97.25

## Slide 8: Mask Assignments
Fixed-length subnet masks
  Organization uses same mask on all networks
Variable-length subnet masks
  Organization chooses size for each physical network
  Mask assigned on per-network basis

## Slide 9: Fixed-Length Subnet Masks
All networks assigned same mask
Advantages
  Uniformity
  Ease of debugging / maintenance
Disadvantages
  Number of nets fixed for entire organization
  Size of physical nets fixed for entire organization

## Slide 10: Possible Fixed-Length Subnets
Subnet Bits* | Max. # of Subnets* | Max # of Hosts per Subnet*
2 | 2 | 16382
3 | 6 | 8190
4 | 14 | 4094
5 | 30 | 2046
6 | 62 | 1022
7 | 126 | 510
8 | 254 | 254
9 | 510 | 126
10 | 1022 | 62
11 | 2046 | 30
12 | 4094 | 14
13 | 8190 | 6
14 | 16382 | 2
* Given a Class B network address

## Slide 11: Variable-Length Subnet Masks
Mask assigned on per-network basis
Advantages
  Flexibility to mix large and small nets
  More complete use of address space
Disadvantages
  Difficult to assign / administer
  Potential address ambiguity

## Slide 12: Address Ambiguity
Network address 128.10.0.0
Subnet 1 (mask = 24 bits, max hosts = 254)
  mask: 11111111 11111111 11111111 00000000
  prefix: 10000000 00001010 00000001 00000000
  broadcast: 10000000 00001010 00000001 11111111
Subnet 2 (mask = 26 bits, max hosts = 62)
  mask: 11111111 11111111 11111111 11000000
  prefix: 10000000 00001010 00000001 11000000
  broadcast: 10000000 00001010 00000001 11111111

## Slide 13: Default Subnet Masks
Each IP network class has natural mask
  Class A natural mask 255.0.0.0
  Class B natural mask 255.255.0.0
  Class C natural mask 255.255.255.0
Default mask of 255.255.0.0 is applied to 10.0.0.0 network address
  Allows 254 subnetworks ranging from 10.1.0.0 to 10.254.0.0

## Slide 14: Subnet Mask Representation
Binary: 11111111 11111111 11111111 00000000
Dotted decimal: 255.255.255.0
3-tuple
  { network #, subnet #, host # }
  -1 means “all ones”
  e.g., 255.255.255.0 can be written {-1, -1, 0}

## Slide 15: Conventional Routing (w/o subnets)
Network Address | Next Hop Address
64.0.0.0 | 137.145.0.9
130.166.0.0 | 151.20.0.5
195.62.155.0 | 202.74.5.11
… | …
Sample Entries of
Conventional Routing Table
R
Network
137.145.0.0
Network 151.20.0.0
Network 202.74.5.0
151.20.0.5
202.74.5.11
137.145.0.9

## Slide 16: Subnet Routing
Given destination address:
  130.166.105.83 10000010 10100110 01101001 01010011
  perform bitwise Boolean AND
  255.255.255.0 11111111 11111111 11111111 00000000
  Result:
  130.166.105.0 10000010 10100110 01101001 00000000
Subnet Mask | Network Address | Next Hop Address
255.255.0.0 | 64.106.0.0 | 137.145.0.9
255.255.255.0 | 130.166.105.0 | 151.20.0.5
255.255.255.240 | 195.62.155.32 | 202.74.5.11
… | … | …
Sample Entries of
Routing Table
with Subnetting

## Slide 17: Subnet Routing: Another Example
Given destination address:
  195.62.155.44 11000011 00111110 10011011 00101100
  perform bitwise Boolean AND
  255.255.255.240 11111111 11111111 11111111 11110000
  Result:
  195.62.155.32 11000011 00111110 10011011 00100000
Subnet Mask | Network Address | Next Hop Address
255.255.0.0 | 64.106.0.0 | 137.145.0.9
255.255.255.0 | 130.166.105.0 | 151.20.0.5
255.255.255.240 | 195.62.155.32 | 202.74.5.11
… | … | …
Sample Entries of
Routing Table
with Subnetting

## Slide 18: Using Subnet Masks for Routing
Host-specific routes
  (20.0.0.3, 30.0.0.7)
  (255.255.255.255 , 20.0.0.3 , 30.0.0.7)
Default routes
  (default, 40.0.0.8)
  (0.0.0.0 , 0.0.0.0 , 40.0.0.8)
Standard, non-subnet class B network
  (128.10.0.0, 10.0.0.3)
  (255.255.0.0 , 128.10.0.0 , 10.0.0.3)

## Slide 19: Broadcasting to Subnets
Broadcast to all hosts on network 128.10.0.0
  Broadcast address: 128.10.255.255
If network 128.10.0.0 has subnets
  Routers that interconnect subnets must propagate datagram to all physical networks
  But routers must take care not to route datagrams in loops (reverse path forwarding)
Broadcast to specific subnet, within subnetted networks
  Subnet broadcast address: {network, subnet, -1}

## Slide 20: Reverse Path Forwarding
datagram will be forwarded
datagram will not be forwarded
R1
R2
R3
R4
R5
R6
R7
S: source
if (datagram received on incoming link on shortest path back to sender)
then forward datagram onto all outgoing links
else ignore datagram

## Slide 21: Classless (Supernet) Addressing
Extend variable-length subnet technology to prefixes
Merge 256 class C numbers into single prefix equivalent to class B
Block of contiguous addresses represented by:
  (network address, count)
(192.5.48.0, 3) specifies 3 network addresses: 192.5.48.0, 192.5.49.0, 192.5.50.0

## Slide 22: Routing to Supernets
Collapse block of contiguous class C addresses into single routing table entry:
  (network address, count, next hop)
Example:
  (192.5.48.0 , 3, 10.0.0.2)
  Route datagrams bound for networks 192.5.48.0, 192.5.49.0, 192.5.50.0 to next hop 10.0.0.2

## Slide 23: Classless Inter-Domain Routing (CIDR)
Represents block of contiguous IP addresses as pair
  (lowest address in block, 32-bit mask)
CIDR uses slash notation to represent mask
  e.g., Mask CIDR Notation
  11111111 11111111 11111000 00000000 /21
Notation 128.211.168.0 /21 means block of 2048 addresses
IP Address | Dotted Decimal | Binary Equivalent
Lowest | 128.211.168.0 | 10000000 11010011 10101000 00000000
Highest | 128.211.175.255 | 10000000 11010011 10101111 11111111
IP prefix
mask length