## Slide 1: Transport Layer Protocols Ch. 11: Protocol Layering Ch. 12: User Datagram Protocol (UDP) Ch. 13: Transmission Control Protocol (TCP)

## Slide 2: Protocol Layering (Chapter 11)

## Slide 3: TCP/IP Internet Layering Model
Conceptual layer
Objects passed
between layers
Major functions
Messages or
streams
Transport protocol
packets
IP datagrams
Network specific
frames
Users invoke application,
interact with transport layer protocols
Reliability, flow control,
Connection with multiple applications
Routing & error handling
ICMP messages
Media Access Control
Link-level error control
APPLICATION
TRANSPORT
INTERNET
NETWORK
INTERFACE
HARDWARE

## Slide 4: The Layering Principle
Internet
network interface
HOST A
ROUTER R
HOST B
application
transport
Internet
network interface
identical
message
identical
packet
Identical
datagram
Identical
frames
physical network 1
physical network 2
application
transport
Internet
network interface
Identical
datagram
Identical
frames

## Slide 5: Building an Internet
IP - Connectionless Datagram Delivery (Unreliable)
ARP
RARP
Network Hardware Interface
UDP
TCP
Connectionless
Transport
(Unreliable)
Connection oriented
Transport
(Reliable)
Applications
(email, FTP, web, etc.)
Notes: 1

## Slide 6: User Datagram Protocol (UDP) (Chapter 12)

## Slide 7: User Datagram Protocol (UDP)
Primary function: Linking application layer to internet layer
Adds ability to distinguish among multiple applications within given host (w/ Port Numbers)
Provides unreliable, connectionless delivery
  No error recovery -- messages can be lost, duplicated or arrive out of order

## Slide 8: Protocol Ports
Protocol port: Abstract destination identified by positive integer
Local OS on each host uses set of port numbers to identify application processes
To contact application on foreign host, both dest-IP address and dest-port number needed
Ports are buffered to prevent data losses

## Slide 9: UDP Demultiplexing and Ports
Application
Process
Application
Process
Application
Process
Port 1
Packets
Demultiplexed
Queues
UDP
Packets arrive
Port 2
Port 3

## Slide 10: UDP Encapsulation
UDP Header | UDP Data Area
IP Header | IP Datagram Data Area
Frame Header | Frame Data Area

## Slide 11: UDP Header & UDP Pseudo-Header
UDP Pseudo-Header
UDP Source Port | UDP Dest. Port
UDP Mesg. Length | UDP Checksum
Data | 
0 16 31
Source IP Address |  | 
Destination IP Address |  | 
Zero | Protocol | UDP Length
UDP
Header
0 8 16 31
UDP Datagram

## Slide 12: Example of checksum calculation
Pseudo- header
UDP header
Data

## Slide 13: Reserved & Available Port Numbers
Well-known port numbers (0 through 1023)
  assigned to core services systems offer
  e.g., port 69 reserved for trivial file transfer protocol
Dynamic port numbers (1024 through 65535)
  used by client hosts as temporary ports for specific communications