## Slide 1: Transmission Control Protocol (TCP) (Chapter 13)

## Slide 2
TCP
Connection-oriented, reliable protocol
Ensures successful delivery of data through acknowledgements and sequence number tracking
Timeout and retransmission mechanism is used to recover lost data

## Slide 3: TCP Connections
TCP uses connection as its fundamental abstraction
Connections are identified as pair of endpoints
  (host, port)
Servers have their endpoints open in passive mode
Client makes active open call to get endpoint assigned by local OS
e.g., (128.10.2.3, 53) and (128.2.254.139, 1184)
Notes: 6

## Slide 4: Reliable Byte Stream Transport
TCP views application data as continuous stream of bytes
TCP divides byte stream into segments for transmission. Each segment placed in single IP datagram.
Sender uses Sequence Number to track each segment transmitted
Receiver uses Acknowledge Number to indicate sequence number of next byte in stream it expects
Notes: 8

## Slide 5: TCP segment structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
rcvr window size
ptr urgent data
checksum
F
S
R
P
A
U
head
len
not
used
Options (variable length)
URG: urgent data
ACK: ACK # valid
PSH: push data now
RST, SYN, FIN:
connection estab, terminate
# bytes
rcvr willing
to accept
counting
by bytes
of data
checksum
(as in UDP)

## Slide 6: TCP Header
Sequence Number Field ( 32 bit)
  Indicates number of first byte in segment
Receiver Window Size (16 bit)
  Window like for Go-Back-N or selective repeat, but window size not fixed – variable based on receiver feedback
Acknowledgment Field (32 bit)
  Contains sequence number of next byte receiver expects
  Cumulative acks: acknowledge all previous segments

## Slide 7: TCP Header: Code Bits (6 bits)
Connection establishment/termination
  SYN – establish; sequence number field contains valid initial sequence number
  FIN - terminate
RESET - abort connection because one side received something unexpected
PUSH - sender invoked push to send
URG – indicated urgent pointer field is valid; special data
ACK - indicates acknowledgement field is valid

## Slide 8: TCP Header: URG Bit
When URG bit set, urgent pointer specifies position in segment where urgent data ends
TCP layer informs receiving process there is urgent data
Telnet and Rlogin use URG when user types interrupt key
FTP uses URG when user aborts file transfer

## Slide 9: TCP Header: PSH Bit
Use to indicate not to leave data in TCP buffer waiting for buffer to fill
Receiver supposed to deliver data to application immediately

## Slide 10: TCP Header
Header Length (4 bits)
  Needed because options field makes header variable length
  Expressed in number of 32 bit words
Options
  Maximum Segment Size (MSS) Option
  Allows TCP to specify MSS it is willing to receive

## Slide 11: Acknowledgement and Retransmission
Send segment seq=100
Receive segment
Send ACK 101
Receive ACK 101
Segment lost
Receive ACK 201
Send segment seq=300
Events at Host 1
Events at Host 2
Messages
Send segment seq=200
Receive segment
Send ACK 201
Resend segment seq=300
Retransmission timer expires
Receive segment
Send ACK 301

## Slide 12: Timeout and Retransmission
Receiver must acknowledge receipt of all packets
Sender sets timer, if ack has not arrived before timer expires then sender will retransmit packet
Adaptive retransmission: timer value computed as function of average round trip times
Notes: Just makes sense if send a fax and want to know it gets there
ask for an acknowledgeent of receipt wait for answer or acknowledgment
if don’t hear anything for some time, resend

## Slide 13: Adaptive Retransmission
Value of retransmission timer depends on
  Distance to destination
  Current traffic conditions
Keep estimate of round trip time on each connection
Use current estimate to set timer
Notes: 14

## Slide 14: TCP Round Trip Time and Timeout
Estimate RTT
  Record time when segment sent and time when ack arrives (sample round trip time)
  Use new round trip samples to change average slowly
  RTT = ( * Old_RTT) + ((1 - ) * New_RTT), (0< <1)
Compute timeout as function of RTT
  Timeout =  * RTT, ( > 1)
  Original TCP recommended  = 2