## Slide 1: Transmission Control Protocol (TCP) (Chapter 13)

## Slide 2
Opening and Closing TCP Connection
TCP connection begins with three-way handshake between two hosts:
  to ensure destination host is available and listening on correct port
  to start tracking byte stream sequence number
Events at client
Events at server
Send SYN seq=x
Receive SYN segment
Send SYN seq=y, ACK x+1
Receive SYN + ACK segment
Send ACK y+1
Receive ACK segment
Messages

## Slide 3: Establishing Connection
Both data channels opened at once
Three-way handshake used to agree on set of parameters for this communication channel
  Initial sequence number for both sides
  Receiver advertised window size for both sides
  Optionally, Maximum Segment Size (MSS) for each side; if not specified MSS of 536 bytes is assumed to fit into 576 byte datagram

## Slide 4: Initial Sequence Numbers
Chosen randomly, changed over time
Vary initial sequence number to avoid packets delayed in network from being delivered later and interpreted as part of newly established connection

## Slide 5: Closing Connection
Send FIN seq=x
Receive FIN
Send ACK x+1
Receive ACK x+1
(Inform application)
Send FIN seq=y, ACK x+1
Receive FIN + ACK
Send ACK y+1
Receive ACK segment
Events at client
Events at server
Messages
(application closes connection)
(application closes connection)
Notes: 25

## Slide 6: TCP State Machine
TCP client
lifecycle
TCP server
lifecycle

## Slide 7: Time Wait State
Wait twice Maximum Segment Lifetime (max time old segment can remain alive in internet)
Avoids having segments from previous connection interfere with current connection
During this time, combination of client IP and port, server IP and port cannot be reused

## Slide 8: TCP Flow Control
TCP uses sliding window for end-to-end flow control
Receiver advertises available buffer space (window size)
Sender can send up to entire window before ACK arrives
Each ACK from receiver carries new window size
  Can be zero (stop transmission)

## Slide 9: TCP Congestion Control
Congestion occurred when routers become overloaded
Congestion window used to restrict data flow to less than receiver’s buffer size when congestion occurs
  Allowed_window = min(receiver_advertisement, congestion_window)
To estimate congestion window size, TCP assumes most datagram loss comes from congestion
TCP avoids congestion using two techniques
  Slow-start
  Multiplicative decrease

## Slide 10: Multiplicative Decrease
In steady state (no congestion), congestion window equals receiver’s window
When segment lost, reduce congestion window by half
Never reduce congestion window to less than one maximum sized segment
Double timeout values before retransmitting

## Slide 11: Slow Start
Used when starting traffic or recovering from congestion
start congestion window at size of single segment
Increase congestion window by one segment each time ACK arrives
When congestion window reaches one half of its original size before congestion, increase congestion window by one segment only if all segments in window acknowledged (congestion avoidance)

## Slide 12: Silly Window Syndrome
ACK advertises small amount of space available, and each segment carries small amount of data
Solutions:
  Receiver doesn’t advertise small windows; instead waits till larger window opens up
  Sender holds off sending data till larger amount accumulated

## Slide 13: Receiver-Side Silly Window Avoidance
Receiver delays advertising increase in window size until available space reaches one half of total buffer size or maximum-sized segment
Implementation
  TCP acknowledges each segment arrives, but doesn’t advertise increase in its window until window reaches specified limit
  TCP delays sending ACK when window is not sufficiently large to advertise (recommended)

## Slide 14: Sender-Side Silly Window Avoidance
Sender waits to transmit until there is sufficient data to fill maximum sized segment or until ACK arrives (send all data accumulated in buffer)