## Slide 1: Ch.15: Exterior Gateway Protocols (BGP) Ch.16: Interior Gateway Protocols (RIP, OSPF)

## Slide 2: Autonomous System (AS)
Group of networks under one administrative authority
Free to choose internal routing update mechanism
Connects to one or more other ASs

## Slide 3: Classifications of Internet Routing Protocols
Exterior Gateway Protocols (EGPs)
  Used among ASs
  Destinations lie throughout Internet
  Border Gateway Protocol (BGP)
Interior Gateway Protocols (IGPs)
  Used among routers within AS
  Destinations lie within AS
  Routing Information Protocol (RIP)
  Open Shortest Path First (OSPF)

## Slide 4: Routing on Internet with BGP, RIP, and OSPF

## Slide 5: Border Gateway Protocol (BGP)
Provides inter-autonomous system communication
Propagates reachability information
Follows next-hop paradigm
Sends path information
Allows authentication
Supports CIDR addresses
Uses reliable transport (TCP)

## Slide 6: BGP Message Types
Type Message Type Description
---------------------------------------------------------------------------------------------
1 OPEN Initialize communication
2 UPDATE Advertise or withdraw routes
3 NOTIFICATION Response to incorrect message
4 KEEPALIVE Actively test peer connectivity

## Slide 7: Routing Information Protocol (RIP)
Uses distance vector routing algorithm
Both routers and hosts can participate
  Routers can run RIP in active mode (advertise routes to others)
  Hosts must use passive mode (listen and update their own routing table based on advertisements received)
Routers broadcasts RIP update message every 30 sec
Update contains pairs of
(network address, distance)
Distance of 16 is infinity (i.e., no route)

## Slide 8: RIP Example*
Net 1
R1
Net 2
R2
R3
Net 3
Net 4
Net 5
R4
R5
R1 broadcasts to Net 2 the pair (1, 1) meaning R1 reaches Net 1 at cost 1 hop
R2 and R3 receive the message and install a route to Net 1 through R1 (at cost 2).
Later R2 and R3 will broadcast the pair (1, 2) to Net 3.
Eventually, all routers and hosts will install a route to Net 1.
* In RIP, from a router to a directly attached network is counted as 1 hop.

## Slide 9: Open Shortest Path First (OSPF)
Uses link state routing algorithm
  Each participating router independently calculates the complete internet topology
Includes type of service routing
Provides load balancing across multiple routs
Allows site to partition its networks and routers into subsets called areas
  Link-status information is propagated within an area
  Router has detailed area topology; Only knows direction (shortest path) to networks in other areas

## Slide 10: OSPF Messages
A pair of neighbor routers exchange hello messages periodically to test reachability
Routers exchange database description messages to initialize their network topology database
Router sends link status request message to neighbor to request updated info about specific set of links
Routers broadcast status of links with link status update message
Notes: 1