## Slide 1: Chapter 17: Internet Multicasting

## Slide 2: A SPECTRUM OF PARADIGMS
Multicast
Unicast
Broadcast
Send to some
Send to one
Send to All
Unicasting
  A destination address identifies a single computer
Broadcasting
  A destination address identifies all computers attached to one network
Multicasting
  A destination address identifies an arbitrary number of computers spanning several networks

## Slide 3: Why Multicast?
Unicasting
Multicasting
In many emerging applications, one sender will transmit to a group of receivers simultaneously
  Audio/Video Conferencing
  Software/File Distribution
  Replicated Database Updates
  Distributed Games, etc.
Notes: We know most flows naturally existing or generated in industrial apparatus are turbulent. Where as current CFD and DNS approaches can not efficiently resolve these problems without extensive validation by experimental data. Current experimental techniques widely in use give either 1D (LDV) or 2D (PIV) data which does not satisfy these requirements. Holographic Particle Image Velocimetry is a promising approach for instantaneous full-field 3D flow measurement.

## Slide 4: IP Multicast
Use Class D addresses
  224.0.0.0 – 239.255.255.255
Dynamic group membership
  An arbitrary computer can join a multicast group at any time
  An arbitrary member can leave a multicast group at any time
  A non-member computer can send a message to any multicast group
  Only a member computer can receive messages sent to the multicast group
Difficult to forward multicast messages: special multicast routers (mrouters) are required (software implementation)

## Slide 5: Hardware Multicast
Example: Ethernet
  One-half of the Ethernet addresses are reserved for multicast
    00-xx-xx-xx-xx-xx16 (unicast)
    01-xx-xx-xx-xx-xx16 (multicast)
  An Ethernet interface might be configured by software to have the multicast address:
    01-5E-00-00-00-0116
IP Multicast will use underlying hardware multicast whenever possible

## Slide 6: Mapping IP Multicast to Ethernet Multicast
Direct mapping; no ARP required
Place the lower-order 23 bits of an IP multicast address into the lower-order 23 bits of the special Ethernet multicast address 01-00-5E-00-00-0016
Example:
  IP multicast address
  11100000.00110011.00001010.000000102 (224.51.10.210)
  Mapped to the Ethernet multicast address
  00000001.00000000.01011110.00110011.00001010.000000102
  (01-00-5E-33-0A-0216) (1.0.94.51.10.210)

## Slide 7: Three Issues in Internet Multicasting
A multicast addressing scheme (Class D)
A membership notification mechanism (IGMP)
  A host needs to notify the mrouter
  A mrouter needs to propagate multicast group information to other mrouters (multicast protocols: DVMRP, CBT, PIM, MOSPF)
An efficient internetwork forwarding facility (multicast forwarding schemes: RPF, TRPF, RPM)

## Slide 8: Internet Group Management Protocol (IGMP)
Used by mrouters to learn about multicast group memberships on their directly attached subnets
Implemented over IP, but considered part of IP
Each network has local mrouter
  Host sends IGMP message to local mrouter to join or leave group; local mrouter propagates info to other remote mrouters
  Local mrouter periodically polls members on local network to determine status of group; multicast group needs at least one member to be kept alive

## Slide 9: Multicast Message Forwarding over Internet
Use Multicast Backbone (MBone) and IP-in-IP Encapsulation (tunneling)

## Slide 10: Reliable Multicast
Uses multicast delivery but guarantees all group members receive data in order without any loss, duplication, or corruption.
Requires acknowledgements from multicast group members to sender (ACK implosion problem)
To avoid ACK implosion
  Hierarchy of acknowledgement points
  Negative ACK (NACK)

## Slide 11: Reliable Multicast
Hierarchy of acknowledgement points
  Router in multicast path (tree) caches copies of data and processes ACKs from routers or hosts further down the tree
Negative ACK (NACK)
  Host does not respond unless datagram is lost. To detect loss, each datagram assigned unique sequence number.