## Slide 1: IGMP: Internet Group Management Protocol (Chapter 17)

## Slide 2: IGMP
Used by mrouters to learn about multicast group memberships on their directly attached subnets
Implemented over IP, but considered part of IP
Each network has local mrouter

## Slide 3: IGMP
Host sends IGMP message to local mrouter to join or leave group; local mrouter propagates info to other remote mrouters
Local mrouter periodically polls members on local network to determine status of group; multicast group needs at least one member to be kept alive

## Slide 4: IGMP Message Encapsulation
IP Header IP Datagram Data
IGMP Message

## Slide 5: IGMP Message Format
0 8 16 31
GROUP ADDRESS (ZERO IN QUERY)
TYPE RESP TIME CHECKSUM
Type | Group Address | Meaning
0x11 | Unused (zero) | General membership query (to all hosts)
0x11 | Used | Specific group membership query
0x16 | Used | Membership report
0x17 | Used | Leave group

## Slide 6: IGMP Message Format
RESP TIME (Max Response Time)
  Specifies the maximum allowed time before sending a responding report
  Each host in the group delays a random time between zero and RESP TIME before responding to the router’s query
  Default value is 10 seconds