## Slide 1
Private Network Interconnection
(VPN, NAT)
(Chapter 20)

## Slide 2: Private and Hybrid Networks
An internet is private to one group (isolated) if none of the facilities or traffic is accessible to other groups
A private network uses leased lines to interconnect routers at various sites of the group
A hybrid network permits some traffic to go over private connections and allows contact with global Internet

## Slide 3: Private and Hybrid Networks

## Slide 4: Virtual Private Network (VPN)
Connect all sites to global Internet
Protect data as it passes from one site to another
  Encryption
  IP-in-IP tunneling

## Slide 5: IP-in-IP Encapsulation used with VPN

## Slide 6: VPN Addressing and Routing

## Slide 7: VPN With Private Addresses

## Slide 8: VPN With Private Addresses
Question:
  How can a site provide access to Internet services without assigning each host a valid IP address?
Two solutions:
  Application gateway (one needed for each service)
  Network Address Translation (NAT)

## Slide 9: Network Address Translation (NAT)
NAT
Box
Global, Public
Internet
Inside Organization
Globally valid IP address (G)
Uses many private IP addresses

## Slide 10: Network Address Translation (NAT)
Replaces source IP address in each outgoing datagram with globally valid IP address of NAT box
  to outsider, all datagrams come from NAT box
Uses translation table to replace destination IP address in each incoming datagram with private address of correct internal host

## Slide 11: Creating Translation Table
On the fly (most popular)
Assumptions:
  A private host must initiate communication (to access public servers)
  Public hosts cannot access private servers
NAT examines all outgoing datagrams; it creates entry in translation table to record address of internal host and address of destination (1-to-1 mapping)

## Slide 12: Network Address Port Translation (NAPT)
Private IP Address | Private Port | External IP Address | External Port | Unique NAT Port
10.0.0.5 | 21023 | 128.10.19.20 | 80 | 14003
10.0.0.1 | 386 | 128.10.19.20 | 80 | 14010
10.0.2.6 | 26600 | 207.20.79.200 | 21 | 14012
10.0.0.3 | 1274 | 128.210.1.5 | 80 | 14007
Translates TCP/UDP port numbers as well as IP addresses

## Slide 13: Network Address Port Translation (NAPT)
For the first two items in the table, the TCP connections identification:
  before NAPT translation
    (10.0.0.5, 23023, 128.10.19.20, 80)
    (10.0.0.1, 386, 128.10.19.20, 80)
  after NAPT translation
    (G, 14003, 128.10.19.20, 80)
    (G, 14010, 128.10.19.20, 80)
G: globally valid address of NAT box

## Slide 14: Side Effects of NAT
Application protocol that passes IP addresses or protocol port numbers as data will not operate correctly across NAT
NAT must analyze the data area and perform translation if necessary
NAT supports few protocols such as ICMP and FTP