## Slide 1: Chapters 3 - 4
Internetworking Concept & Architecture
Classful Internet Addresses

## Slide 2: Internetworking
Interconnect heterogeneous networks
Scheme hides details of underlying network hardware

## Slide 3: Approaches to Hiding Heterogeneity
Using application programs
  Application level program executes on each machine in network
  Each program can inter-operate with application programs on other computers
  e.g., mailer programs forward mails from machines one-at-a-time with path involving many different networks

## Slide 4: Approaches to Hiding Heterogeneity
Network Level Approach
  Separates data communication from applications
  Concentrates on moving small packets across network
Applications
Diverse underlying physical networks connected by hardware
New software hides low-level details
and makes it a single universal network
TCP/IP

## Slide 5: Internet Architecture
net1
net2
net3
R1
R2
Networks connected by gateways or IP routers
Router forwards packets to next-hop router, based on destination IP address
Routing decisions become complex as size of internet expands

## Slide 6: The User’s View
Internet
Host
a) Single large cloud
physical
network
router
b) Actual structure

## Slide 7: Classful Internet Addresses (Chapter 4)

## Slide 8: Internet Addresses
Universal internet requires method of identifying computers attached to internet
Host identifiers classified as
  Names,
  Addresses, or
  Routes (interfaces)

## Slide 9
IPv4 Addressing Basics
IPv4 uses three-part addressing scheme:
  Symbolic e.g., www.csun.edu
  Logical numeric 130.166.1.1
  Physical numeric ef.09.35.a6.00.b5

## Slide 10: IPv4 Logical Addresses
Each host on TCP/IP internet assigned unique 32-bit integer IP address
IP address encodes
  identification of network to which host attaches
  identification of unique host on that network
IP address = (netid, hostid)

## Slide 11: Classful Internet Addresses
0 1 2 3
7 8
16
24
31
0
netid
hostid
1 0
netid
hostid
1 1 0
netid
hostid
1 1 1 0
multicast address
1 1 1 1 0
reserved for future use
Class A
Class B
Class C
Class D
Class E

## Slide 12: Class A Addresses
Expressed in binary form (ones and zeroes only)
Class A addresses take the form:
  0nnnnnnn.hhhhhhhh.hhhhhhhh.hhhhhhhh
IP addresses consisting of all zeroes and all ones reserved for special uses
Of 128 possible Class A network addresses (netid), only those from 00000001 to 01111110 (or 1 to 126) considered usable

## Slide 13: Private Class A Addresses
Address 127.x.x.x reserved for loopback
Used for
  testing TCP/IP
  inter-process communication on local computer

## Slide 14: Address Classes B and C
Class B addresses take the form:
  10nnnnnn.nnnnnnnn.hhhhhhhh.hhhhhhhh
Class C addresses take the form:
  110nnnnn.nnnnnnnn.nnnnnnnn.hhhhhhhh

## Slide 15: Address Classes D and E
Class D addresses always take the form:
  1110bbbb.bbbbbbbb.bbbbbbbb.bbbbbbbb
Class E addresses always take the form:
  11110bbb.bbbbbbbb.bbbbbbbb.bbbbbbbbb
Class D is used for multicast addresses
  Multiple users “share” single IP address and receive same packet across network from single transmission

## Slide 16: IP Network Address Space
Class | Lowest Address | Highest Address
A | 1.0.0.0 | 126.0.0.0
B | 128.1.0.0 | 191.255.0.0
C | 192.0.1.0 | 223.255.255.0
D | 224.0.0.0 | 239.255.255.255
E | 240.0.0.0 | 255.255.255.254

## Slide 17: Using Network and Host Portions of IP Address
Router uses network portion (netid) when forwarding packet from source host’s network to destination host’s network
Host portion (hostid) used when packet reaches router attached to final network where destination host resides

## Slide 18: Special IP Addresses
IP address with hostid all 0’s refers to network itself
Directed broadcast address refers to all hosts on network with hostid all 1’s
Limited broadcast address (all 32 bits 1’s) may be used in startup process to learn host’s or network’s IP address

## Slide 19: Special IP Addresses Summary
all 0’s
This host
host
Host on this net
all 1’s
Limited broadcast (local net)
net
all 1’s
Directed broadcast for net
127
anything (often 1)
Loop-back address (127.0.0.1)
all 0’s

## Slide 20: Example of IP addressing
Ethernet 131.108.0.0
131.108.99.5
223.240.129.2
Token ring
223.240.129.0
223.240.129.17
78.0.0.17
WAN 78.0.0.0
R1
R2
131.108.2.31
78.0.81.154
Computer has two or more physical connections, called multi-homed host