## Slide 1: Internet Protocol Chapter 7: Connectionless Datagram Delivery Chapter 8: Routing IP Datagrams Chapter 9: Error and Control Messages (ICMP)

## Slide 2
Connectionless Datagram Delivery
(Chapter 7)

## Slide 3: Conceptual Layers of Internet Services
APPLICATION SERVICES
RELIABLE TRANSPORT SERVICE
CONNECTIONLESS PACKET DELIVERY
Physical Network Hardware
IP
TCP
Email, file
transfer, Web, etc.

## Slide 4: Purpose of Internet Protocol
IP provides connectionless, unreliable, best-effort packet delivery system
IP defines hardware-independent packet format: IP datagram
IP software performs link-to-link routing function
IP defines set of rules hosts and routers follow to process datagrams and handle error conditions

## Slide 5: IPv4 Datagram Format
IP datagram header
data area
0
16
31
4
8
19
24
IP Datagram
VERS | HLEN | SERVICE TYPE | TOTAL LENGTH |  | 
IDENTIFICATION |  |  | FLAGS | FRAGMENT OFFSET | 
TIME TO LIVE |  | PROTOCOL | HEADER CHECKSUM |  | 
SOURCE IP ADDRESS |  |  |  |  | 
DESTINATION IP ADDRESS |  |  |  |  | 
IP OPTIONS (IF ANY) |  |  |  |  | 
 |  |  |  |  | PADDING
DATA |  |  |  |  | 

## Slide 6: Service Type
8-bit field specifies how datagram should be handled
Precedence
  000 normal
  : :
  111 network control
Type of Transport
  100 low delay
  010 high throughput
  001 high reliability
0 1 2 3 4 5 6 7
PRECEDENCE
D
T
R
UNUSED
PRECEDENCE bits indicate importance of datagram
Bits D, T, R specify type of transport desired for datagram

## Slide 7: Differentiated Services (DS)
Redefine meaning of 8-bit SERVICE TYPE field
0 1 2 3 4 5 6 7
CODEPOINT (DSCP)
UNUSED
Maintain backward compatibility with original definition
xxx000
precedence bits
Three administrative groups for codepoint values
Pool Codepoint Assigned By__________
1 xxxxx0 Standards organization 2 xxxx11 Local or experimental 3 xxxx01 Local or experimental for now

## Slide 8: Datagram Encapsulation
Physical network limits amount of data transferred in one physical frame, e.g.,
  Ethernet MTU = 1500 octets
  FDDI MTU = 4470 octets
DATAGRAM HEADER
DATAGRAM DATA AREA
FRAME HEADER
FRAME DATA AREA
In IPv4, datagram
can be up to 65,535
octets in size
Maximum transfer unit (MTU)

## Slide 9: Efficiency Vs. Size
Limiting datagrams to fit smallest MTU makes transfers inefficient for network with larger MTU
Larger datagrams may not fit entirely into single network frame with smaller MTU
TCP/IP software chooses initial size of datagram
Routers perform fragmentation when forwarding datagrams over networks with smaller MTUs

## Slide 10: Fragmentation
HOST A
HOST B
R1
R2
Net 2
MTU=620
Net 1
MTU=1500
Net 3
MTU=1500

## Slide 11: Datagram Fragments: An Example
FRAGMENT 1
HEADER
data 1
FRAGMENT 2
HEADER
data 2
FRAGMENT 3
HEADER
data 3
FRAGMENT1 (offset 0)
FRAGMENT 2 (offset 600)
FRAGMENT 3 (offset 1200)
DATAGRAM
HEADER
data 1
600 octets
data 2
600 octets
data 3
200 octets
Except FLAGS and FRAGMENT OFFSET fields, fragment header is same as original datagram header

## Slide 12: Fragmentation Control
IDENTIFICATION field uniquely identifies datagram
FRAGMENT OFFSET field specifies, in units of 8 octets, distance of fragment from start of original data block
Low-order 2 bits of FLAG control fragmentation
  do-not-fragment bit prohibits fragmentation when set
  more-fragment bit indicates whether this is last fragment in original datagram

## Slide 13: Reassembly of Fragments
Where should fragments be reassembled?
In TCP/IP fragments proceed independently to destination before reassembly
Advantage:
  Reduce router workload
Disadvantages:
  Inefficiency of carrying small fragments
  Probability of datagram loss increases due to loss of fragment

## Slide 14: Other Fields in Datagram Header
Time to Live (TTL) specifies how many hops datagram is allowed to take before it is dropped
Protocol field identifies which high-level protocol was used to create datagram (TCP,UDP,ICMP,...)
Header-Checksum ensures integrity of header values
Source and Destination IP Addresses
IP Options

## Slide 15: IP Options
Mainly used for network testing and debugging

## Slide 16: No Operation
Used to align octets in a list of options

## Slide 17: End of Option
Used if options do not end at end of header

## Slide 18: Record Route Option
Source creates empty list of IP addresses in header
Set Record route option
  Code 7, length (including first three), and pointer
Each router that handles datagram appends its IP address to list
Destination machine can extract and process route information

## Slide 19: Record Route
Allow source to create empty list of IP addresses and arrange for each router that handles datagram to add its IP address

## Slide 20: Source Route Option
Sender dictates path through internet over which datagram must travel
Sender lists IP addresses (in order) of route datagram should take
Sender sets source route option

## Slide 21: Source Route Option (cont)
Strict source routing
  Path between two successive addresses in list must consist of single physical network
Loose source routing
  Datagram must follow sequence of IP addresses in list
  Allows multiple network hops between successive addresses on list

## Slide 22: Strict Source Route

## Slide 24: Loose Source Route

## Slide 25: Timestamp Option
Sender creates empty list in header
Sender enables timestamp option
Each router that handles datagram appends to list its:
  IP address
  Local timestamp (in Universal Time)

## Slide 26: Internet Timestamp

## Slide 28: Processing Options During Fragmentation
When fragmenting datagram
  Router replicates some IP options in all fragments
    Source Route
  Router replicates some IP options in only one fragment
    Record Route