## Slide 1
Lectures for 2nd Edition
Note: these lectures are often supplemented with other materials and also problems from the text worked out on the blackboard. You’ll want to customize these lectures for your class. The student audience for these lectures have had assembly language programming and exposure to logic design

## Slide 2
Chapter 1

## Slide 3
Introduction
Rapidly changing field:
  vacuum tube -> transistor -> IC -> VLSI (see section 1.4)
  doubling every 1.5 years: memory capacity processor speed (Due to advances in technology and organization)
Things you’ll be learning:
  how computers work, a basic foundation
  how to analyze their performance (or how not to!)
  issues affecting modern processors (caches, pipelines)
Why learn this stuff?
  you want to call yourself a “computer scientist”
  you want to build software people use (need performance)
  you need to make a purchasing decision or offer “expert” advice

## Slide 4
What is a computer?
Components:
  input (mouse, keyboard)
  output (display, printer)
  memory (disk drives, DRAM, SRAM, CD)
  network
Our primary focus: the processor (datapath and control)
  implemented using millions of transistors
  Impossible to understand by looking at each transistor
  We need...

## Slide 5
Abstraction
Delving into the depths reveals more information
An abstraction omits unneeded detail, helps us cope with complexity What are some of the details that appear in these familiar abstractions?

## Slide 6
Instruction Set Architecture
A very important abstraction
  interface between hardware and low-level software
  standardizes instructions, machine language bit patterns, etc.
  advantage: different implementations of the same architecture
  disadvantage: sometimes prevents using new innovations True or False: Binary compatibility is extraordinarily important?
Modern instruction set architectures:
  80x86/Pentium/K6, PowerPC, DEC Alpha, MIPS, SPARC, HP

## Slide 7
Where we are headed
Performance issues (Chapter 2) vocabulary and motivation
A specific instruction set architecture (Chapter 3)
Arithmetic and how to build an ALU (Chapter 4)
Constructing a processor to execute our instructions (Chapter 5)
Pipelining to improve performance (Chapter 6)
Memory: caches and virtual memory (Chapter 7)
I/O (Chapter 8) Key to a good grade: reading the book!

## Slide 8
Chapter 2

## Slide 9
Measure, Report, and Summarize
Make intelligent choices
See through the marketing hype
Key to understanding underlying organizational motivation Why is some hardware better than others for different programs? What factors of system performance are hardware related? (e.g., Do we need a new machine, or a new operating system?) How does the machine's instruction set affect performance?
Performance

## Slide 10
Which of these airplanes has the best performance?
Airplane Passengers Range (mi) Speed (mph)
Boeing 737-100 101 630 598
Boeing 747 470 4150 610
BAC/Sud Concorde 132 4000 1350
Douglas DC-8-50 146 8720 544
How much faster is the Concorde compared to the 747?
How much bigger is the 747 than the Douglas DC-8?

## Slide 11
Response Time (latency) — How long does it take for my job to run? — How long does it take to execute a job? — How long must I wait for the database query?
Throughput — How many jobs can the machine run at once? — What is the average execution rate? — How much work is getting done?
If we upgrade a machine with a new processor what do we increase?
If we add a new machine to the lab what do we increase?
Computer Performance: TIME, TIME, TIME
Notes: Have them raise their hands when answering questions

## Slide 12
Elapsed Time
  counts everything (disk and memory accesses, I/O , etc.)
  a useful number, but often not good for comparison purposes
CPU time
  doesn't count I/O or time spent running other programs
  can be broken up into system time, and user time
Our focus: user CPU time
  time spent executing the lines of code that are "in" our program
Execution Time

## Slide 13
For some program running on machine X, PerformanceX = 1 / Execution timeX
"X is n times faster than Y" PerformanceX / PerformanceY = n
Problem:
  machine A runs a program in 20 seconds
  machine B runs the same program in 25 seconds
Book's Definition of Performance

## Slide 14
Clock Cycles
Instead of reporting execution time in seconds, we often use cycles
Clock “ticks” indicate when to start activities (one abstraction):
cycle time = time between ticks = seconds per cycle
clock rate (frequency) = cycles per second (1 Hz. = 1 cycle/sec) A 200 Mhz. clock has a cycle time
time

## Slide 15
So, to improve performance (everything else being equal) you can either ________ the # of required cycles for a program, or ________ the clock cycle time or, said another way, ________ the clock rate.
How to Improve Performance

## Slide 16
Could assume that # of cycles = # of instructions
This assumption is incorrect, different instructions take different amounts of time on different machines. Why? hint: remember that these are machine instructions, not lines of C code
time
1st instruction
2nd instruction
3rd instruction
4th
5th
6th
...
How many cycles are required for a program?

## Slide 17
Multiplication takes more time than addition
Floating point operations take longer than integer ones
Accessing memory takes more time than accessing registers
Important point: changing the cycle time often changes the number of cycles required for various instructions (more later)
time
Different numbers of cycles for different instructions

## Slide 18
Our favorite program runs in 10 seconds on computer A, which has a 400 Mhz. clock. We are trying to help a computer designer build a new machine B, that will run this program in 6 seconds. The designer can use new (or perhaps more expensive) technology to substantially increase the clock rate, but has informed us that this increase will affect the rest of the CPU design, causing machine B to require 1.2 times as many clock cycles as machine A for the same program. What clock rate should we tell the designer to target?"
Don't Panic, can easily work this out from basic principles
Example

## Slide 19
A given program will require
  some number of instructions (machine instructions)
  some number of cycles
  some number of seconds
We have a vocubulary that relates these quantities:
  cycle time (seconds per cycle)
  clock rate (cycles per second)
  CPI (cycles per instruction) a floating point intensive application might have a higher CPI
  MIPS (millions of instructions per second) this would be higher for a program using simple instructions
Now that we understand cycles

## Slide 20
Performance
Performance is determined by execution time
Do any of the other variables equal performance?
  # of cycles to execute program?
  # of instructions in program?
  # of cycles per second?
  average # of cycles per instruction?
  average # of instructions per second?
Common pitfall: thinking one of the variables is indicative of performance when it really isn’t.

## Slide 21
Suppose we have two implementations of the same instruction set architecture (ISA). For some program, Machine A has a clock cycle time of 10 ns. and a CPI of 2.0 Machine B has a clock cycle time of 20 ns. and a CPI of 1.2 What machine is faster for this program, and by how much?
If two machines have the same ISA which of our quantities (e.g., clock rate, CPI, execution time, # of instructions, MIPS) will always be identical?
CPI Example

## Slide 22
A compiler designer is trying to decide between two code sequences for a particular machine. Based on the hardware implementation, there are three different classes of instructions: Class A, Class B, and Class C, and they require one, two, and three cycles (respectively). The first code sequence has 5 instructions: 2 of A, 1 of B, and 2 of C The second sequence has 6 instructions: 4 of A, 1 of B, and 1 of C. Which sequence will be faster? How much? What is the CPI for each sequence?
# of Instructions Example

## Slide 23
Two different compilers are being tested for a 100 MHz. machine with three different classes of instructions: Class A, Class B, and Class C, which require one, two, and three cycles (respectively). Both compilers are used to produce code for a large piece of software. The first compiler's code uses 5 million Class A instructions, 1 million Class B instructions, and 1 million Class C instructions. The second compiler's code uses 10 million Class A instructions, 1 million Class B instructions, and 1 million Class C instructions.
Which sequence will be faster according to MIPS?
Which sequence will be faster according to execution time?
MIPS example

## Slide 24
Performance best determined by running a real application
  Use programs typical of expected workload
  Or, typical of expected class of applications e.g., compilers/editors, scientific applications, graphics, etc.
Small benchmarks
  nice for architects and designers
  easy to standardize
  can be abused
SPEC (System Performance Evaluation Cooperative)
  companies have agreed on a set of real program and inputs
  can still be abused (Intel’s “other” bug)
  valuable indicator of performance (and compiler technology)
Benchmarks

## Slide 25
SPEC ‘89
Compiler “enhancements” and performance

## Slide 26
SPEC ‘95

## Slide 27
SPEC ‘95
Does doubling the clock rate double the performance?
Can a machine with a slower clock rate have better performance?

## Slide 28
Execution Time After Improvement = Execution Time Unaffected +( Execution Time Affected / Amount of Improvement )
Example: "Suppose a program runs in 100 seconds on a machine, with multiply responsible for 80 seconds of this time. How much do we have to improve the speed of multiplication if we want the program to run 4 times faster?" How about making it 5 times faster?
Principle: Make the common case fast
Amdahl's Law

## Slide 29
Suppose we enhance a machine making all floating-point instructions run five times faster. If the execution time of some benchmark before the floating-point enhancement is 10 seconds, what will the speedup be if half of the 10 seconds is spent executing floating-point instructions?
We are looking for a benchmark to show off the new floating-point unit described above, and want the overall benchmark to show a speedup of 3. One benchmark we are considering runs for 100 seconds with the old floating-point hardware. How much of the execution time would floating-point instructions have to account for in this program in order to yield our desired speedup on this benchmark?
Example

## Slide 30
Performance is specific to a particular program/s
  Total execution time is a consistent summary of performance
For a given architecture performance increases come from:
  increases in clock rate (without adverse CPI affects)
  improvements in processor organization that lower CPI
  compiler enhancements that lower CPI and/or instruction count
Pitfall: expecting improvement in one aspect of a machine’s performance to affect the total performance
You should not always believe everything you read! Read carefully! (see newspaper articles, e.g., Exercise 2.37)
Remember

## Slide 31
Chapter 3

## Slide 32
Instructions:
Language of the Machine
More primitive than higher level languages e.g., no sophisticated control flow
Very restrictive e.g., MIPS Arithmetic Instructions
We’ll be working with the MIPS instruction set architecture
  similar to other architectures developed since the 1980's
  used by NEC, Nintendo, Silicon Graphics, Sony
Design goals: maximize performance and minimize cost, reduce design time

## Slide 33
MIPS arithmetic
All instructions have 3 operands
Operand order is fixed (destination first) Example: C code: A = B + C MIPS code: add $s0, $s1, $s2 (associated with variables by compiler)

## Slide 34
MIPS arithmetic
Design Principle: simplicity favors regularity. Why?
Of course this complicates some things... C code: A = B + C + D; E = F - A; MIPS code: add $t0, $s1, $s2 add $s0, $t0, $s3 sub $s4, $s5, $s0
Operands must be registers, only 32 registers provided
Design Principle: smaller is faster. Why?

## Slide 35
Registers vs. Memory
Processor
I/O
Control
Datapath
Memory
Input
Output
Arithmetic instructions operands must be registers, — only 32 registers provided
Compiler associates variables with registers
What about programs with lots of variables

## Slide 36
Memory Organization
Viewed as a large, single-dimension array, with an address.
A memory address is an index into the array
"Byte addressing" means that the index points to a byte of memory.
0
1
2
3
4
5
6
...
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data

## Slide 37
Memory Organization
Bytes are nice, but most data items use larger "words"
For MIPS, a word is 32 bits or 4 bytes.
232 bytes with byte addresses from 0 to 232-1
230 words with byte addresses 0, 4, 8, ... 232-4
Words are aligned i.e., what are the least 2 significant bits of a word address?
0
4
8
12
...
32 bits of data
32 bits of data
32 bits of data
32 bits of data
Registers hold 32 bits of data

## Slide 38
Instructions
Load and store instructions
Example: C code: A[8] = h + A[8]; MIPS code: lw $t0, 32($s3) add $t0, $s2, $t0 sw $t0, 32($s3)
Store word has destination last
Remember arithmetic operands are registers, not memory!

## Slide 39
Our First Example
Can we figure out the code?
swap(int v[], int k);
{ int temp;
temp = v[k]
v[k] = v[k+1];
v[k+1] = temp;
}
swap:
muli $2, $5, 4
add $2, $4, $2
lw $15, 0($2)
lw $16, 4($2)
sw $16, 0($2)
sw $15, 4($2)
jr $31

## Slide 40
So far we’ve learned:
MIPS — loading words but addressing bytes — arithmetic on registers only
Instruction Meaning add $s1, $s2, $s3 $s1 = $s2 + $s3 sub $s1, $s2, $s3 $s1 = $s2 – $s3 lw $s1, 100($s2) $s1 = Memory[$s2+100] sw $s1, 100($s2) Memory[$s2+100] = $s1

## Slide 41
Instructions, like registers and words of data, are also 32 bits long
  Example: add $t0, $s1, $s2
  registers have numbers, $t0=9, $s1=17, $s2=18
Instruction Format: 000000 10001 10010 01000 00000 100000 op rs rt rd shamt funct
Can you guess what the field names stand for?
Machine Language
Notes: Board work: Binary Numbers

## Slide 42
Consider the load-word and store-word instructions,
  What would the regularity principle have us do?
  New principle: Good design demands a compromise
Introduce a new type of instruction format
  I-type for data transfer instructions
  other format was R-type for register
Example: lw $t0, 32($s2) 35 18 9 32 op rs rt 16 bit number
Where's the compromise?
Machine Language

## Slide 43
Instructions are bits
Programs are stored in memory — to be read or written just like data
Fetch & Execute Cycle
  Instructions are fetched and put into a special register
  Bits in the register "control" the subsequent actions
  Fetch the “next” instruction and continue
Processor
Memory
memory for data, programs,
compilers, editors, etc.
Stored Program Concept

## Slide 44
Decision making instructions
  alter the control flow,
  i.e., change the "next" instruction to be executed
MIPS conditional branch instructions: bne $t0, $t1, Label beq $t0, $t1, Label
Example: if (i==j) h = i + j; bne $s0, $s1, Label add $s3, $s0, $s1 Label: ....
Control

## Slide 45
MIPS unconditional branch instructions: j label
Example: if (i!=j) beq $s4, $s5, Lab1 h=i+j; add $s3, $s4, $s5 else j Lab2 h=i-j; Lab1: sub $s3, $s4, $s5 Lab2: ...
Can you build a simple for loop?
Control

## Slide 46
So far:
Instruction Meaning add $s1,$s2,$s3 $s1 = $s2 + $s3 sub $s1,$s2,$s3 $s1 = $s2 – $s3 lw $s1,100($s2) $s1 = Memory[$s2+100] sw $s1,100($s2) Memory[$s2+100] = $s1 bne $s4,$s5,L Next instr. is at Label if $s4 ° $s5 beq $s4,$s5,L Next instr. is at Label if $s4 = $s5 j Label Next instr. is at Label
Formats:
op rs rt rd shamt funct
op rs rt 16 bit address
op 26 bit address
R
I
J

## Slide 47
We have: beq, bne, what about Branch-if-less-than?
New instruction: if $s1 < $s2 then $t0 = 1 slt $t0, $s1, $s2 else $t0 = 0
Can use this instruction to build "blt $s1, $s2, Label" — can now build general control structures
Note that the assembler needs a register to do this, — there are policy of use conventions for registers
2
Control Flow
Notes: Board work: Binary Numbers

## Slide 48
Policy of Use Conventions

## Slide 49
Small constants are used quite frequently (50% of operands) e.g., A = A + 5; B = B + 1; C = C - 18;
Solutions? Why not?
  put 'typical constants' in memory and load them.
  create hard-wired registers (like $zero) for constants like one.
MIPS Instructions: addi $29, $29, 4 slti $8, $18, 10 andi $29, $29, 6 ori $29, $29, 4
How do we make this work?
3
Constants

## Slide 50
We'd like to be able to load a 32 bit constant into a register
Must use two instructions, new "load upper immediate" instruction lui $t0, 1010101010101010
Then must get the lower order bits right, i.e., ori $t0, $t0, 1010101010101010
1010101010101010
0000000000000000
0000000000000000
1010101010101010
1010101010101010
1010101010101010
ori
1010101010101010
0000000000000000
filled with zeros
How about larger constants?

## Slide 51
Assembly provides convenient symbolic representation
  much easier than writing down numbers
  e.g., destination first
Machine language is the underlying reality
  e.g., destination is no longer first
Assembly can provide 'pseudoinstructions'
  e.g., “move $t0, $t1” exists only in Assembly
  would be implemented using “add $t0,$t1,$zero”
When considering performance you should count real instructions
Assembly Language vs. Machine Language

## Slide 52
Things we are not going to cover support for procedures linkers, loaders, memory layout stacks, frames, recursion manipulating strings and pointers interrupts and exceptions system calls and conventions
Some of these we'll talk about later
We've focused on architectural issues
  basics of MIPS assembly language and machine code
  we’ll build a processor to execute these instructions.
Other Issues

## Slide 53
simple instructions all 32 bits wide
very structured, no unnecessary baggage
only three instruction formats
rely on compiler to achieve performance — what are the compiler's goals?
help compiler where we can
op rs rt rd shamt funct
op rs rt 16 bit address
op 26 bit address
R
I
J
Overview of MIPS

## Slide 54
Instructions:
bne $t4,$t5,Label Next instruction is at Label if $t4 ° $t5
beq $t4,$t5,Label Next instruction is at Label if $t4 = $t5
j Label Next instruction is at Label
Formats:
Addresses are not 32 bits — How do we handle this with load and store instructions?
op rs rt 16 bit address
op 26 bit address
I
J
Addresses in Branches and Jumps

## Slide 55
Instructions:
bne $t4,$t5,Label Next instruction is at Label if $t4°$t5
beq $t4,$t5,Label Next instruction is at Label if $t4=$t5
Formats:
Could specify a register (like lw and sw) and add it to address
  use Instruction Address Register (PC = program counter)
  most branches are local (principle of locality)
Jump instructions just use high order bits of PC
  address boundaries of 256 MB
op rs rt 16 bit address
I
Addresses in Branches

## Slide 56
To summarize:

## Slide 58
Design alternative:
  provide more powerful operations
  goal is to reduce number of instructions executed
  danger is a slower cycle time and/or a higher CPI
Sometimes referred to as “RISC vs. CISC”
  virtually all new instruction sets since 1982 have been RISC
  VAX: minimize code size, make assembly language easy instructions from 1 to 54 bytes long!
We’ll look at PowerPC and 80x86
Alternative Architectures

## Slide 59
PowerPC
Indexed addressing
  example: lw $t1,$a0+$s3 #$t1=Memory[$a0+$s3]
  What do we have to do in MIPS?
Update addressing
  update a register as part of load (for marching through arrays)
  example: lwu $t0,4($s3) #$t0=Memory[$s3+4];$s3=$s3+4
  What do we have to do in MIPS?
Others:
  load multiple/store multiple
  a special counter register “bc Loop” decrement counter, if not 0 goto loop

## Slide 60
80x86
1978: The Intel 8086 is announced (16 bit architecture)
1980: The 8087 floating point coprocessor is added
1982: The 80286 increases address space to 24 bits, +instructions
1985: The 80386 extends to 32 bits, new addressing modes
1989-1995: The 80486, Pentium, Pentium Pro add a few instructions (mostly designed for higher performance)
1997: MMX is added “This history illustrates the impact of the “golden handcuffs” of compatibility “adding new features as someone might add clothing to a packed bag” “an architecture that is difficult to explain and impossible to love”

## Slide 61
A dominant architecture: 80x86
See your textbook for a more detailed description
Complexity:
  Instructions from 1 to 17 bytes long
  one operand must act as both a source and destination
  one operand can come from memory
  complex addressing modes e.g., “base or scaled index with 8 or 32 bit displacement”
Saving grace:
  the most frequently used instructions are not too difficult to build
  compilers avoid the portions of the architecture that are slow
“what the 80x86 lacks in style is made up in quantity, making it beautiful from the right perspective”

## Slide 62
Instruction complexity is only one variable
  lower instruction count vs. higher CPI / lower clock rate
Design Principles:
  simplicity favors regularity
  smaller is faster
  good design demands compromise
  make the common case fast
Instruction set architecture
  a very important abstraction indeed!
Summary

## Slide 63
Chapter Four

## Slide 64
Arithmetic
Where we've been:
  Performance (seconds, cycles, instructions)
  Abstractions: Instruction Set Architecture Assembly Language and Machine Language
What's up ahead:
  Implementing the Architecture
32
32
32
operation
result
a
b
ALU

## Slide 65
Bits are just bits (no inherent meaning) — conventions define relationship between bits and numbers
Binary numbers (base 2) 0000 0001 0010 0011 0100 0101 0110 0111 1000 1001... decimal: 0...2n-1
Of course it gets more complicated: numbers are finite (overflow) fractions and real numbers negative numbers e.g., no MIPS subi instruction; addi can add a negative number)
How do we represent negative numbers? i.e., which bit patterns will represent which numbers?
Numbers

## Slide 66
Sign Magnitude: One's Complement Two's Complement 000 = +0 000 = +0 000 = +0 001 = +1 001 = +1 001 = +1 010 = +2 010 = +2 010 = +2 011 = +3 011 = +3 011 = +3 100 = -0 100 = -3 100 = -4 101 = -1 101 = -2 101 = -3 110 = -2 110 = -1 110 = -2 111 = -3 111 = -0 111 = -1
Issues: balance, number of zeros, ease of operations
Which one is best? Why?
Possible Representations

## Slide 67
32 bit signed numbers: 0000 0000 0000 0000 0000 0000 0000 0000two = 0ten 0000 0000 0000 0000 0000 0000 0000 0001two = + 1ten 0000 0000 0000 0000 0000 0000 0000 0010two = + 2ten ... 0111 1111 1111 1111 1111 1111 1111 1110two = + 2,147,483,646ten 0111 1111 1111 1111 1111 1111 1111 1111two = + 2,147,483,647ten 1000 0000 0000 0000 0000 0000 0000 0000two = – 2,147,483,648ten 1000 0000 0000 0000 0000 0000 0000 0001two = – 2,147,483,647ten 1000 0000 0000 0000 0000 0000 0000 0010two = – 2,147,483,646ten ... 1111 1111 1111 1111 1111 1111 1111 1101two = – 3ten 1111 1111 1111 1111 1111 1111 1111 1110two = – 2ten 1111 1111 1111 1111 1111 1111 1111 1111two = – 1ten
maxint
minint
MIPS

## Slide 68
Negating a two's complement number: invert all bits and add 1
  remember: “negate” and “invert” are quite different!
Converting n bit numbers into numbers with more than n bits:
  MIPS 16 bit immediate gets converted to 32 bits for arithmetic
  copy the most significant bit (the sign bit) into the other bits 0010 -> 0000 0010 1010 -> 1111 1010
  "sign extension" (lbu vs. lb)
Two's Complement Operations

## Slide 69
Just like in grade school (carry/borrow 1s) 0111 0111 0110 + 0110 - 0110 - 0101
Two's complement operations easy
  subtraction using addition of negative numbers 0111 + 1010
Overflow (result too large for finite computer word):
  e.g., adding two n-bit numbers does not yield an n-bit number 0111 + 0001 note that overflow term is somewhat misleading, 1000 it does not mean a carry “overflowed”
Addition & Subtraction

## Slide 70
No overflow when adding a positive and a negative number
No overflow when signs are the same for subtraction
Overflow occurs when the value affects the sign:
  overflow when adding two positives yields a negative
  or, adding two negatives gives a positive
  or, subtract a negative from a positive and get a negative
  or, subtract a positive from a negative and get a positive
Consider the operations A + B, and A – B
  Can overflow occur if B is 0 ?
  Can overflow occur if A is 0 ?
Detecting Overflow

## Slide 71
An exception (interrupt) occurs
  Control jumps to predefined address for exception
  Interrupted address is saved for possible resumption
Details based on software system / language
  example: flight control vs. homework assignment
Don't always want to detect overflow — new MIPS instructions: addu, addiu, subu note: addiu still sign-extends! note: sltu, sltiu for unsigned comparisons
Effects of Overflow

## Slide 72
Problem: Consider a logic function with three inputs: A, B, and C. Output D is true if at least one input is true Output E is true if exactly two inputs are true Output F is true only if all three inputs are true
Show the truth table for these three functions.
Show the Boolean equations for these three functions.
Show an implementation consisting of inverters, AND, and OR gates.
Review: Boolean Algebra & Gates

## Slide 73
Let's build an ALU to support the andi and ori instructions
  we'll just build a 1 bit ALU, and use 32 of them
Possible Implementation (sum-of-products):
b
a
operation
result
op
a
b
res
An ALU (arithmetic logic unit)

## Slide 74
Selects one of the inputs to be the output, based on a control input
Lets build our ALU using a MUX:
S
C
A
B
0
1
Review: The Multiplexor
note: we call this a 2-input mux
even though it has 3 inputs!

## Slide 75
Not easy to decide the “best” way to build something
  Don't want too many inputs to a single gate
  Dont want to have to go through too many gates
  for our purposes, ease of comprehension is important
Let's look at a 1-bit ALU for addition:
How could we build a 1-bit ALU for add, and, and or?
How could we build a 32-bit ALU?
Different Implementations
cout = a b + a cin + b cin
sum = a xor b xor cin

## Slide 76
Building a 32 bit ALU

## Slide 77
Two's complement approch: just negate b and add.
How do we negate?
A very clever solution:
What about subtraction (a – b) ?

## Slide 78
Need to support the set-on-less-than instruction (slt)
  remember: slt is an arithmetic instruction
  produces a 1 if rs < rt and 0 otherwise
  use subtraction: (a-b) < 0 implies a < b
Need to support test for equality (beq $t5, $t6, $t7)
  use subtraction: (a-b) = 0 implies a = b
Tailoring the ALU to the MIPS

## Slide 79
Supporting slt
Can we figure out the idea?

## Slide 81
Test for equality
Notice control lines: 000 = and 001 = or 010 = add 110 = subtract 111 = slt
Note: zero is a 1 when the result is zero!

## Slide 82
Conclusion
We can build an ALU to support the MIPS instruction set
  key idea: use multiplexor to select the output we want
  we can efficiently perform subtraction using two’s complement
  we can replicate a 1-bit ALU to produce a 32-bit ALU
Important points about hardware
  all of the gates are always working
  the speed of a gate is affected by the number of inputs to the gate
  the speed of a circuit is affected by the number of gates in series (on the “critical path” or the “deepest level of logic”)
Our primary focus: comprehension, however,
  Clever changes to organization can improve performance (similar to using better algorithms in software)
  we’ll look at two examples for addition and multiplication

## Slide 83
Is a 32-bit ALU as fast as a 1-bit ALU?
Is there more than one way to do addition?
  two extremes: ripple carry and sum-of-products
Can you see the ripple? How could you get rid of it?
c1 = b0c0 + a0c0 + a0b0
c2 = b1c1 + a1c1 + a1b1 c2 =
c3 = b2c2 + a2c2 + a2b2 c3 =
c4 = b3c3 + a3c3 + a3b3 c4 =
Not feasible! Why?
Problem: ripple carry adder is slow

## Slide 84
An approach in-between our two extremes
Motivation:
  If we didn't know the value of carry-in, what could we do?
  When would we always generate a carry? gi = ai bi
  When would we propagate the carry? pi = ai + bi
Did we get rid of the ripple?
c1 = g0 + p0c0
c2 = g1 + p1c1 c2 =
c3 = g2 + p2c2 c3 =
c4 = g3 + p3c3 c4 = Feasible! Why?
Carry-lookahead adder

## Slide 85
Can’t build a 16 bit adder this way... (too big)
Could use ripple carry of 4-bit CLA adders
Better: use the CLA principle again!
Use principle to build bigger adders

## Slide 86
More complicated than addition
  accomplished via shifting and addition
More time and more area
Let's look at 3 versions based on gradeschool algorithm 0010 (multiplicand) __x_1011 (multiplier)
Negative numbers: convert and multiply
  there are better techniques, we won’t look at them
Multiplication

## Slide 87
Multiplication: Implementation

## Slide 88
Second Version

## Slide 89
Final Version

## Slide 90
Floating Point (a brief look)
We need a way to represent
  numbers with fractions, e.g., 3.1416
  very small numbers, e.g., .000000001
  very large numbers, e.g., 3.15576 × 109
Representation:
  sign, exponent, significand: (–1)sign × significand × 2exponent
  more bits for significand gives more accuracy
  more bits for exponent increases range
IEEE 754 floating point standard:
  single precision: 8 bit exponent, 23 bit significand
  double precision: 11 bit exponent, 52 bit significand

## Slide 91
IEEE 754 floating-point standard
Leading “1” bit of significand is implicit
Exponent is “biased” to make sorting easier
  all 0s is smallest exponent all 1s is largest
  bias of 127 for single precision and 1023 for double precision
  summary: (–1)sign × (1+significand) × 2exponent – bias
Example:
  decimal: -.75 = -3/4 = -3/22
  binary: -.11 = -1.1 x 2-1
  floating point: exponent = 126 = 01111110
  IEEE single precision: 10111111010000000000000000000000

## Slide 92
Floating Point Complexities
Operations are somewhat more complicated (see text)
In addition to overflow we can have “underflow”
Accuracy can be a big problem
  IEEE 754 keeps two extra bits, guard and round
  four rounding modes
  positive divided by zero yields “infinity”
  zero divide by zero yields “not a number”
  other complexities
Implementing the standard can be tricky
Not using the standard can be even worse
  see text for description of 80x86 and Pentium bug!

## Slide 93
Chapter Four Summary
Computer arithmetic is constrained by limited precision
Bit patterns have no inherent meaning but standards do exist
  two’s complement
  IEEE 754 floating point
Computer instructions determine “meaning” of the bit patterns
Performance and accuracy are important so there are many complexities in real machines (i.e., algorithms and implementation).
We are ready to move on (and implement the processor) you may want to look back (Section 4.12 is great reading!)