## Slide 1
Chapter Five

## Slide 2
We're ready to look at an implementation of the MIPS
Simplified to contain only:
  memory-reference instructions: lw, sw
  arithmetic-logical instructions: add, sub, and, or, slt
  control flow instructions: beq, j
Generic Implementation:
  use the program counter (PC) to supply instruction address
  get the instruction from memory
  read registers
  use the instruction to decide exactly what to do
All instructions use the ALU after reading the registers Why? memory-reference? arithmetic? control flow?
The Processor: Datapath & Control

## Slide 3
Abstract / Simplified View: Two types of functional units:
  elements that operate on data values (combinational)
  elements that contain state (sequential)
More Implementation Details

## Slide 4
Unclocked vs. Clocked
Clocks used in synchronous logic
  when should an element that contains state be updated?
cycle time
rising edge
falling edge
State Elements

## Slide 5
The set-reset latch
  output depends on present inputs and also on past inputs
An unclocked state element

## Slide 6
Output is equal to the stored value inside the element (don't need to ask for permission to look at the value)
Change of state (value) is based on the clock
Latches: whenever the inputs change, and the clock is asserted
Flip-flop: state changes only on a clock edge (edge-triggered methodology)
"logically true",
— could mean electrically low
A clocking methodology defines when signals can be read and written
— wouldn't want to read a signal at the same time it was being written
Latches and Flip-flops

## Slide 7
Two inputs:
  the data value to be stored (D)
  the clock signal (C) indicating when to read & store D
Two outputs:
  the value of the internal state (Q) and it's complement
D-latch

## Slide 8
D flip-flop
Output changes only on the clock edge

## Slide 9
Our Implementation
An edge triggered methodology
Typical execution:
  read contents of some state elements,
  send values through some combinational logic
  write results to one or more state elements

## Slide 10
Built using D flip-flops
Register File

## Slide 11
Register File
Note: we still use the real clock to determine when to write

## Slide 12
Simple Implementation
Include the functional units we need for each instruction
Why do we need this stuff?

## Slide 13
Building the Datapath
Use multiplexors to stitch them together

## Slide 14
Control
Selecting the operations to perform (ALU, read/write, etc.)
Controlling the flow of data (multiplexor inputs)
Information comes from the 32 bits of the instruction
Example: add $8, $17, $18 Instruction Format: 000000 10001 10010 01000 00000 100000 op rs rt rd shamt funct
ALU's operation based on instruction type and function code

## Slide 15
e.g., what should the ALU do with this instruction
Example: lw $1, 100($2) 35 2 1 100 op rs rt 16 bit offset
ALU control input 000 AND 001 OR 010 add 110 subtract 111 set-on-less-than
Why is the code for subtract 110 and not 011?
Control

## Slide 16
Must describe hardware to compute 3-bit ALU conrol input
  given instruction type 00 = lw, sw 01 = beq, 11 = arithmetic
  function code for arithmetic
Describe it using a truth table (can turn into gates):
ALUOp
computed from instruction type
Control

## Slide 17
Control

## Slide 18
Control
Simple combinational logic (truth tables)

## Slide 19
All of the logic is combinational
We wait for everything to settle down, and the right thing to be done
  ALU might not produce “right answer” right away
  we use write signals along with clock to determine when to write
Cycle time determined by length of the longest path
Our Simple Control Structure
We are ignoring some details like setup and hold times

## Slide 20
Single Cycle Implementation
Calculate cycle time assuming negligible delays except:
  memory (2ns), ALU and adders (2ns), register file access (1ns)

## Slide 21
Where we are headed
Single Cycle Problems:
  what if we had a more complicated instruction like floating point?
  wasteful of area
One Solution:
  use a “smaller” cycle time
  have different instructions take different numbers of cycles
  a “multicycle” datapath:

## Slide 22
We will be reusing functional units
  ALU used to compute address and to increment PC
  Memory used for instruction and data
Our control signals will not be determined soley by instruction
  e.g., what should the ALU do for a “subtract” instruction?
We’ll use a finite state machine for control
Multicycle Approach

## Slide 23
Finite state machines:
  a set of states and
  next state function (determined by current state and the input)
  output function (determined by current state and possibly input)
  We’ll use a Moore machine (output based only on current state)
Review: finite state machines

## Slide 24
Review: finite state machines
Example: B. 21 A friend would like you to build an “electronic eye” for use as a fake security device. The device consists of three lights lined up in a row, controlled by the outputs Left, Middle, and Right, which, if asserted, indicate that a light should be on. Only one light is on at a time, and the light “moves” from left to right and then from right to left, thus scaring away thieves who believe that the device is monitoring their activity. Draw the graphical representation for the finite state machine used to specify the electronic eye. Note that the rate of the eye’s movement will be controlled by the clock speed (which should not be too great) and that there are essentially no inputs.

## Slide 25
Break up the instructions into steps, each step takes a cycle
  balance the amount of work to be done
  restrict each cycle to use only one major functional unit
At the end of a cycle
  store values for use in later cycles (easiest thing to do)
  introduce additional “internal” registers
Multicycle Approach

## Slide 26
Instruction Fetch
Instruction Decode and Register Fetch
Execution, Memory Address Computation, or Branch Completion
Memory Access or R-type instruction completion
Write-back step INSTRUCTIONS TAKE FROM 3 - 5 CYCLES!
Five Execution Steps

## Slide 27
Use PC to get instruction and put it in the Instruction Register.
Increment the PC by 4 and put the result back in the PC.
Can be described succinctly using RTL "Register-Transfer Language" IR = Memory[PC]; PC = PC + 4; Can we figure out the values of the control signals? What is the advantage of updating the PC now?
Step 1: Instruction Fetch

## Slide 28
Read registers rs and rt in case we need them
Compute the branch address in case the instruction is a branch
RTL: A = Reg[IR[25-21]]; B = Reg[IR[20-16]]; ALUOut = PC + (sign-extend(IR[15-0]) << 2);
We aren't setting any control lines based on the instruction type (we are busy "decoding" it in our control logic)
Step 2: Instruction Decode and Register Fetch

## Slide 29
ALU is performing one of three functions, based on instruction type
Memory Reference: ALUOut = A + sign-extend(IR[15-0]);
R-type: ALUOut = A op B;
Branch: if (A==B) PC = ALUOut;
Step 3 (instruction dependent)

## Slide 30
Loads and stores access memory MDR = Memory[ALUOut]; or Memory[ALUOut] = B;
R-type instructions finish Reg[IR[15-11]] = ALUOut; The write actually takes place at the end of the cycle on the edge
Step 4 (R-type or memory-access)

## Slide 31
Reg[IR[20-16]]= MDR;
What about all the other instructions?
Write-back step

## Slide 32
Summary:

## Slide 33
How many cycles will it take to execute this code? lw $t2, 0($t3) lw $t3, 4($t3) beq $t2, $t3, Label #assume not add $t5, $t2, $t3 sw $t5, 8($t3) Label: ...
What is going on during the 8th cycle of execution?
In what cycle does the actual addition of $t2 and $t3 takes place?
Simple Questions

## Slide 34
Value of control signals is dependent upon:
  what instruction is being executed
  which step is being performed
Use the information we’ve acculumated to specify a finite state machine
  specify the finite state machine graphically, or
  use microprogramming
Implementation can be derived from specification
Implementing the Control

## Slide 35
How many state bits will we need?
Graphical Specification of FSM

## Slide 36
Implementation:
Finite State Machine for Control

## Slide 37
PLA Implementation
If I picked a horizontal or vertical line could you explain it?

## Slide 38
ROM = "Read Only Memory"
  values of memory locations are fixed ahead of time
A ROM can be used to implement a truth table
  if the address is m-bits, we can address 2m entries in the ROM.
  our outputs are the bits of data that the address points to. m is the "heigth", and n is the "width"
ROM Implementation
m
n
0 0 0 0 0 1 1
0 0 1 1 1 0 0
0 1 0 1 1 0 0
0 1 1 1 0 0 0
1 0 0 0 0 0 0
1 0 1 0 0 0 1
1 1 0 0 1 1 0
1 1 1 0 1 1 1

## Slide 39
How many inputs are there? 6 bits for opcode, 4 bits for state = 10 address lines (i.e., 210 = 1024 different addresses)
How many outputs are there? 16 datapath-control outputs, 4 state bits = 20 outputs
ROM is 210 x 20 = 20K bits (and a rather unusual size)
Rather wasteful, since for lots of the entries, the outputs are the same — i.e., opcode is often ignored
ROM Implementation

## Slide 40
Break up the table into two parts — 4 state bits tell you the 16 outputs, 24 x 16 bits of ROM — 10 bits tell you the 4 next state bits, 210 x 4 bits of ROM — Total: 4.3K bits of ROM
PLA is much smaller — can share product terms — only need entries that produce an active output — can take into account don't cares
Size is (#inputs ´ #product-terms) + (#outputs ´ #product-terms) For this example = (10x17)+(20x17) = 460 PLA cells
PLA cells usually about the size of a ROM cell (slightly bigger)
ROM vs PLA

## Slide 41
Complex instructions: the "next state" is often current state + 1
Another Implementation Style

## Slide 42
Details

## Slide 43
Microprogramming
What are the “microinstructions” ?

## Slide 44
A specification methodology
  appropriate if hundreds of opcodes, modes, cycles, etc.
  signals specified symbolically using microinstructions
Will two implementations of the same architecture have the same microcode?
What would a microassembler do?
Microprogramming

## Slide 45
Microinstruction format

## Slide 46
No encoding:
  1 bit for each datapath operation
  faster, requires more memory (logic)
  used for Vax 780 — an astonishing 400K of memory!
Lots of encoding:
  send the microinstructions through logic to get control signals
  uses less memory, slower
Historical context of CISC:
  Too much logic to put on a single chip with everything else
  Use a ROM (or even RAM) to hold the microcode
  It’s easy to add new instructions
Maximally vs. Minimally Encoded

## Slide 47
Microcode: Trade-offs
Distinction between specification and implementation is sometimes blurred
Specification Advantages:
  Easy to design and write
  Design architecture and microcode in parallel
Implementation (off-chip ROM) Advantages
  Easy to change since values are in memory
  Can emulate other architectures
  Can make use of internal registers
Implementation Disadvantages, SLOWER now that:
  Control is implemented on same chip as processor
  ROM is no longer faster than RAM
  No need to go back and make changes

## Slide 48
The Big Picture