## Slide 1: Firewalls
Definition:
A firewall is a system or group of systems that enforces an access control policy.
Consequently:
There should be a well defined access control policy.
The firewall system ( firewalls, their connectivity, and the set up are all governed by the access control policy).
Unlike other network devices, a firewall must control traffic while talking into account that not all the packets of data it sees may be what they appear to be.

## Slide 2: Firewalls
For example:
A bridge filters traffic based on the destination MAC address. If a host incorrectly labels destination MAC address and the bridge inadvertently passes the packet to the wrong destination, the bridge is not seen as being faulty. It is expected the host will follow certain rules. It is the host fault not the bridge.

## Slide 3: Firewalls continue
A firewall must assume that hosts may try to fool it in order to sneak information past it.
A firewall cannot use communication rules as a catch; rather, it should expect that the rules will not be followed.
This places a lot of pressure on the firewall design and set up, which must plan for every contingency.
Notes: s

## Slide 4: When a Firewall Required?
Typically, access is controlled between the internal Network and the Internet,
Internet
Internal network
but there are many other situations in which a firewall
may be required:
Firewall
Notes: s

## Slide 5: When a Firewall Required?
  Dial In Modem Pool:
  AN organization may have an access control policy that specifies that dial-in users may only access a single mail system. A firewall is needed to preclude dial in users to access servers in the organization other than the mail server.
Mail server
? server
Web server
Mail server
? server
Web server
firewall
Notes: s

## Slide 6: When a Firewall Required?
External Connection to Business:
  Many organization have a permanent connections to remote business partners through Internet. Now someone has an access to the internal network from an area where security is not controlled by the organization. A firewall is needed in this case.
Internet
Your
organization
Business
partner
Firewall
Notes: s

## Slide 7: When a Firewall Required? Continue
  Between Departments:
  Some organizations ( such as trading companies) are required to maintain so called “ Chinese firewalls” between different areas of the network. This is to insure that internal users only have access to the information they require. A firewall at the point of connection between these two networks enforces access control.
Department
Department
Department
Department
Notes: s

## Slide 8: Firewall Types
Not all firewalls are built the same. The most popular ones are
  Static Packet Filtering
  Dynamic Packet Filtering
  Proxy
Notes: s

## Slide 9: Static Packet Filtering
  Operation:
  Static Packet filtering controls traffic by using information stored within the packet headers. As packet received by the filtering device, the attributes of the data (information) stored within the packet headers compared against the access control policy ( referred to as Access Control List (ACL)). Based on the comparison results the traffic is either allowed or blocked.
Reject
Accept
Header
Compare
ACL rules
The message
Notes: s

## Slide 10: Static Packet Filtering: continue
  The information used to regulate the traffic flow in the packet header include:
Destination IP address or subnet.
Source IP address or subnet.
Destination service port.
Source service port.
Flag (TCP only).
Notes: s

## Slide 11: Static Packet Filtering: continue
The TCP Flag Fields
Figure 51 A TCP/IP packet decode:
Notes: s

## Slide 12: Static Packet Filtering: continue
The TCP Flag Fields
ACK | Indicated that this is a response to a data request and that there is useful information within the Acknowledged Number Filed
FIN | Indicates that the transmitting system wishes to terminate the current session
PSH | Used to transmit data if it is less than the packet size.
RST | Reset is used when a non recoverable transmission failure occurs. It is transmitting system ways of stating , “ Were you listening to me? Do I have to say it again?This is typically caused by a non-responsive host.
SYN | Used while initializing a communication session.
URG | Indicates that the transmitting system has some high-priority information to pass along and that there is useful information writing the Urgent pointer field, which indicates where the important data starts with in the payload. The system has to process this data before any thing else. This is referred to as processing the data out-of-band
Notes: s

## Slide 13: Static Packet Filtering: continue
Let us explain the functionality of SPF through this case:
Access Policy States: “ Our internal users can access any service out on the Internet, but all internet traffic headed to our network should be blocked”
While the above case it seems sound an acceptable policy but it would not work!!
This would be obvious if we recall that all communications represents a two-step process:
When you access a web site, you make a data request
The Web site replies by returning the data that has been requested
Notes: s

## Slide 14: Static Packet Filtering: continue
If the second statement of your policy is verbatim, our replies will never make it back to the requesting host. “ We are back to the “ wire cutters as an effective security device” model:our firewall will not allow a complete communication sessions.
This is where flag fields comes into play. Here use SYN=1 and all flags =0. So the ACP will be “ all internet packets headed to our network with SYN=1 and all other flags =0 should be blocked.
Locking down your network perimeter is not the most secure method. By playing with the flag values, a would be attacker can fool a SPF into allowing malicious traffic through.
Notes: s

## Slide 15: Static Packet Filtering: continue
FIN Scanner:
Let the transmitted packet have FIN=1, ACK =1 and all other flags =0. ( This packet is happily passed along).
The result is that an attacker can analyze the retuning data stream to determine which host are offering what services.
  If he destination host returns an ACK=1, RST=1( a generic system response to a nonexistence services), the attacker knows that this is an unused port.
  If he destination host returns an ACK=1, FIN=1 ( the service's agreeing to close the connect). The FIN scanner knows that there is a service monitoring that port.
This means that out packet filter is unable to deter these scanning probes.
Notes: s

## Slide 16: Static Packet Filtering: continue
Filtering UDP Traffic:
It does not use flags to indicate session’s state.
This means there is no way to determine if a packet is a data request or reply to a previous request.
The only information that can be used is the source and destination port numbers. Even this information is of little use because some services use the same source and destination port number .
when two DNS are exchanging information on same port number say 53. You cannot block inbound traffic to port 53, because that would block data replies as well as data requests.
For example
Notes: s

## Slide 17: Static Packet Filtering: continue
Filtering UDP Traffic:
Figure 52
Notes: s

## Slide 18: Static Packet Filtering: continue
Filtering UDP Traffic:
This is why in many cases the only effective means
of controlling UDP traffic with a SPF is :
Either to block all UDP ports or
Let it through and hope for the best
Notes: s

## Slide 19: Static Packet Filtering: continue
Packet Filtering ICMP:
The Internet Control Message Protocol (ICMP) provides background support for the IP protocol.
It is not used to transmit data, but is used for maintenance and control duty to insure that all running smoothly.
It does not use service ports. There is a Type field to identify the ICMP packet type as well as Code field to provide even more granular information about the current session as will be explained shortly
For Example:
Ping uses ICMP to insure that there is connectivity between two hosts.
A transparency Fig. 53 shows a packet decode of an ICMP header
Notes: s

## Slide 20: Static Packet Filtering: continue
Packet Filtering ICMP:
Figure 53
Notes: s

## Slide 21: Static Packet Filtering: continue
Packet Filtering ICMP:
Present the case study to demonstrate how increasing security measures may produce communication problems in SPF. This mandates that system manager should have an excellent understanding of the system. Otherwise we will face problems and loose business may more that it would have been with less security
Notes: s

## Slide 22: Dynamic Packet Filtering (DPF): continue
Desktop System
Desktop System
Server
Router
Web Server
Static Packet Filter
Internet
Token
Ring
Desktop Systems
Notes: s

## Slide 23: Static Packet Filtering Summary:
Static packet filters are non-intelligent filtering devices. They offer little protection against advanced types of attack.
They look at a minimal amount of information in order to determine which traffic should be allowed to pass and which traffic should be dropped.
Many routers have the ability to perform SPF
Notes: s

## Slide 24: Dynamic Packet Filtering (DPF)
DPF in points
DPF takes SPF one step further by maintaining a connection table in order to monitor the state of a communication session. It does not simply rely on the flag settings.
The example next explains the power of DPF.
Notes: s

## Slide 25: Dynamic Packet Filtering (DPF)
Example:
  Assume that an attacker sends a system a packet of data with a payload designed to crash your system.
  The attacker may perform some packet trickery in order to make this packet look like a reply to information requested by the internal system.
  Unlike A SPF, A DPF would not be so easily fooled. When the information was received, the dynamic packet filter would reference its connection table ( sometimes referred to as a state table).
  When reviewing the table entries, the dynamic packet filter realizes that the internal system never actually connected to this external system to place a data request.
Notes: s

## Slide 26: Dynamic Packet Filtering (DPF): continue
The dynamic packet filter may even verify the sequence and acknowledgment numbers all match. ( that is why the attackers effort now is on how to steal the information of the packet fields which include source, destination, sequence no. and acknowledgment no. ..etc. Ways of doing that is beyond a scope of any introductory course)
The state table entry of a session will be removed
  Once the FIN packets are sent by each system.
  If no reply is received for a period of time ( anywhere from one minute to one hour, depending on the configuration)
Maintain the state table and perform checking for every entry is time consuming ( Delay).
Notes: s

## Slide 27: Dynamic Packet Filtering (DPF): continue
Spoofing DPF
Referring to the Figure in the next slide
In order for the attacker to launch a successful attack, a number of conditions would have to be met:
Woolly attacker would have to spoof or assume the IP address of the remote server.
If the address has been spoofed, Woolly Attacker might have to take further measures to insure that the remote server will not respond to requests.
If the address has been spoofed, Woolly Attacker would need some method of reading replies off the wire.
Woolly Attacker would need to know the source and destination service ports being used so that his traffic will match the entries in the state table.
Notes: s

## Slide 28: Dynamic Packet Filtering (DPF): continue
Spoofing DPF
Wooly Attacker
Protected Host
Remote Server
Static Packet Filter
SYN = 1
Wooly Attacker
Protected Host
Remote Server
Dynamic Packet Filter
SYN = 1
Notes: s

## Slide 29: Dynamic Packet Filtering (DPF): continue
Port Scan
Wooly Attacker
Protected Host
Remote Server
Static Packet Filter
Wooly Attacker
Protected Host
Remote Server
Dynamic Packet Filter
ACK =1 FIN= 1
ACK=1 FIN=1
STATE TABLE
Sorry the protected host has
not opened a session with you.
It has Only opened a session
with Remote Server
Source port = 1037
Destination port = 23
Notes: s

## Slide 30: Dynamic Packet Filtering (DPF): continue
Spoofing DPF
Depending on the implementation, the acknowledgment and sequence numbers might have to match, as well
Wooly Attacker would have to manipulate the communication session fast enough to avoid timeouts, both on the firewall and on the protected host.
So while it is possible to launch this type of attack, it is not very easy to succeed. Clearly, Woolly Attacker would have to be very knowledgeable and feel that he has much to gain by going to all this effort.
Notes: s

## Slide 31: Dynamic Packet Filtering (DPF): continue
UDP Traffic and DPF
It is extremely advised that DPF be used instead of static filtering when UDP traffic must be allowed through.
The reason behind this is that although UDP header has zero information regarding connection state, dynamic packet filter is capable of remembering the state information. It does not rely on the information on the header.
Notes: s

## Slide 32: Dynamic Packet Filtering (DPF): continue
Is My Transport Supported?
The Implementation of DPF is transport specific. That is, it has to be specifically implemented for each protocol transport, such as TCP, UDP, and ICMP. When choosing a dynamic packet filter, make sure that the firewall is capable of maintain state for all transport that you wish to use.
Notes: s

## Slide 33: Dynamic Packet Filtering (DPF): continue
Summary
Dynamic Packet filters are intelligent devices that make traffic-control decisions based on packet attributes and state tables.
State tables enable the fire walling device to remember previous communication packet exchanges and make judgments based on this additional information.
Notes: s

## Slide 34: Dynamic Packet Filtering (DPF): continue
DPF Limitations:
It cannot make filtering decisions based upon payload, which is the actual data contained within the packet.In order to filter the pay load, one must use a Proxy-Based Firewall
Notes: s

## Slide 35: Proxy-Based Firewalls
What is a proxy?
The proxy plays middleman in all connection attempts. (For analogy, think of two people speaking through a language interpreter. The two people never talk to each other directly and all communication passes through the interpreter.)
Unlike its packet-filtering counterparts, a proxy does not route any traffic. In fact, a properly configured proxy will have all routing functionality disabled.
Notes: s

## Slide 36: Proxy-Based Firewalls: continue
How it works
Reference Figure next
Our internal host wishes to request a Web page from the remote server.
It formulates the request and transmits the information to the gateway leading to the remote network, which in his case the proxy server.
Once the proxy receives the request, it identifies what type of service the internal host is trying to access.
Notes: s

## Slide 37: Proxy-Based Firewalls: continue
Remote Server
Internal Host
Proxy
Data Request
Data Request
HTTP Application
1
5
4
3
2
Notes: s

## Slide 38: Proxy-Based Firewalls: continue
How it works continue
Since in this case the host has requested a Web page, the proxy passes the request to a special application used only for processing HTTP sessions. ( This application is simply a program running in memory that has the sole function of dealing with HTTP Communications)
When the HTTP application receives the request, it verifies that the ACL allows this type of traffic, if the traffic is acceptable, the proxy formulates a new request to the remote server. ( this is a good security measure; if the request were checked with a network analyzer, it would look like proxy had made the HTTP request, the internal host is invisible)
Notes: s

## Slide 39: Proxy-Based Firewalls: continue
Once the Proxy server receives the reply, it again passes it to the HTTP application.
The HTTP application then scrutinizes the actual data sent by the remote server for abnormalities.
If the data is acceptable, the HTTP application creates a new packet and forwards the information to the internal hosts.
How it works: continue
Notes: s

## Slide 40: Proxy-Based Firewalls: continue
Security in Proxy
As you can see, the two systems never actually exchange information directly. The proxy constantly butts into the conversation to make sure that all goes securely.
Protocol- Specific Security:
Since proxies must “ Understand’ the applications protocol being utilized, they can also implement protocol-specific Security.
Example: Create a Read-Only FTP.
Notes: s

## Slide 41: Proxy-Based Firewalls: continue
Example: Create a Read-Only FTP.
An inbound FTP proxy can be configured to filter out all put and mput requests received by an external system. So people outside the firewall would be unable to write to the server. However, the users can get outside information by the command get.
Internal Host
Proxy
Get
FTP Application
Put and Mput
Server
Notes: s

## Slide 42: Proxy-Based Firewalls: continue
Filtering Java, and ActiveX
When it comes to content (payload) filtering, the first thing most people think about is Java applets and Active X.
With Active X, one can create a self sufficient program known as an Active X control. The benefit with active X control is that it can be shared across multiple applications. ( Note that Active X is not a programming language. Active X controls are created using some other programming languages such as C++ and even Microsoft Java) .
Notes: s

## Slide 43: Proxy-Based Firewalls: continue
Filtering Java, and ActiveX
Java applets and Active X controls can be pulled down from a server and run on any compatible Web browser ( Portable).
Functionally, those programs can include anything from dancing icons to shared applications. There are few limits to the types of programs that can be created.
This is exactly where our problems begin.
While both Java and Active X were developed with security in mind, quit a few exploits have been discovered in both. See www.digicrime.com ( Note Java is more secure than Active X)
Notes: s

## Slide 44: What Type of Firewall Shall I Use?
DPF verses Proxy
Proxy works better in the face of dubious traffic. DPF typically ( not always) will pass questionable traffic.
Proxy checks the content of a packet and so it is more secure.
DPF is typically easier to work with and has a better ability to meet most business needs. For example many proxies have trouble supporting modern services such as Microsoft’s NetMeeting or real Audio and Video.
Notes: s

## Slide 45: Should I Run My Firewall on UNIX or NT?
Note:
The discussion here will not tell you which platform to choose: It will simply expose the strength and weaknesses of each platform and leave the final decision up to you
As we will see the discussion will be centralized on UNIX longevity and stability and NT Familiarity.
UNIX Versus NT:
Unix has been around far longer that NT and it is open system which means its platform is well understood and people have an intimate knowledge of its inner working. This make the operating system far easier to secure.
Notes: s

## Slide 46: Should I Run My Firewall on UNIX or NT? continue
Windows on the other hand, has been around only for less time and it is closed OS. While it was originally thought that this closed attitude would help to keep the product more secure . (that is, security through obscurity), the number of NT exploits that have been discovered over the past few years has shown this approach does not work
Along the same thread, the UNIX camp will argue that the firewalls have been developed for UNIX far long than for NT. This stability and longevity is extremely important because a firewall is, after all, a security product.
UNIX OS is far easier to secure. It is a simple matter to remove all non-firewall related programs from a UNIX system, thus locking it down as tightly as possible.
UNIX Versus NT continue :
Notes: s

## Slide 47: Should I Run My Firewall on UNIX or NT? continue
Windows have been far the most popular ever produced and a far more familiar environment to the typical user. This means it would be not wise ( stupid) to learn completely new environment just to run firewall software.
Even more important a company is not required to hire additional recourses to manage its firewall.
The Familiarity will augment security. Since people are familiar with NT, they are less likely to configure the platform incorrectly and cause a security problem.
NT Versus UNIX :
Notes: s

## Slide 48: Should I Run My Firewall on UNIX or NT? continue
NT Versus UNIX continue :
Consistency. Since the organization runs NT for file, print, and application services, it makes more sense to use one platform for all required services. This makes administration easier and more harmonic and consequently more secure.
Notes: s

## Slide 49: Security Through Address Translation on Firewalls
When an IP address is converted from one value to another, it is called address translation.
This feature ( supported by many firewall products) is used when you do not wish to let remote systems know the true IP address of your system.
Example is shown next.
Address Translation
Notes: s

## Slide 50: Security Through Address Translation on Firewalls
Desktop System
Address Translation
Internet
Source IP 192.168.1.50
Destination IP 206.121.73.5
Source Port 1037
Destination Port 80
Source IP 199.53.72.2.2
Destination IP 206.121.73.5
Source Port 1058
Destination Port 80
Router
Firewall
51
1058
..
..
192.168.1.50
..
..
Notes: s

## Slide 51: Security Through Address Translation on Firewalls
Address Translation
Private addressing is IP subnet ranges that are not allowed to be used (routed) on the internet. So they can be safely used internally without fear of conflict. Those ranges are:
10.0.0.0 10.255.255.255.
172.16.0.0 172.32.255.255
192.168.0.0 192.168.255.255
All external systems (servers) can reply (not access) to the internal systems through the Firewall.
Notes: s

## Slide 52: Security Through Address Translation on Firewalls
Address Translation: continue
Problem:
How does the firewall distinguish between replies which goes to who?
Solution: Through the port numbers
As you may notice in previous figure, the port number is changed along with the IP address. The port number identifies which replies go to which system.
A table should be kept in the firewall where it registers the each outgoing port with an internal IP.
Notes: s

## Slide 53: Security Through Address Translation on Firewalls
There are three ways of deploying address translation:
  Hiding Network Address Translation (Hiding NAT)
  Static Network Address Translation (Static NAT)
  Port Address Translation (PAT)
Address Translation: continue
Notes: s

## Slide 54: Security Through Address Translation on Firewalls
Address Translation: continue
Hiding NAT:
All internal hosts are hidden behind a single IP address.
It can support thousands of concurrent sessions. If it becomes a bottle neck, multiple hiding addresses can be used.
All inbound traffic is dropped because there is no way to identify where it goes. Although this can be viewed as a limitation, it can be considered a feature as it augments security policy.
Notes: s

## Slide 55: Security Through Address Translation on Firewalls
Address Translation: continue
Static NAT:
Static NAT functions similarly to hiding NAT, except that only a single private IP address is mapped to each public IP address used.
It augments security as it hides your real IP ???
It is also useful for services that will break if hiding NAT is used.
Notes: s

## Slide 56: Security Through Address Translation on Firewalls
For example:
Some communications between DNS servers require that the source and destination port both be set to port 53. If one uses Hiding NAT, the firewall would be required to change the source port to some random port number, thus breaking the Communication session.
By using Static NAT, the port number does not need to be changed and the communication session can be carried out normally.
Notes: s

## Slide 57: Security Through Address Translation on Firewalls
Address Translation: continue
PAT:
Notes: s

## Slide 58: Security Through Address Translation on Firewalls
Exercise
Firewall Deployment.
Notes: s